## Slide 1: JVET-M0282 CE2.2.8: Affine Motion Vector Pruning
January 2019
A. Robert - Technicolor

## Slide 2: Motivation
  VTM-3:
    In Affine AMVP and Affine Merge coding modes, motion predictor lists are constructed.
    But in the current reference software, almost all pruning has been removed and some predictor redundancy can be observed
  Goal of this contribution:
    Reduce predictor redundancies
    Harmonize motion predictor lists construction

## Slide 3: Affine AMVP coding mode
  Adopted last meeting:
    Remove all pruning
    Get only 2 spatial inherited like in AMVP
  Proposed uniformization with AMVP
    2 spatial inherited predictor are pruned together
    Virtual predictor is pruned
    Simple and early pruning of the virtual translational predictors
      If vLT and vRT exist and are equal, then vRT is set invalid
      If vLT and vLB exist and are equal or vRT and vLB exist and are equal, then vLB is set invalid
  → 18 integer comparisons per ref frame (16 AMVP)
List | Affine AMVP
Candidates type | -> Spatial inherited Affine A0/A1 + unscaled + rounding ¼-pel -> Spatial inherited Affine B0/B1/B2 + unscaled + rounding ¼-pel - Pruned spatial inherited cand - Spatial LT B2/B3/A2 + unscaled + rounding ¼-pel - Spatial RT B1/B0 + unscaled + rounding ¼-pel - Spatial LB A1/A0 + unscaled + rounding ¼-pel -> Virtual Affine with {LT,RT,LB}/{LT,RT} + pruned all -> Translational with pruned LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero Affine
list size/total nb of possible candidates | 2 / 2+1+3+1+2 = 9 for each ref pic
Nb comparison mv refidx total int | 3+3+3+0+0 = 0+9 = 9 for each ref pic (x4) 0 18

## Slide 4: Affine Merge coding mode
  Adopted last meeting:
    Reduced pruning to only virtual predictors (same reference frame but different MVs)
  Proposed uniformization with Affine AMVP
    2 spatial inherited predictor are pruned together
    Consider zero Affine predictor in the RDO
  → 14 integer comparisons more (+15%)
List | Affine merge
Candidates type | - Spatial A1 - Spatial B1 + pruned A1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 -> ATMVP -> Spatial inherited Affine A0/A1 -> Spatial inherited Affine B0/B1/B2 - Pruned spatial inherited cand - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual Affine with pruned {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero Affine
list size/total nb of possible candidates | 5 / 1+2+6+5 = 14
Nb comparison mv refidx total int | 3*2+3*2+(4*2+2)*2+0 = 26+6 = 32 3*2+1*2+(4*2+2)*2+0 = 26+2 = 28 78 92

## Slide 5: Simulation Results
  Results over VTM-3.0:
    Affine AMVP uniformization

## Slide 6: Simulation Results
  Results over VTM-3.0:
    Affine Merge uniformization

## Slide 7: Simulation Results
  Results over VTM-3.0:
    Proposed Affine AMVP + Affine Merge

## Slide 8: Simulation Results
  Results over VTM-3.0:
    Proposed Affine uniformization + CE4.1.5 (JVET-M0281)