## Slide 1
JVET-M0329
Modified Enabling Condition for Triangle Prediction Unit Mode
Fangdong Chen and Li Wang
Hikvision
Notes: Hello everyone. I’m fangdong chen from Hikvision. Today, what I will repot is ….

## Slide 2
Modified Enabling Condition
The enabling condition for triangle prediction in VTM 3.0
  Current frame is B frame
  The area of current block is larger or equal than 64
Our proposed condition
  Current frame is inter frame (including P frame)
  The size condition is modified from two folds: the minimum size and the maximum size.
Fast mode decision
  bestIsSkip is always set as false (Always conduct fast rough RDO ranking)
  The number of candidate numTriangleCandidate is reduced from 40 to 14
Notes: Decoder side MV derivation is another possible approach, and Bilateral matching and Template Matching are two main methods. However, the Bilateral matching requires two lists, thus it is invalid for P frame. As far as I know, P frames are quite common in many low delay applications. TM can be used in both B and P frames. But, its usage of neighboring samples brings high decoding delay.

## Slide 3
Five tests:
  Test A: Enable the triangular prediction unit mode for P frames with mode decision in VTM3.0.
  Test B: Enable the triangular prediction unit mode for P frames with the proposed fast mode decision method.
  Test C: Apply the proposed fast mode decision method to B frames.
  Test D: The triangular prediction unit mode is only applied to a CU which both block width and height are larger than or equal to 8. (Aligned with merge sub-block mode)
  Test E: The triangular prediction unit mode is applied to a CU which size is larger or equal than 64, and both block width and height are less than 128. (Aligned with CIIP)
Modified Enabling Condition
Notes: Decoder side MV derivation is another possible approach, and Bilateral matching and Template Matching are two main methods. However, the Bilateral matching requires two lists, thus it is invalid for P frame. As far as I know, P frames are quite common in many low delay applications. TM can be used in both B and P frames. But, its usage of neighboring samples brings high decoding delay.

## Slide 4
Experimental Results
Results of test A
Results of test B （with proposed fast mode decision）
Thank Peking University for the cross-checking!
Notes: These are the results for LDB and RA, it also achieves some coding gains for these two configurations.

## Slide 5
Experimental Results
Results of test C
Notes: These are the results for LDB and RA, it also achieves some coding gains for these two configurations.

## Slide 6
Experimental Results
Results of test D
Notes: These are the results for LDB and RA, it also achieves some coding gains for these two configurations.

## Slide 7
Experimental Results
Results of test E
Notes: These are the results for LDB and RA, it also achieves some coding gains for these two configurations.

## Slide 8
Conclusion
Propose to modify the enabling condition for triangle prediction
  Current frame is inter frame (including P frame)
  The size condition is modified from two folds: the minimum size and the maximum size.
  The first modification brings significant coding gains, and the other one tries to align the triangle prediction mode with other modes.
Based on the above results, it is suggested to study it in CE.
Notes:   As a conclusion, we propose a Low Latency Template based Motion Vector Refinement method. And it has Low latency because of the reuse of neighboring motion
  and it has low decoder complexity because of the small size of template. And significant coding gains are achieved especially for LDP configuration. Based on the above results, it is suggested to study it in the related CE.

## Slide 9
Thank you！