## Slide 1
CE10-related: Simplification of Triangular Partitions
JVET-M0352
The 13th JVET Meeting
Jan. 2019
Dohyeon Park, Yong-Uk Yoon, Jae-Gon Kim (KAU)
Jinho Lee, Jungwon Kang (ETRI)

## Slide 2: Summary
Proposed simplifications to reduce complexity of triangle PU mode
  Test 1: Simplfication of motion vector storage skipping reference picture mapping process
  Test 2: Reduction of the number of motion information combinations
 |  | Over VTM-3.0 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Test 1 | RA | 0.00% | 0.02% | 0.01% | 100% | 100%
 | LB | 0.17% | 0.28% | 0.10% | 100% | 100%
Test 2 | RA | 0.01% | 0.05% | 0.09% | 96% | 100%
 | LB | 0.03% | 0.01% | 0.13% | 94% | 100%

## Slide 3: Background
Triangle prediction mode divides a CU into two triangle prediction units for inter prediction, which makes more flexible inter prediction
In motion vector storage, a bi-prediction MV is stored at the grids located at diagonal areas between triangle PUs
  Reference picture mapping process is performed when the motion vector of each PU has the same reference picture list
The syntax element of a merge_triangle_idx is used to indicate the combinations of the split direction and the motion vectors of two partitions
  The index represents 40 combinations as follows:
    { 0, 1, 0 }, { 1, 0, 1 }, { 1, 0, 2 }, { 0, 0, 1 }, { 0, 2, 0 }, ……

## Slide 4: Proposed Simplifications
Proposed simplification 1 – Test 1
  When a bi-directional motion vector is derived, the reference picture mapping process is removed
    If two motion vectors of triangle PUs are from the same list, using the motion vector of the first PU only

## Slide 5: Proposed Simplifications
Proposed simplification 2 – Test 2
  Reduction of the number of motion vector combinations for both partitions
    Restriction to 16 combinations from 40 combinations to be checked
      Size of the LUT is reduced (403 → 163)
    In addition, binarization of the index is modified with fixed length coding and truncated binary coding
IDX | Bins |  |  |  | 
0 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 |  | 
2 | 0 | 1 | 0 |  | 
3 | 0 | 1 | 1 |  | 
4 | 1 | 0 | 0 | 0 | 
5 | 1 | 0 | 0 | 1 | 
6 | 1 | 0 | 1 | 0 | 
7 | 1 | 0 | 1 | 1 | 
8 | 1 | 1 | 0 | 0 | 0
9 | 1 | 1 | 0 | 0 | 1
10 | 1 | 1 | 0 | 1 | 0
11 | 1 | 1 | 0 | 1 | 1
12 | 1 | 1 | 1 | 0 | 0
13 | 1 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1 | 1
      The first bin is regular coded, the remains are bypass coded

## Slide 6: Experimental Results
Test 1: Removing the reference picture mapping process
Test 2: Reduction of the number of motion information combinations
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | 0.07% | 100% | 100%
Class A2 | 0.00% | 0.21% | 0.11% | 100% | 100%
Class B | 0.00% | 0.01% | -0.02% | 100% | 100%
Class C | 0.02% | -0.12% | -0.06% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.02% | 0.01% | 100% | 100%
Class D | -0.05% | -0.03% | 0.03% | 100% | 100%
Class F | -0.01% | 0.00% | 0.01% | 100% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.11% | -0.05% | 0.03% | 100% | 100%
0.18% | 0.37% | 0.34% | 100% | 100%
0.26% | 0.71% | -0.09% | 100% | 99%
0.17% | 0.28% | 0.10% | 100% | 100%
0.06% | -0.22% | 0.27% | 100% | 100%
0.08% | 0.13% | 0.19% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.04% | 0.08% | 96% | 100%
Class A2 | 0.01% | 0.08% | 0.10% | 95% | 100%
Class B | 0.01% | 0.02% | 0.01% | 96% | 100%
Class C | 0.03% | 0.14% | 0.17% | 95% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.05% | 0.09% | 96% | 100%
Class D | 0.03% | 0.02% | -0.04% | 95% | 101%
Class F | 0.04% | 0.02% | 0.01% | 94% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.25% | -0.17% | 95% | 100%
0.07% | 0.25% | 0.19% | 95% | 101%
0.00% | 0.12% | -0.48% | 92% | 100%
0.03% | 0.01% | -0.13% | 94% | 100%
0.04% | 0.18% | 0.46% | 94% | 101%
0.09% | 0.31% | 0.21% | 93% | 100%

## Slide 7: Experimental Results
Test 3: Test 1 + Test 2
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.09% | 0.02% | 96% | 100%
Class A2 | 0.00% | 0.06% | 0.16% | 96% | 100%
Class B | 0.03% | 0.05% | 0.07% | 96% | 100%
Class C | 0.05% | 0.14% | 0.13% | 95% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.05% | 0.10% | 96% | 100%
Class D | 0.03% | 0.04% | -0.10% | 95% | 100%
Class F | 0.02% | 0.04% | 0.01% | 94% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.14% | -0.04% | 0.20% | 95% | 100%
0.25% | 0.45% | 0.51% | 95% | 100%
0.26% | 0.80% | 0.26% | 93% | 100%
0.20% | 0.33% | 0.32% | 94% | 100%
0.19% | 0.41% | 0.84% | 94% | 100%
0.19% | 0.43% | 0.20% | 93% | 99%

## Slide 8: Conclusions
Proposed two simplifications
  Skipping the reference picture mapping process (Test 1)
  Reducing the number of motion information combinations (Test 2)
Test 1
  No loss in RA – redundant process
  0.17% loss in LB
  It needs further investigation to reduce the loss in LB
Test 2
  Number of cost checks for triangle partitions can be reduced with minor loss
    (RA) 0.01% BD-rate with 96%/100% encoding/decoding time
    (LDB) 0.03% BD-rate with 94%/100% encoding/decoding time
  Suggest to study this method in the CE of multiple shape prediction partitions