## Slide 1: JVET-M0384: Non-CE3: LM in the middle
JVET 13th Meeting - Marrakech, MO, 9–18 Jan. 2019

## Slide 2: Problems with methods studied in CE3
Computing of average prior to classifying samples
  This dependency is not ideal for various implementations, as it requires an additional stage
  Complexity increase in any case for the smallest block
Potential discontinuity in MMLM prediction
Ymean

## Slide 3: Proposed improvements
Restriction of use of the average/MMLM to greater block sizes
  Strictly more than 16 samples in the test
For MMLM: use of a knee point T based on average
  Simple formula (e.g. linear combination): T = f(avg, min, max)
  Replaces one of the points used for computing both α and β parameters
Computations compared to CCLM modes
  Luma and chroma averages
  No additional comparison
  1 scaling (same as MMLM)
Ymean
T

## Slide 4: Results
Competitive coding efficiency while solving said mentioned issues
Table below uses a 18:1:1 weighting
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.7% | -1.4% | -2.8% | 99% | 91%
Class A2 | -0.1% | -0.5% | -0.4% | 99% | 92%
Class B | -0.2% | -1.5% | -1.7% | 101% | 92%
Class C | -0.3% | -1.2% | -1.5% | 101% | 105%
Class E | -0.1% | -0.3% | -0.4% | 102% | 99%
Overall | -0.3% | -1.1% | -1.4% | 100% | 96%
Class D | -0.1% | -0.7% | -0.4% | 103% | 98%
Class F | -0.3% | -0.7% | -0.9% | 103% | 102%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.5% | -1.2% | -2.1% | 100% | 93%
Class A2 | -0.1% | -0.4% | -0.2% | 100% | 92%
Class B | -0.1% | -1.2% | -1.5% | 99% | 107%
Class C | -0.1% | -0.6% | -0.2% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.2% | -0.9% | -1.0% | 100% | 99%
Class D | 0.0% | -0.9% | -0.1% | 103% | 87%
Class F | -0.1% | -0.3% | -0.7% | 99% | 104%
 | AI | RA
M0384 | -0.375% | -0.237%
CE3.2.1: MMLM + 3 VTM LM modes | -0.418% | -0.258%
CE3.2.2: CE3.2.1 + 2 MMLM modes | -0.485% | -0.321%
CE3.2.5.2 | -0.252% | -0.175%

## Slide 5: Conclusion
Tests in CE are all noticeably increasing complexity of worst case
But multiple model do provide interesting gains, in particular in AI
Proposed 2 solutions
Suggestion that these solutions are added to any adopted scheme using multiple models, classification or average computation

## Slide 6: Thank you for your attention.

## Slide 7: Annex
M0384 LM modes:
  ≤16 samples: CCLM + above MDLM + left MDLM
  >16: same as above but in MMLM mode
Example of effective f(avg, min, max)
  avg += (2*avg – min – max)>>3
M0384:
  Is disadvantaged by not applying to smaller blocks (where most of the CCLM gains are obtained)
  Is disadvantaged by not being an additional mode
  Offer better RA performance because of the prediction continuity