## Slide 1: JVET-M0387 AHG14: Updates on Intra Refresh Proposal
Jean-Marc Thiesse
Didier Nicholson
David Gommelet

## Slide 2: Background
Intra Refresh is a classical technology addressing:
  Low-latency by removing of sizeable I picture while keeping random accessibility of stream
  And/or error resilience.
Usually implemented by encoder-only modifications leading to significant efficiency losses.
AhG 14 was established at Ljubljana to study
JVET-M0387

## Slide 3: Summary
This contribution provides updated results of JVET-L0160 and JVET-L0161 to address AhG14 following mandates:
  Proposition of test conditions for studying Intra Refresh.
  Proposition of an encoder-only Intra Refresh.
  Characterization of the solution.
  Study of a normative solution.
Loss of 21.3% for enc-only solution vs fair reference.
Normative solution improvement of 5% with slightly intrusive modifications.
JVET-M0387

## Slide 4: Encoder-only Intra Refresh proposal
The software modifications to support Intra Refresh tool at the encoder-level in VTM software include:
  Intra prediction mode forced on column basis at CU level.
  Constrained Intra Prediction enabled.
  Motion vectors constrained (6 pixels due to filters).
  Removing of former reference pictures at re-looping.
  Disabling of ALF of CTU including Intra refresh pixels.
JVET-M0387

## Slide 5: Software modifications
Shared on AHG14 Gitlab.
15 changed files, 330 lines modifications.
The additional parameters added to the configuration file are as follows:
  IntraRefreshType : 1 # Intra Refresh type flag 0: disable, 1: enc-only, 2: normative
  IntraRefreshStart : 0 # Position of the first column of Intra refresh (in pixels)
  IntraRefreshDirection : 0 # Direction of Intra Refresh 0: left to right, 1: right to left
  IntraRefreshPeriod : 32 # Period of the Intra Refresh
JVET-M0387

## Slide 6: Test condition for Intra Refresh
Intra Refresh anchor proposal:
  Basis= Low-Delay B Main10 configuration.
  Without pyramidal B structure (GOPSize = 1)
  QP offset of 1 between I and P picture (same QP for IR).
  Intra Refresh period of 32 (as Random Access).
Reference for losses characterization:
  Same with an Intra period of 32 (DecodingRefreshType = 1).
JVET-M0387

## Slide 7: Results: Enc-only Intra Refresh
Significant losses, especially for low motion sequences.
JVET-M0387
 | Low delay B Intra Refresh Encoder Only Main 10 |  |  |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 12,53% | 23,35% | 35,68% | 93% | #DIV/0!
Class C | 18,75% | 24,36% | 26,79% | 94% | #DIV/0!
Class E | 39,27% | 43,52% | 51,34% | 91% | #DIV/0!
Overall | 21,29% | 28,73% | 36,63% | 93% | #DIV/0!
Class D | 22,34% | 33,67% | 36,18% | 86% | #DIV/0!
Class F | 37,68% | 39,80% | 42,51% | 133% | #DIV/0!

## Slide 8: Proposal: Normative Intra Refresh
Add the signalization for indicating the position of IR CUs.
Exploit this IR CUs positions knowledge to improve the quality for this low latency use-case:
  Do not transmit pred_mode_flag nor cu_skip_flag on IR CU.
  Enable CIP only on IR CU.
  Disabling Deblocking at IR boundary
  => This allows to partially relax the MV constraint (from 6 to 2 pixels).
JVET-M0387

## Slide 9: New signalization
SPS level:
  sps_intra_refresh_enabled_flag
PPS level:
  pps_intra_refresh_mode
  pps_intra_refresh_size
  pps_intra_refresh_delta_qp
Tile-group level:
  tile_group_intra_refresh_direction
  tile_group_intra_refresh_position
JVET-M0387

## Slide 10: Results: Normative Intra Refresh
Promising improvement.
JVET-M0387
 | Low-delay B ormative intra refresh Main 10 |  |  |  | 
 | Over Enc-only Intra Refresh VTM3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALEUR! | #VALEUR! | #VALEUR! | #NOMBRE! | #DIV/0!
Class C | -5,12% | -8,00% | -9,01% | 110% | #DIV/0!
Class E | -6,59% | -7,69% | -9,05% | 106% | #DIV/0!
Overall | #VALEUR! | #VALEUR! | #VALEUR! | #NOMBRE! | #DIV/0!
Class D | -5,18% | -7,74% | -8,50% | 108% | #DIV/0!
Class F | -8,03% | -10,09% | -10,93% | 79% | #DIV/0!

## Slide 11: Conclusion
The implementation of both encoder-only and normative Intra Refresh have been updated for VTM3 and shared on AHG14 Gitlab.
Associated testing conditions have been proposed.
Performance have been characterized:
  Significant losses of 21.6% in average for encoder-only implementation.
  Normative solution improvement of 5% against enc-only.
A normative solution is desirable to bring low-latency functionnality with reduced loss on VVC.
Recommendation:
  To agree on the proposed test conditions for AHG 14 testing.
  To integrate encoder-only modfications within VTM software.
  To further study the normative solution.
JVET-M0387

## Slide 12: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.