## Slide 1: JVET-M0387 AHG14: Updates on Intra Refresh Proposal
Jean-Marc Thiesse
Didier Nicholson
David Gommelet

## Slide 2: Background
Intra Refresh is a classical technology addressing:
  Low-latency by removing of sizeable I picture while keeping random accessibility of stream
  And/or error resilience.
Usually implemented by encoder-only modifications leading to significant efficiency losses.
AhG 14 was established at Ljubljana.
JVET-M0387

## Slide 3: Summary
This contribution provides updated results of JVET-L0160 and JVET-L0161 to address AhG14 following mandates:
  Proposition of test conditions for studying Intra Refresh.
  Proposition of an encoder-only Intra Refresh implementation.
  Characterization of the solution.
  Study of a normative solution.
Loss of 21.3% for enc-only solution vs fair reference.
Normative solution improvement of 5% with slightly intrusive modifications.
JVET-M0387

## Slide 4: Encoder-only Intra Refresh
The software modifications to support Intra Refresh tool at the encoder-level in VTM software include:
  Intra prediction mode forced on column basis at CU level.
  Constrained Intra Prediction enabled.
  Motion vectors constrained (+6 pixels due to filters).
  Removing of former reference pictures at re-looping.
  Disabling of ALF of CTU including Intra refresh pixels.
JVET-M0387

## Slide 5: Software modifications
Shared on AHG14 Gitlab.
15 changed files, 330 lines modifications.
The additional parameters added to the configuration file are as follows:
  IntraRefreshType : 1 # Intra Refresh type flag 0: disable, 1: enc-only, 2: normative
  IntraRefreshStart : 0 # Position of the first column of Intra refresh (in pixels)
  IntraRefreshDirection : 0 # Direction of Intra Refresh 0: left to right, 1: right to left
  IntraRefreshPeriod : 32 # Period of the Intra Refresh
JVET-M0387

## Slide 6: Test condition for Intra Refresh
Intra Refresh anchor proposal:
  Basis= Low-Delay B Main10 configuration.
  Without pyramidal B structure (GOPSize = 1)
  QP offset of 1 between I and P picture (same QP for IR).
  Intra Refresh period of 32 (as Random Access).
Reference for losses characterization:
  Same with an Intra period of 32 (DecodingRefreshType = 1).
JVET-M0387

## Slide 7: Results: Enc-only Intra Refresh
Significant losses, especially for low motion sequences.
JVET-M0387
 | Low delay B Intra Refresh Encoder Only Main 10 |  |  |  | 
 |  |  | Over VTM-3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 12,53% | 23,35% | 35,68% | 93% | #DIV/0!
Class C | 18,75% | 24,36% | 26,79% | 94% | #DIV/0!
Class E | 39,27% | 43,52% | 51,34% | 91% | #DIV/0!
Overall | 21,29% | 28,73% | 36,63% | 93% | #DIV/0!
Class D | 22,34% | 33,67% | 36,18% | 86% | #DIV/0!
Class F | 37,68% | 39,80% | 42,51% | 133% | #DIV/0!

## Slide 8: Proposal: Normative Intra Refresh
Add the signalization for indicating the position of IR CUs.
Exploit this IR CUs positions knowledge to improve the quality for this low latency use-case:
  Do not transmit pred_mode_flag nor cu_skip_flag on IR CU.
  Enable CIP only on IR CU.
  Disabling Deblocking at IR boundary
  => This allows to partially relax the MV constraint (from 6 to 2 pixels).
JVET-M0387

## Slide 9: New signalization
SPS level:
  sps_intra_refresh_enabled_flag
PPS level:
  pps_intra_refresh_mode
  pps_intra_refresh_size
  pps_intra_refresh_delta_qp
Tile-group level:
  tile_group_intra_refresh_direction
  tile_group_intra_refresh_position
JVET-M0387

## Slide 10: Results: Normative Intra Refresh
Promising improvement.
JVET-M0387
 | Low delay B Normative Intra Refresh Main10 |  |  |  | 
 | Over Low delay B Enc-only Intra Refresh VTM3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.01% | -7.00% | -8.82% | 88% | #DIV/0!
Class C | -5.12% | -8.00% | -9.01% | 110% | #DIV/0!
Class E | -6.59% | -7.69% | -9.05% | 106% | #DIV/0!
Overall | -5.02% | -7.51% | -8.94% | 99% | #DIV/0!
Class D | -5.18% | -7.74% | -8.50% | 108% | #DIV/0!
Class F | -8.03% | -10.09% | -10.93% | 79% | #DIV/0!

## Slide 11: Conclusion
The implementation of both encoder-only and normative Intra Refresh have been updated for VTM3 and shared on AHG14 Gitlab.
Associated testing conditions have been proposed.
Performance have been characterized:
  Significant losses of 21.6% in average for encoder-only implementation.
  Normative solution improvement of 5% against enc-only.
A normative solution is desirable to bring low-latency functionnality with reduced loss on VVC.
Recommendation:
  To agree on the proposed test conditions for AHG 14 testing.
  To integrate encoder-only modfications within VTM software.
  To further study the normative solution.
JVET-M0387

## Slide 12: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.

## Slide 13: Context: Low latency
Low latency is key for several market use-cases.
  Not only for video conferencing
    e.g. any application with someone in the loop (cloud gaming, drones, remote system operation…)
    Contribution market which needs ultra low latency
  Latency is one key marketing feature for selling encoders
Latency (and error resilience) were a mandate of JVET CfP.

## Slide 14: Context: Low latency
Latency comes from various parts of a streaming system:
  Encoding configuration such as GOP structure (=>no reordering)
  Encoding/Decoding time itself (=>dependent slices)
  Network handling:
    Intra picture size is significantly higher than Inter to get the quality.
    Intra pictures took the time of several pictures to be sent.
  No normative solution to address specifically this latency issue

## Slide 15: Classical solution: Intra Refresh
Intra Refresh (IR) is often used to solve this issue by encoder manufacturers:
  A group of pixels (column, line, pseudo-random…) is periodically forced to Intra instead of sending one big Intra picture (latency ok).
  The position of refreshed pixels moves along the encoding so that a clean region is produced to ensure the reconstruction/stream access:

## Slide 16: Without Intra Refresh
x8!!

## Slide 17: Intra Refresh

## Slide 18: Intra Refresh drawbacks
This solution is a « trick » at the encoder level.
Needs several modifications that make bitrate losses:
  Constrained Intra Prediction (CIP) to insure clean refresh.
  Motion vector restrictions (do not point to dirty regions).
  Reference picture constraints at re-looping, etc.
Stream connection not well-managed.
This situation can be improved with a clean and appropriate normative syntax.