## Slide 1: JVET-M0444 CE4-related: Simplified symmetric MVD based on CE4.4.3
Jiancong Luo, Yuwen He
InterDigital Inc.
January, 2019

## Slide 2: Introduction
Symmetric MVD mode in CE4.4.3 (JVET-M0481)
  ref_l0_dx and ref_l1_idx are not signaled but derived
  MvdL0 is signaled, MvdL1 is not signaled.
  MV calculation

## Slide 3: Proposed Simplified Symmetric MVD
Disallow BDOF for Symmetric MVD mode
  BDOF is not effective for Symmetric MVD and can be disallowed to reduce decoder complexity
Encoder side optimization
  Choose initial MV from a set of candidates
    the MV obtained from uni-prediction search
    the MV obtained from bi-prediction search
    the MVs from the AMVP list

## Slide 4: Experimental results
4
© 2018 InterDigital, Inc. All Rights Reserved.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.34% | -0.44% | -0.46% | 105% | 99%
Class A2 | -0.42% | -0.41% | -0.41% | 105% | 99%
Class B | -0.34% | -0.32% | -0.33% | 105% | 99%
Class C | -0.25% | -0.27% | -0.22% | 104% | 99%
Class E |  |  |  |  | 
Overall | -0.33% | -0.35% | -0.34% | 105% | 99%
Class D | -0.17% | -0.29% | -0.18% | 104% | 99%
Class F (optional) | -0.33% | -0.33% | -0.29% | 105% | 99%
Table 1: Compare to VTM-3.0
Peak gain: -0.51% (class A1 Tango2), -0.79% (class F slideshow)

## Slide 5: Experimental results
5
© 2018 InterDigital, Inc. All Rights Reserved.
 | Random Access Main 10 |  |  |  | 
 | Over CE4.4.3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.29% | -0.25% | 101% | 100%
Class A2 | -0.22% | -0.27% | -0.26% | 101% | 99%
Class B | -0.19% | -0.23% | -0.16% | 102% | 98%
Class C | -0.12% | -0.16% | -0.12% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.17% | -0.23% | -0.18% | 101% | 99%
Class D | -0.09% | -0.21% | -0.14% | 100% | 100%
Class F (optional) | -0.21% | -0.21% | -0.18% | 100% | 100%
Table 2: Compare to CE4.4.3

## Slide 6: Summary
Propose simplified Symmetric MVD based on CE4.4.3
  Disable BDOF in Symmetric MVD mode
  Symmetric MVD search algorithm optimization
Performance
  -0.33% with 5% Encoder Time increase over VTM 3.0
  -0.17% with 1% Encoder Time increase over CE4.4.3
Propose for adoption to VVC
Thank Huawei for cross-checking (JVET-M0721)