## Slide 1: Non-CE3: Combined-Hypothesis Intra-Prediction
Gosala Kulupana, André Seixas Dias, Saverio Blasi
13th JVET Meeting: Marrakech, MA, 9–18 Jan. 2019
JVET-M0458

## Slide 2
General idea
VTM 3.0 allows intra-prediction with Planar, DC or one of 65 Angular modes
When using one of the Angular modes, idea is to also compute Planar prediction of the same block and average the two predictions

## Slide 3
Proposed method
Combined-Hypothesis Intra-Prediction is computed by averaging an Angular prediction (PAng) with the Planar prediction (PPlanar) of the same sample
One flag is signalled if the current mode is Angular, to indicate if the combination is used or not.
The method is restricted to be used only on large blocks (larger than 8x8 with no size smaller than 32)
Method is not used if MRL is used

## Slide 4
Performance results
 |  |  | AI Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.46% | -0.30% | -0.18% | 108% | 101%
Class A2 | -0.13% | -0.07% | -0.05% | 106% | 101%
Class B | -0.10% | -0.10% | -0.07% | 103% | 100%
Class C | -0.03% | -0.01% | -0.06% | 102% | 98%
Class E | -0.11% | -0.07% | -0.01% | 103% | 98%
Overall | -0.15% | -0.10% | -0.07% | 104% | 99%
Class D | -0.02% | -0.08% | -0.08% | 103% | 104%
Class F | -0.01% | 0.08% | 0.08% | 104% | 97%
 |  |  | RA Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.18% | -0.37% | -0.31% | 103% | 101%
Class A2 | -0.07% | -0.04% | 0.03% | 101% | 102%
Class B | -0.07% | 0.14% | -0.15% | 101% | 101%
Class C | 0.00% | -0.10% | -0.09% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.07% | -0.06% | -0.13% | 101% | 101%
Class D | -0.01% | -0.01% | -0.23% | 100% | 102%
Class F | 0.00% | 0.06% | 0.16% | 101% | 101%

## Slide 5
Conclusion
Combination of angular prediction with planar prediction of the same block is proposed
Single flag change in the syntax
Average All-Intra BD-rates of -0.15% (Y), -0.10% (U) and -0.07% (V) for 104% encoder complexity and ~100% (99%) decoder complexity
Class A1 All-Intra gains -0.46% (Y), -0.30% (U) and -0.18% (V)
Class A1 Random-Access gains -0.18% (Y), -0.37% (U) and -0.31%

## Slide 6: Thank you
www.bbc.co.uk/rd
gosala.kulupana@bbc.co.uk
Email: