## Slide 1: Non-CE8: CPR with chroma 4x4 sub-block size when dual-tree is on (JVET-M0544)
X. Xu, X. Li, S. Liu (Tencent)
2019/01

## Slide 2: Summary
Currently, when Dual-Tree is used, a CPR coded chroma CU works on sub-block mode where each sub-block size is 2x2
In VTM-3.0, chroma sub-block size for inter coding (affine) is expanded from 2x2 to 4x4.
It is proposed that for CPR case, the chroma sub-block size is also set to 4x4, as a unification
  The top-left 4x4 luma block’s vector is used to represent the whole 4x4 chroma sub-block
It is reported that with the proposed method, the runtime/BD rate changes are

## Slide 3: Motivation
In affine MC, the chroma sub-block size is set to be 4x4.
  The average MV of 4 4x4 corresponding luma MVs is used to derive the chroma MV
It is desirable to have CPR/inter unified
  With the same chroma sub-block size

## Slide 4: Proposed method
In CPR with dual-tree on, chroma CU is coded in sub-block mode with sub-block size 2x2
It is proposed to expand the sub-block size of CPR chroma CU to be 4x4, same as affine sub-block
  The top-left 4x4 luma MV is used to derive the chroma MV
  Using the average of luma MVs may cause availability issue

## Slide 5: Simulation results
Results are compared with VTM-3.0 and VT-3.0+CPR=1 anchors
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on-bugfix |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.11% | 0.07% | 127% | 99% | 0.00% | -0.01% | 0.01% | 97% | 97%
Class A2 | -0.47% | -0.54% | -0.52% | 131% | 100% | 0.00% | -0.04% | 0.02% | 100% | 101%
Class B | -0.29% | -0.37% | -0.33% | 138% | 98% | 0.01% | 0.01% | 0.02% | 101% | 98%
Class C | -0.09% | -0.25% | -0.25% | 142% | 96% | 0.00% | -0.01% | 0.00% | 99% | 96%
Class E | -0.63% | -0.82% | -0.63% | 141% | 96% | 0.00% | -0.01% | -0.03% | 99% | 95%
Overall | -0.27% | -0.40% | -0.33% | 136% | 98% | 0.00% | -0.01% | 0.01% | 100% | 97%
Class D | -0.10% | -0.24% | 0.21% | 138% | 96% | 0.00% | -0.01% | 0.00% | 101% | 98%
Class F (optional) | -12.04% | -11.99% | -11.92% | 156% | 94% | 0.06% | 0.08% | 0.22% | 99% | 96%
Class SCC 1080p | -36.60% | -35.56% | -35.74% | 142% | 87% | 0.57% | 0.90% | 1.02% | 99% | 96%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on-bugfix |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.14% | -0.03% | 0.32% | 98% | 99% | 0.00% | -0.01% | 0.02% | 97% | 98%
Class A2 | 0.00% | 0.07% | 0.16% | 96% | 99% | 0.00% | 0.11% | -0.01% | 97% | 98%
Class B | 0.02% | -0.02% | -0.26% | 97% | 96% | -0.01% | 0.01% | 0.01% | 98% | 95%
Class C | 0.20% | -0.21% | 0.05% | 101% | 95% | 0.01% | -0.17% | -0.11% | 99% | 96%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.09% | -0.06% | 0.02% | 98% | 97% | 0.00% | -0.02% | -0.03% | 98% | 97%
Class D | 0.16% | -0.22% | 0.13% | 101% | 96% | -0.03% | -0.08% | -0.09% | 100% | 99%
Class F (optional) | -9.80% | -9.78% | -9.81% | 106% | 96% | 0.11% | 0.20% | 0.22% | 99% | 97%
Class SCC 1080p | -22.04% | -21.62% | -22.13% | 101% | 91% | 0.25% | 0.41% | 0.41% | 98% | 95%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on-bugfix |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.08% | -0.13% | -0.06% | 106% | 99% | 0.01% | -0.12% | -0.35% | 99% | 101%
Class C | 0.12% | 0.48% | 0.39% | 107% | 96% | 0.01% | 0.10% | 0.02% | 98% | 94%
Class E | 0.13% | 1.00% | -0.36% | 103% | 96% | -0.06% | -0.28% | -0.16% | 98% | 95%
Overall | 0.10% | 0.35% | 0.02% | 106% | 97% | 0.00% | -0.09% | -0.18% | 98% | 97%
Class D | 0.17% | -0.34% | 0.63% | 111% | 93% | 0.00% | -0.10% | -0.01% | 99% | 92%
Class F (optional) | -5.12% | -4.89% | -5.35% | 107% | 95% | 0.07% | 0.64% | 0.29% | 100% | 97%
Class SCC 1080p | -13.29% | -13.69% | -13.93% | 109% | 98% | -0.08% | -0.08% | -0.12% | 97% | 100%

## Slide 6: Conclusion
In this contribution, chroma CU sub-block size in CPR mode is set to be 4x4, from 2x2 originally
  Top-left luma 4x4 MV is used to derive chroma MV
It is assert that this unifies the corresponding aspect with inter sub-block size (4x4)
It is recommended to adopt this proposal into next VTM release
Thanks LGE for performing crosschecking!