## Slide 1: Non-CE7: On derivation of quantization parameter predictor (JVET-M0685)
K. Misra and A. Segall

## Slide 2: Introduction
In the current VVC design, QP is predicted as follows:
  Average of the QP value to the left and above quantization group
  When neither of the CU neighbors are available, then the QP predictor is set equal to the Slice QP
  When one of the neighbors is not available, set the QP for that neighbor equal to the QP of the previous coded CU
This contribution considers the last condition.

## Slide 3: Problem
When coding a picture, the left neighbor will not be available at the start of a CTU row
This means that the QP of the previous quantization group will correspond to the quantization group at the end of the previous row

## Slide 4: Problem
When coding a picture, the left neighbor will not be available at the start of a CTU row
This means that the QP of the previous quantization group will correspond to the quantization group at the end of the previous row

## Slide 5: Problem
We assert that using the QP from the end of the previous CTU row is undesirable for two reasons
  When modulating the QP value based on image content (such as activity or intensity), the QP value at the end of the previous row is often a poor predictor for the beginning of the row
  When encoding a sequence using a wavefront technique, the QP value of the end of the last row isn’t known when beginning to code the current row

## Slide 6: Problem
To address the issue, we propose the following:
  Average of the QP value to the left and above quantization group
  When neither of the CU neighbors are available, then the QP predictor is set equal to the Slice QP
  When one of the neighbors is not available, set the QP for that neighbor equal to the QP of the previous coded CU available neighbor.