## Slide 1: JVET-M0736
CE10-related: Triangular prediction with MMVD
Max Bläser
RWTH Aachen University
blaeser@ient.rwth-aachen.de

## Slide 2: Introduction
Current method of motion information coding for triangular prediction is based on merge mode [1]
Other methods, especially AMVP based motion coding has been proposed [2]
In the current VVC draft [3] and VTM software, an apparent syntax redundancy exists, where the triangle merge mode flag is signaled independent of the value of the MMVD mode flag
Combination of the two approaches is currently not possible
 Instead of removing redundancy it is proposed to enable MMVD-based coding of motion vector for triangular prediction

## Slide 3: Proposed method
Syntax changes required
  Signaling of triangle split direction separately if MMVD flag and triangle flag is enabled
  MMVD-related syntax elements (base predictor flag, direction index, distance index) decoded twice
  Otherwise if MMVD flag disabled, triangle merge index is decoded as currently specified
Decoder
  MMVD related reconstruction branch integrated next to MERGE based reconstruction
  Triangular merge candidate list is used for MMVD base predictor selection to ensure uni-directional MVs are used
Encoder
  Full search of all 64 possible MMVD-based vectors for each triangle
Figure 1: Decoder loop changes for the integration of MMVD and triangular partitioning (red).

## Slide 4: Experimental results (RA)
Experiments conducted using the VTM-3.0 software [4] with the VTM configuration and according to the JVET common test conditions JVET-L1010 [5], bandwidth measurements according to JVET-K0451 [6]
 | Random Access Main 10 |  |  |  |  |  |  | Random Access Main10 | 
 | Over VTM-3.0 |  |  |  |  |  |  | Tool off | 
 | Y | U | V | EncT | DecT | ave mem BW | max mem BW | Impacted Pixels | Adj DecT
Class A1 | -0.02% | -0.17% | -0.21% | 142% | 101% | 100% | 101% | 1.51% | 
Class A2 | -0.19% | -0.26% | -0.39% | 154% | 101% | 100% | 100% | 1.39% | 
Class B | -0.14% | -0.19% | -0.07% | 157% | 99% | 100% | 101% | 1.71% | 
Class C | -0.19% | -0.30% | -0.31% | 171% | 101% | 100% | 100% | 3.64% | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.14% | -0.23% | -0.23% | 157% | 100% | 100% | 101% | 2.12% | 
Class D | -0.30% | -0.41% | -0.52% | 176% | 100% | 99% | 100% | 2.91% | 
Class F | -0.08% | -0.13% | -0.17% | 158% | 101% | 100% | 103% | 2.56% | 

## Slide 5: Experimental results (LB)
 | Low delay B Main10 |  |  |  |  |  |  | Low delay B Main10 | 
 | Over VTM-3.0 |  |  |  |  |  |  | Tool off | 
 | Y | U | V | EncT | DecT | ave mem BW | max mem BW | Impacted Pixels | Adj DecT
Class A1 |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  | 
Class B | -0.27% | -0.24% | -0.42% | 204% | 100% | 100% | 101% | 3.71% | 
Class C | -0.44% | -0.89% | -0.57% | 233% | 97% | 100% | 101% | 6.09% | 
Class E | -0.65% | -0.26% | -0.58% | 219% | 99% | 100% | 100% | 3.90% | 
Overall | -0.33% | -0.48% | -0.54% | 224% | 100% | 100% | 101% | 4.55% | 
Class D | -0.65% | -0.26% | -0.58% | 219% | 99% | 100% | 100% | 7.56% | 
Class F | -0.37% | -0.61% | 0.71% | 184% | 103% | 100% | 100% | 2.88% | 

## Slide 6: Conclusion
For RA, a BD-rate change of -0.14% can be achieved with an increase in encoder complexity to 157%
For LB, a BD-rate change of ‑0.33% can be achieved with an encoder complexity increase to 224%
No increase in decoder complexity or memory bandwidth is reported
It is proposed to further study the integration of MMVD with triangular partitioning, as no additional decoder complexity is added when the two tools are combined
It is recommended to investigate how fast-decision heuristics at the encoder side can limit the additional encoder runtime

## Slide 7: References
[1] R.-L. Liao, C. S. Lim, "CE10.3.1.b: Triangular prediction unit mode", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-L0124, 12th Meeting, Macao, CN, October 2018
[2] Y. Ahn, D. Sim (Digital Insights), "CE10: Diagonal motion partitions with uni-prediction constraint (Test 1 0.3.3)", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-L0125, 12th Meeting, Macao, CN, October 2018
[3] B. Bross, J. Chen, S. Liu (editors), "Versatile Video Coding (Draft 3)", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-L01001, 12th Meeting, Macao, CN, October 2018
[4] VVC Reference Software, https://vcgit.hhi.fraunhofer.de/jvet/VVCSoftware_VTM
[5] F. Bossen, J. Boyce, K. Suehring, X. Li, V. Seregin, “JVET common test conditions and software reference configurations”, Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET- L1010, 12th Meeting, Macao, CN, October 2018.
[6] R. Hashimoto, S. Mochizuki, "AHG5: How to use the software to evaluate memory bandwidth", Joint Video Exploration Team of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JVET-K0451 11th Meeting, Ljubljana, SI, July 2018