## Slide 1: JVET-N0133 CE13-related: Integrated in-loop filter based on CNN
Authors：
Shuai Wan, Mingze Wang,
Yanzhuo Ma, Junyan Huo,
Hao Gong, Chengyi Zou,
YuanFang Yu, Yang Liu
Reporter： Mingze Wang

## Slide 2: Outline
JVET-N0133
Introduction
Proposed WSE-CNNLF
Experimental Results
Conclusion

## Slide 3: Introduction
JVET-N0133
In-loop filters in VTM-4.0
In-loop filters proposed
  All conventional filters (DBF, SAO and ALF) are replaced

## Slide 4: Proposed WSE-CNNLF
JVET-N0133
Network inputs
  Reconstructed frames before in-loop filters (Y/U/V)
  Two CUmaps, one for Y, the other shared by U/V
  One QPmap
Y
U
V
CUmap_Y
CUmap_UV

## Slide 5: Proposed WSE-CNNLF
JVET-N0133
CUmap
  Indicating QTBTTT partition strcture
  The positions of the boundary are filled by 2
  and other positions by 1

## Slide 6: Proposed WSE-CNNLF
JVET-N0133
QPmap
  Indicating the level of degradation
  All positions are filled by QP
  One model with one set of parameters, applied to multi-quality reconstruction

## Slide 7: Proposed WSE-CNNLF
JVET-N0133
Processing module —— wide-SE-block
  Wide-activated convolution
    works well on the task of image enhancement/super-resolution/denoising
    wider channels before ReLU activation
  Squeeze-and-Excitation
    channel attention

## Slide 8: Proposed WSE-CNNLF
JVET-N0133
stage1. separately
stage2. jointly
stage3. separately

## Slide 9: Experimental Results
JVET-N0133
Training stage
Mandatory | Information in Training Stage |  | 
 | Basic Settings: |  | 
 |  | learning rate: | 1e-3
 |  | optimizer: | ADAM
 |  | batch size: | 100
 |  | epoch: | 200
 |  | loss function: | L2
 |  | training GPU: | GTX 1080ti
 |  | training time: | 96h
 |  | framework: | Tensorflow
Optional | Other Settings: |  | 
 |  | patch size: | 64x64, randomly cropped
 |  | additional dataset (besides DIV2K): | None
 |  | QP set for generating training dataset: | {22,27,32,37}

## Slide 10: Experimental Results
JVET-N0133
Reference stage
Network Details |  |  |  |  |  | 
Total Conv. Layers | Total FC Layers | Frame-work | Param. Num | Param. Precision | Mem.P(MB) | Mem.T(MB) (e.g., 4K input)
39 | 36 | Tensorflow | 519112 | 32(F) | 1.98 | H*W*2.68*10e-3

## Slide 11: Experimental Results
JVET-N0133
 | All Intra Main10 (GPU) |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -3.99% | -10.41% | -10.75% | 81% | 1762%
Class C | -5.92% | -9.56% | -12.46% | 61% | 2847%
Class E | -7.26% | -6.89% | -9.10% | 60% | 2451%
Overall | -5.72% | -8.95% | -10.77% | 67% | 2353%
Class D | -6.24% | -12.31% | -16.61% | 62% | 4510%
Class F | 10.52% | 11.89% | 6.30% | 62% | 2127%
Simulation results (with GPU)
The negative gain of classF is caused by the lack of screen contents in DIV2K dataset

## Slide 12: Conclusion
JVET-N0133
Propose a CNN filter as a integrated in-loop filter to replace DBF,SAO and ALF
  Discover useful information(CUmap) as auxiliary inputs to guide deblocking
  One network shared by Y/U/V component
  Residual learning
Experimental results shows -5.72%,.-8.95%, -10.77% BD-rate savings for luma and both chroma components for VTM4.0 with AI configuration.