## Slide 1
JVET-P0110
AHG15 Quantization matrices with single identifier and enhanced prediction

## Slide 2
Summary
© 2019 InterDigital, Inc. All Rights Reserved.
Changes to Quantization Matrix indexing and prediction
  1. Add inter-size prediction (like JVET-O0223)
  2. Add residual to prediction
  3. Add scaled prediction
  4. Remove prediction flag
Simplified syntax
54% bit savings for example QMs
Notes: Follow-up of JVET-O0223. Meeting notes said: For further study and potential action at the next meeting + It was commented that the bit efficiency depends on the selected example QMs to encoded.
It was commented that having the ability to do a prediction with a difference would provide more of an assurance that the bits would generally be minimized for more arbitrary selections of QMs to be encoded

## Slide 3
Syntax
© 2019 InterDigital, Inc. All Rights Reserved.
Current
Proposed

## Slide 4
1. Add inter-size prediction
© 2019 InterDigital, Inc. All Rights Reserved.
Current VVC draft identifies QMs with two ids: sizeId and matrixId
  Allows prediction (copy) from same sizeId only
  Controlled by scaling_list_pred_matrix_id_delta
Proposal uses a single id
  Sort QMs by decreasing size, allow prediction from any
  Downsample reference when needed.

## Slide 5
QM indexing & prediction paths
© 2019 InterDigital, Inc. All Rights Reserved.
Current
Proposed

## Slide 6
2. Add residual to prediction
© 2019 InterDigital, Inc. All Rights Reserved.
Use the current coef signalling on top of prediction
But with variable length: signal coefNum
Diagonal scan
  Low-frequency coefficients (most significant) are sent first
  Enables adjusting just a few LF coefficients at low cost
DCPM-coding makes last residual coefficient repeat
  One coefficient = global offset

## Slide 7
3. Add scale to prediction
© 2019 InterDigital, Inc. All Rights Reserved.
Apply a scale factor to prediction
  Matches commonly found adjustment, e.g. intra > inter
  Pivot around 16: QM = (predQM – 16)*scale + 16
  0 to 2 scale, in 1/16th steps.
  se(v) coding with -16 bias: scale=1 cost is 1 bit
HEVC default - intra (grid)
- inter (solid)
intra scaled
(12/16)

## Slide 8
4. Remove prediction flag
© 2019 InterDigital, Inc. All Rights Reserved.
Enhanced prediction makes it more likely
  Flag almost always 0 (prediction ON)
No-prediction mode = all-8 predictor
  Similar to prediction from all-16 default matrix, or zero-scale from any. No feature loss.
Always predict = save 30 bits of flags
  Always signal prediction data (coefNum)
  Tests indicate a small gain
  Simplifies spec

## Slide 9
Draft text amount
© 2019 InterDigital, Inc. All Rights Reserved.
 | Current | Proposed
Pages | 5 | 3
Lines | 579 | 216
Words | 2691 | 1057
Characters | 10402 | 5332
Text to support QMs is approximately cut by half

## Slide 10
Less bits
© 2019 InterDigital, Inc. All Rights Reserved.
 | VVC d.6 | P0110
QMs every picture | +7.2% | +3.4%
QMs every I-period | +.14% | +.06%
Test performed with example QMs derived from HEVC CEs + popular standards + captures
 | bits | / VVC
VVC.d6 | 2964 | -
P0110 | 1378 | -54%
Impact of QMs on BDRate
scaling_list_data
Picture-level QMs: ~4% gain

## Slide 11
Conclusion
© 2019 InterDigital, Inc. All Rights Reserved.
Proposal enables prediction across all QMs (including other sizes)
Prediction with scale factor and custom-sized residual
Simplified syntax and unified derivation for all QMs
Ability to transmit a first QM and derive all others with scale and small adjustments greatly reduces the overhead of custom QMs
opens the door to picture-level QMs with block-size and block-type adaptation
Thanks to MediaKind for cross-checking (JVET-P0754)
Notes: ~ 500 bits is a reasonable target still offering good flexibility  per-picture = 1.2% BDRate

## Slide 12
- backup -

## Slide 13
Syntax diff

## Slide 14
QM decoding functional diagram
© 2019 InterDigital, Inc. All Rights Reserved.
↓
default QM
other QM
QM
scaling_list_pred_matrix_id_delta
coefNum
↓
ScalingList
scaling_list_pred_scale_minus16

## Slide 15
Less bits
© 2019 InterDigital, Inc. All Rights Reserved.
 | VVC d.6 | P0110 | Lossy
QMs every picture | +7.2% | +3.4% | +2.5%
QMs every I-period | +.14% | +.06% | +.05%
Test performed with example QMs derived from HEVC CEs + popular standards + captures Lossy : truncated residual with <1.5 mean absolute error (per QM)
 | bits | / VVC | / HEVC
HEVC | 2340 | - | -
VVC.d6 | 2964 | - | +27%
P0110 | 1378 | -54% | -41%
lossy | 991 | -67% | -58%
Impact of QMs on BDRate
scaling_list_data
Picture-level QMs: ~4% gain