## Slide 1: JVET-P0136: MIP modifications
Junyan Huo, Haixin Wang, Yu Sun, Yanzhuo Ma,
Shuai Wan, Fuzheng Yang,
Yuanfang Yu, Yang Liu,
October. 2019
MIP simplification

## Slide 2: Summary
To get input values p[ i ]
The MIP prediction signal predMip[ x ][ y ] is computed as
If MipSizeId[ xTbCmp ][ yTbCmp ] is equal to 2, the following applies:
p[ i ] = pTemp[ i + 1 ] − pTemp[ 0 ]
Otherwise (MipSizeId[ xTbCmp ][ yTbCmp ] is less than 2), the following applies:
p[ 0 ] = pTemp[ 0 ] −( 1 << ( BitDepthY − 1 ) ) p[ i ] = pTemp[ i ] − pTemp[ 0 ] for i = 1.. inSize − 1
predMip[ x ][ y ] = ( ( ( ) +oW ) >> sW ) + pTemp[ 0 ]

## Slide 3: Summary
Proposed method to simply the table of offset factor (fO)
  Modify the input value p[0]
  Simplify the table of fO
Benefits
  Reduce fO table size and dimension
  No coding loss

## Slide 4: MIP simplification
sW, fO, and mWeight are changed correspondingly

## Slide 5: MIP simplification
Simply table of the offset factor (fO) by depending on MipSizeId only
 | modeId |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MipSizeId | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
0 | 34 | 19 | 7 | 32 | 27 | 24 | 21 | 13 | 24 | 15 | 27 | 20 | 16 | 7 | 20 | 23 | 21 | 24
1 | 17 | 20 | 11 | 21 | 17 | 11 | 23 | 10 | 21 | 11 |  |  |  |  |  |  |  | 
2 | 8 | 46 | 16 | 10 | 13 | 11 |  |  |  |  |  |  |  |  |  |  |  | 
MipSizeId | fO
0 | 34
1 | 23
2 | 46
Reduce 34 fO values to 3 fO values.

## Slide 6: Experimental results
 |  |  | All Intra |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | 0.05% | 100% | 100%
Class A2 | 0.01% | 0.04% | -0.03% | 101% | 101%
Class B | 0.00% | 0.01% | -0.03% | 100% | 100%
Class C | 0.01% | -0.15% | 0.01% | 100% | 100%
Class E | 0.00% | 0.04% | -0.03% | 99% | 101%
Overall | 0.00% | -0.01% | -0.01% | 100% | 100%
Class D | -0.01% | -0.07% | -0.12% | 100% | 100%
Class F | 0.01% | -0.01% | -0.02% | 100% | 101%
 |  |  | Random Access |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.11% | 0.04% | 100% | 100%
Class A2 | 0.01% | 0.08% | 0.03% | 100% | 100%
Class B | -0.01% | 0.09% | -0.09% | 100% | 100%
Class C | -0.01% | -0.09% | -0.02% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.02% | 100% | 100%
Class D | 0.01% | -0.21% | -0.27% | 100% | 100%
Class F | -0.03% | 0.10% | -0.10% | 101% | 101%

## Slide 7: Conclusion
2D fO table with 34 values are reduced into 1D table with 3 values.
No loss:
    AI: 0.00% -0.01% -0.01% 100% 100%
    RA: 0.00% 0.00% -0.02% 100% 100%
Recommend to adopt into VVC CD.
Thanks crosschecking by.

## Slide 8
Thank you

## Slide 9: MIP simplification
sW, fO, and mWeight are changed correspondingly

## Slide 10: MIP simplification
sW, fO, and mWeight are changed correspondingly
The matrix values are identical with the matrix values in VVC CD