## Slide 1
JVET-P0173
AHG16/Non-CE5: Cross component ALF simplification
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
AHG16 has following comments on CCALF (CE5-2.1/JVET-O0636):
The multiplication overhead of the CCALF being tested in the CE is about 50% of the current luma and chroma ALF design, while the expected gain is about 1% (on the top of existing ~5% ALF gain in RA). It would be desirable to study whether a better trade-off exists outside the CE.
ALF has approximately 4.65% coding gain (RA) over VTM6.0
CCALF increases complexity (counting number of multiplications) by 42% with approximately 1.16% coding gain (RA, 24.5% increase w.r.t. ALF), which is not a desirable trade-off.

## Slide 3
Proposal
The first part of this proposal proposes to reduce filter shape. 3 settings (a, b, c) are tested.

## Slide 4
Simulation results (without gain shift)
number of coefficients = 6
number of coefficients = 7
number of coefficients = 8
 |  | All Intra Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.13% | -3.49% | -4.16% | 105% | 103%
0.13% | -8.67% | -8.93% | 103% | 104%
0.10% | -10.56% | -8.57% | 102% | 102%
0.13% | -4.18% | -3.91% | 102% | 101%
0.19% | -10.16% | -3.46% | 103% | 103%
0.13% | -7.58% | -6.01% | 103% | 103%
0.11% | -2.74% | -3.28% | 101% | 103%
0.18% | -6.58% | -6.64% | 102% | 102%
 |  | Random access Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.13% | -5.65% | -5.34% | 100% | 99%
0.21% | -11.72% | -15.74% | 100% | 101%
0.21% | -17.63% | -14.08% | 102% | 100%
0.09% | -5.03% | -4.35% | 103% | 100%
0.16% | -10.69% | -10.07% | 101% | 100%
0.11% | -4.45% | -4.46% | 100% | 100%
0.18% | -4.73% | -4.61% | 102% | 98%
 |  | Low delay B Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.18% | -21.52% | -19.23% | 102% | 100%
0.12% | -8.18% | -6.44% | 101% | 100%
0.24% | -15.69% | -6.37% | 100% | 97%
0.17% | -15.62% | -11.75% | 101% | 99%
0.18% | -8.10% | -6.04% | 103% | 102%
0.13% | -10.52% | -7.54% | 104% | 100%
CE5-2.1
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | -2.80% | -2.76% | 98% | 103%
Class A2 | 0.13% | -7.17% | -8.05% | 98% | 102%
Class B | 0.07% | -9.61% | -7.01% | 98% | 98%
Class C | 0.08% | -3.20% | -2.77% | 100% | 98%
Class E | 0.13% | -9.35% | -2.79% | 98% | 98%
Overall | 0.10% | -6.60% | -4.83% | 98% | 99%
Class D | 0.07% | -2.72% | -2.09% | 106% | 102%
Class F | 0.14% | -5.81% | -6.21% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.12% | -4.37% | -3.59% | 100% | 107%
Class A2 | 0.24% | -9.11% | -14.21% | 101% | 107%
Class B | 0.18% | -15.93% | -11.52% | 101% | 104%
Class C | 0.09% | -3.74% | -3.07% | 101% | 98%
Class E |  |  |  |  | 
Overall | 0.16% | -9.00% | -8.22% | 101% | 103%
Class D | 0.14% | -4.70% | -3.68% | 100% | 95%
Class F | 0.17% | -4.00% | -3.88% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.17% | -17.58% | -14.83% | 96% | 98%
Class C | 0.09% | -3.68% | -3.16% | 96% | 100%
Class E | 0.14% | -13.71% | -4.03% | 98% | 97%
Overall | 0.13% | -11.98% | -8.24% | 96% | 99%
Class D | 0.13% | -5.65% | -3.80% | 97% | 100%
Class F | 0.04% | -6.96% | -4.99% | 94% | 92%
All Intra Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.10% | -2.96% | -3.14% | 100% | 104%
0.13% | -7.52% | -8.30% | 98% | 104%
0.08% | -9.81% | -7.56% | 100% | 101%
0.08% | -3.29% | -2.83% | 100% | 99%
0.14% | -9.80% | -3.26% | 100% | 102%
0.10% | -6.84% | -5.18% | 100% | 102%
0.08% | -2.72% | -2.07% | 100% | 97%
0.15% | -5.98% | -6.21% | 100% | 99%
Random Access Main 10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.12% | -4.88% | -4.64% | 100% | 106%
0.26% | -9.88% | -14.72% | 99% | 105%
0.21% | -16.74% | -12.99% | 100% | 103%
0.09% | -4.15% | -3.37% | 101% | 100%
0.17% | -9.64% | -9.10% | 100% | 103%
0.12% | -4.70% | -3.77% | 100% | 95%
0.20% | -4.16% | -4.05% | 101% | 101%
Low delay B Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.17% | -19.04% | -17.39% | 98% | 105%
0.09% | -5.47% | -4.26% | 97% | 101%
0.14% | -15.85% | -4.55% | 99% | 102%
0.14% | -13.72% | -9.80% | 98% | 103%
0.13% | -6.25% | -3.99% | 96% | 99%
0.27% | -7.73% | -5.98% | 99% | 103%
All Intra Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.11% | -3.09% | -3.43% | 110% | 110%
0.13% | -7.76% | -8.40% | 98% | 101%
0.08% | -10.18% | -7.75% | 100% | 98%
0.09% | -3.59% | -3.34% | 108% | 102%
0.15% | -10.22% | -3.30% | 97% | 94%
0.11% | -7.13% | -5.42% | 102% | 100%
0.08% | -2.77% | -2.63% | 98% | 94%
0.15% | -5.99% | -6.31% | 102% | 101%
Random Access Main 10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.12% | -4.87% | -4.73% | 100% | 106%
0.24% | -10.08% | -14.94% | 100% | 106%
0.19% | -16.81% | -13.46% | 100% | 103%
0.09% | -4.33% | -3.67% | 100% | 98%
0.16% | -9.75% | -9.40% | 100% | 103%
0.07% | -4.63% | -3.74% | 99% | 95%
0.20% | -4.27% | -4.17% | 100% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.19% | -19.33% | -17.45% | 101% | 109%
0.14% | -5.44% | -4.45% | 95% | 99%
0.15% | -16.13% | -5.20% | 98% | 100%
0.16% | -13.90% | -10.05% | 98% | 103%
0.11% | -6.38% | -3.90% | 95% | 98%
0.21% | -7.91% | -6.68% | 98% | 104%

## Slide 5
Simulation results (without gain shift)
# of coefficients | ratio of multiplications w.r.t CE5-2.1 | ratio of additions w.r.t CE5-2.1 | ratio of gain w.r.t CE5-2.1 | Observations
6 | 43% | 33% | 83% | best gain-complexity trade-off. removes all necessary process of horizontal virtual boundary handling
7 | 50% | 44% | 90% | very similar coding performance with setting of 8 coefficients with more reduction of complexity
8 | 57% | 44% | 92% | retains most of gain
(CE5-2.1 without gain shift) RA: 0.16%, -10.69%, -10.17%
(CE5-2.1+ 6 coefficients without gain shift): RA: 0.16%, -9.00%, -8.22%
(CE5-2.1+ 7 coefficients without gain shift): RA: 0.17%, -9.64%, -9.10%
(CE5-2.1+ 8 coefficients without gain shift): RA: 0.16%, -9.75%, -9.40%

## Slide 6
Proposal
The second part of this proposal proposes to reduce on-chip buffer by adding a clipping process to refinement value.
The clipping value is signaled in PPS with default clipping range as [-16, 15] (the default clipping range is also the maximum allowed range).
Illustration of CCALF refinement:
pBSampleC = pBSampleC + Clip(R);
By adding a clipping process, the on-chip buffer needed to store R (for parallel processing) is reduced from 16 bits per sample (16,384 bytes per CTU) to 5 bits per sample (5120 bytes per CTU).

## Slide 7
Simulation results (without gain shift)
Proposal of clipping
(implemented on top of CE5-2.1)
 |  | All Intra Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.13% | -3.49% | -4.16% | 105% | 103%
0.13% | -8.67% | -8.93% | 103% | 104%
0.10% | -10.56% | -8.57% | 102% | 102%
0.13% | -4.18% | -3.91% | 102% | 101%
0.19% | -10.16% | -3.46% | 103% | 103%
0.13% | -7.58% | -6.01% | 103% | 103%
0.11% | -2.74% | -3.28% | 101% | 103%
0.18% | -6.58% | -6.64% | 102% | 102%
 |  | Random access Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.13% | -5.65% | -5.34% | 100% | 99%
0.21% | -11.72% | -15.74% | 100% | 101%
0.21% | -17.63% | -14.08% | 102% | 100%
0.09% | -5.03% | -4.35% | 103% | 100%
0.16% | -10.69% | -10.07% | 101% | 100%
0.11% | -4.45% | -4.46% | 100% | 100%
0.18% | -4.73% | -4.61% | 102% | 98%
 |  | Low delay B Main10 |  | 
 |  | Over VTM-6.0 |  | 
Y | U | V | EncT | DecT
0.18% | -21.52% | -19.23% | 102% | 100%
0.12% | -8.18% | -6.44% | 101% | 100%
0.24% | -15.69% | -6.37% | 100% | 97%
0.17% | -15.62% | -11.75% | 101% | 99%
0.18% | -8.10% | -6.04% | 103% | 102%
0.13% | -10.52% | -7.54% | 104% | 100%
CE5-2.1
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.13% | -3.49% | -4.07% | 105% | 105%
Class A2 | 0.11% | -8.45% | -8.83% | 104% | 105%
Class B | 0.10% | -10.36% | -8.36% | 104% | 103%
Class C | 0.13% | -4.18% | -3.90% | 100% | 101%
Class E | 0.19% | -10.03% | -3.45% | 102% | 104%
Overall | 0.13% | -7.47% | -5.92% | 103% | 103%
Class D | 0.12% | -2.68% | -3.25% | 102% | 104%
Class F | 0.17% | -5.73% | -5.97% | 101% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.12% | -5.66% | -5.26% | 103% | 102%
Class A2 | 0.20% | -11.45% | -15.47% | 102% | 103%
Class B | 0.22% | -17.44% | -13.97% | 101% | 104%
Class C | 0.08% | -5.01% | -4.25% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.16% | -10.57% | -9.93% | 101% | 102%
Class D | 0.12% | -4.46% | -4.46% | 102% | 101%
Class F | 0.20% | -4.73% | -4.55% | 102% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.18% | -21.36% | -18.88% | 101% | 107%
Class C | 0.12% | -8.30% | -6.67% | 101% | 102%
Class E | 0.02% | -16.23% | -6.51% | 104% | 101%
Overall | 0.12% | -15.72% | -11.72% | 102% | 104%
Class D | 0.23% | -7.88% | -6.36% | 102% | 108%
Class F | 0.20% | -10.65% | -7.65% | 102% | 100%

## Slide 8
8
Conclusion
This contribution proposes 2 modifications for CCALF
Use reduced filter shape (6, 7, 8 coefficients) to save CCALF complexity to 43%, 50%, 57% (multiplications) respectively with most gain retained.
Use clipping process to reduce on chip memory to 31% with negligible impact on coding performance.

## Slide 9
9
Thank Bytedance for cross-check

## Slide 10
Additional Simulation results (with gain shift)
number of coefficients = 6
number of coefficients = 7
number of coefficients = 8
CE5-2.1
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.19% | 5.37% | 3.75% | 102% | 102%
Class A2 | -2.04% | -0.29% | -0.74% | 100% | 101%
Class B | -0.74% | -1.74% | 0.92% | 101% | 101%
Class C | -0.76% | 3.98% | 4.51% | 99% | 101%
Class E | -0.46% | -2.81% | 4.71% | 101% | 99%
Overall | -0.99% | 0.78% | 2.54% | 101% | 101%
Class D | -0.75% | 5.36% | 4.85% | 100% | 102%
Class F | -0.73% | -1.03% | -1.29% | 100% | 98%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.82% | 5.25% | 4.13% | 99% | 101%
Class A2 | -2.05% | -1.14% | -6.18% | 97% | 102%
Class B | -0.54% | -6.34% | -2.25% | 100% | 99%
Class C | -0.78% | 5.75% | 6.57% | 101% | 97%
Class E |  |  |  |  | 
Overall | -1.16% | 0.24% | 0.59% | 99% | 100%
Class D | -0.64% | 6.08% | 6.42% | 98% | 97%
Class F | -0.92% | 1.86% | 2.34% | 100% | 97%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.54% | -9.26% | -6.60% | 102% | 101%
Class C | -0.73% | 3.86% | 5.44% | 100% | 99%
Class E | -0.24% | -5.62% | 7.60% | 102% | 98%
Overall | -0.53% | -3.98% | 0.96% | 101% | 100%
Class D | -0.56% | 4.90% | 7.37% | 105% | 104%
Class F | -0.84% | -2.82% | -0.28% | 104% | 101%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.22% | 6.10% | 5.31% | 96% | 102%
Class A2 | -2.03% | 1.48% | 0.26% | 95% | 101%
Class B | -0.77% | -0.56% | 2.73% | 98% | 99%
Class C | -0.81% | 5.03% | 5.80% | 98% | 97%
Class E | -0.52% | -1.81% | 5.49% | 103% | 104%
Overall | -1.02% | 1.92% | 3.89% | 98% | 100%
Class D | -0.81% | 5.56% | 6.29% | 95% | 92%
Class F | -0.77% | -0.16% | -0.85% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.87% | 6.89% | 6.19% | 98% | 104%
Class A2 | -2.04% | 1.74% | -4.37% | 96% | 103%
Class B | -0.55% | -4.40% | 0.83% | 98% | 101%
Class C | -0.80% | 7.25% | 8.07% | 99% | 96%
Class E |  |  |  |  | 
Overall | -1.18% | 2.19% | 2.79% | 98% | 101%
Class D | -0.64% | 6.21% | 7.39% | 99% | 95%
Class F | -0.98% | 2.69% | 2.97% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.55% | -4.39% | -1.22% | 101% | 103%
Class C | -0.81% | 9.47% | 9.92% | 101% | 99%
Class E | -0.22% | -3.03% | 10.08% | 102% | 101%
Overall | -0.55% | 0.57% | 5.31% | 101% | 101%
Class D | -0.59% | 8.04% | 9.66% | 101% | 100%
Class F | -0.97% | 0.77% | 2.43% | 101% | 98%
All Intra Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-1.21% | 5.96% | 4.82% | 100% | 106%
-2.03% | 1.11% | -0.02% | 99% | 105%
-0.77% | -0.76% | 2.12% | 100% | 101%
-0.81% | 4.95% | 5.73% | 99% | 98%
-0.51% | -2.31% | 5.04% | 103% | 104%
-1.02% | 1.68% | 3.51% | 100% | 102%
-0.80% | 5.60% | 6.29% | 100% | 96%
-0.76% | -0.37% | -0.98% | 101% | 100%
Random Access Main 10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-1.85% | 6.21% | 5.23% | 100% | 107%
-2.02% | 0.79% | -4.95% | 96% | 104%
-0.53% | -5.29% | -0.97% | 99% | 103%
-0.82% | 6.68% | 7.70% | 99% | 97%
-1.17% | 1.42% | 1.79% | 99% | 103%
-0.67% | 5.98% | 7.60% | 100% | 96%
-0.95% | 2.54% | 2.85% | 99% | 99%
Low delay B Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.53% | -6.10% | -4.14% | 101% | 104%
-0.74% | 7.53% | 8.80% | 101% | 100%
-0.12% | -5.17% | 9.28% | 102% | 101%
-0.50% | -1.32% | 3.53% | 101% | 102%
-0.51% | 6.87% | 9.30% | 101% | 101%
-0.90% | 0.07% | 1.95% | 101% | 100%
All Intra Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-1.21% | 5.82% | 4.54% | 104% | 108%
-2.03% | 0.82% | -0.14% | 108% | 112%
-0.76% | -1.27% | 1.90% | 110% | 108%
-0.80% | 4.63% | 5.17% | 95% | 89%
-0.50% | -2.80% | 4.99% | 97% | 95%
-1.01% | 1.32% | 3.24% | 103% | 102%
-0.79% | 5.46% | 5.66% | 95% | 88%
-0.75% | -0.44% | -1.09% | 101% | 99%
Random Access Main 10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-1.84% | 6.05% | 4.89% | 99% | 106%
-2.03% | 0.65% | -5.13% | 97% | 104%
-0.54% | -5.37% | -1.39% | 99% | 102%
-0.78% | 6.62% | 7.49% | 97% | 94%
-1.16% | 1.31% | 1.49% | 98% | 101%
-0.68% | 6.31% | 7.50% | 99% | 95%
-0.96% | 2.40% | 2.68% | 100% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.51% | -6.32% | -4.62% | 101% | 103%
-0.80% | 7.60% | 8.53% | 101% | 100%
-0.29% | -4.88% | 8.79% | 103% | 101%
-0.55% | -1.32% | 3.12% | 102% | 102%
-0.58% | 6.67% | 9.82% | 101% | 101%
-0.93% | -0.33% | 1.41% | 102% | 99%

## Slide 11
Simulation results (with gain shift)
(CE5-2.1+ with gain shift): RA: -1.16%, 0.24%, 0.59%
Test a1 (CE5-2.1+ 6 coefficients with gain shift): RA: -1.18%, 2.19%, 2.79%
Test a2 (CE5-2.1+ 7 coefficients with gain shift): RA: -1.17%, 1.42%, 1.79%
Test a3 (CE5-2.1+ 8 coefficients with gain shift): RA: -1.16%, 1.31%, 1.49%