## Slide 1
Non-CE3: On Constraint of CCLM with CST
Che-Wei Kuo, Jingya Li, Chong Soon Lim, Abe Kiyofumi

## Slide 2: Introduction
CCLM may have latency issue when CST is on
  Luma VPDU is BT_H split but chroma VPDU is BT_V split
  The worst case latency is 64x64 luma reconstruction samples
O1124 was adopted to solve the latency issue
  Limit the latency within 32x32 luma reconstruction samples
  CCLM can only be enabled when
Luma VPDU | Chroma VPDU
No split && Not ISP | No split QT BT_H (no further split or followed by BT_V)
QT | No split QT BT_H (no further split or followed by BT_V)

## Slide 3: Problem Statement
For luma NoSplit with chroma QT case, luma subpart processing is required to achieve 32x32 latency
all intra mode (normal)
all intra mode (subpart)
all intra mode
subpart prediction
IQ/IT
all intra mode
subpart prediction
luma end
subpart
reconstruction
luma end
subpart
reconstruction
IQ/IT
all intra mode
prediction
luma end
reconstruction
This engine needs to support all intra predictions
Luma VPDU
Chroma VPDU

## Slide 4: Problem Statement
Angular, DC, planar, and PDPC
  Special handling for luma subpart prediction and residue addition
  Can not simply reuse luma QT case (different reference samples)
MIP
  Need subpart matrix multiplication
  Need subpart Interpolation process. Note the prediction samples for interpolation may across the subpart boundary.
IBC
  Not a problem since luma block copy can be performed in subpart
ISP
  CCLM is not allowed in luma no split case.

## Slide 5: Proposed Method
Disallow luma no split with chroma split case, to reduce hardware complexity for supporting luma subpart processing
The ISP constraint can also be removed (single tree case)
Luma VPDU | Chroma VPDU
No split && Not ISP | No split QT BT_H (no further split or followed by BT_V)
QT | No split QT BT_H (no further split or followed by BT_V)

## Slide 6: Simulation Results
Luma blocks are usually smaller than chroma blocks, the complexity for luma subpart processing is not a good trade-off.
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.31% | 0.11% | 94% | 94%
Class A2 | 0.02% | 0.27% | 0.31% | 93% | 93%
Class B | 0.01% | 0.08% | 0.00% | 100% | 99%
Class C | 0.00% | -0.01% | 0.02% | 99% | 99%
Class E | 0.00% | 0.02% | 0.00% | 101% | 101%
Overall | 0.00% | 0.12% | 0.07% | 98% | 97%
Class D | 0.00% | 0.02% | 0.01% | 98% | 99%
Class F | 0.01% | 0.05% | 0.07% | 97% | 96%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.06% | 0.10% | 102% | 95%
Class A2 | 0.03% | 0.12% | 0.13% | 104% | 100%
Class B | 0.02% | 0.20% | 0.01% | 102% | 97%
Class C | -0.02% | 0.00% | 0.07% | 102% | 97%
Class E |  |  |  |  | 
Overall | 0.01% | 0.08% | 0.07% | 102% | 97%
Class D | 0.00% | 0.00% | 0.00% | 100% | 98%
Class F | -0.02% | -0.06% | -0.04% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.04% | -0.02% | 95% | 95%
Class C | 0.00% | 0.02% | 0.05% | 98% | 98%
Class E | -0.06% | -0.29% | 0.60% | 98% | 98%
Overall | -0.02% | -0.05% | 0.16% | 97% | 97%
Class D | 0.00% | 0.00% | 0.00% | 98% | 98%
Class F | -0.01% | 0.43% | 0.69% | 96% | 97%

## Slide 7: Conclusion
Luma subpart processing is required for all intra prediction
  To achieve 32x32 latency
  To support luma no split with chroma QT case
Propose to disallow CCLM when luma no split with chroma split case, to reduce hardware complexity

## Slide 8: Acknowledgment
Thanks Alibaba for cross-checking