## Slide 1: JVET-P0276 Non-CE6: On Supporting 64x64Chroma Transform Unit with Composite VPDU
Fujitsu
16th JVET meeting, Geneva , 2019/10/1-11
Notes: p0.
それではよろしくお願いします。
活動報告と題しまして江崎が発表します。

## Slide 2: Introduction
In VTM6.0, VPDU is defined as non-overlapping 64x64 luma samples and 32x32 chroma samples for 4:2:0 format. Data are coded/processed in VPDU order successively so that maximum chroma TU size is 32x32.
The motivation of VPDU is to keep buffer size small in hardware decoder. The VPDU size is roughly proportional to the buffer size in most pipeline stages.
However, the concept of VPDU in VTM6.0 limits maximum chroma TU size.
This contribution presents a composite VPDU to make maximum chroma TB size be 64x64 without increase of buffer size in hardware decoder.

## Slide 3: Proposed method(1/3)
For dual-tree partitioning in I slice, when cbSize in luma is 128x128,
  use a flag named split_chroma_cu_flag to indicate whether a 64x64 chroma block is split into 4 32x32 blocks or not.
    CCLM is disabled for 64x64 chroma block.
  If split_chroma_cu_flag is 0, chroma CU and TU size is 64x64.
  128x128 luma CB is still implicitly split into 4 64x64 blocks.
  CCLM is not supported for 64x64 chroma CU in order to not introduce additional buffer.

## Slide 4: Proposed method(2/3)
For single tree partitioning in P and B slices,
  If CU is larger or equal to 128x128,chroma TU size is 64x64.
  If CU size equals to 128x64,chroma TU size is 64x32.
  If CU size equals to 64x128,chroma TU size is 32x64.
  Otherwise, maximum transform TB for luma is 64x64; maximum chroma TU size is 32x32.

## Slide 5: Proposed method(3/3)
Data processing order
  Dual tree case
  Single tree case

## Slide 6: Concerns on VPDU(1/2)
There was concern on breaking the 64x64 VPDU concept if introducing 64x64 chroma TU in Gothenburg meeting.
Classic pipeline processing timing of video decoder in VTM6.0 as below. T0 is time to process a VPDU including 64x64 luma and 2x32x32 chroma samples.
Y0
Y1
Y2
Y3
C0
C1
C2
C3
Luma CTU
Chroma CTU
Latency:
T0

## Slide 7: Concerns on VPDU(2/2)
Break happens in classic pipeline processing timing if introducing 64x64 chroma TU.
  Reason: The buffer for Y2 is same as that for Y0. Break is to avoid buffer read/write conflict.

## Slide 8: Composite VPDU(1/3)
If adjusting the latency of each pipeline stage from T0 to T1(time to process 64x64 samples, T0=1.5xT1), break is avoided.
There are several VPDU types. Examples are,
  TYPE 0: maximum chroma size is 32x32 as in VTM6.0
  TYPE 1: chroma TU size is 64x64
Latency:
T1

## Slide 9: Composite VPDU(2/3)
  TPYE 2
    corresponding to 128x64 inter CU in above or 64x128 inter CU in left part
    the other part is normal case (chroma TU less or equal to 32x32).
64x128
CU
128x64
CU
normal case:
further split
into CUs

## Slide 10: Composite VPDU(3/3)
  TYPE 3
    corresponding to 128x64 inter CU in bottom and 64x128 inter CU in right part
    the other part is normal case (chroma TU less or equal to 32x32).
64x128
CU
normal case:
further split
into CUs
128x64
CU

## Slide 11: Hardware for Composite VPDU
No additional buffer.
  For VPDU type 1, 64x64 luma block and chroma block share internal buffer.
  For other VPDU types, same as that in VTM6.0.
  CCLM is not supported for 64x64 chroma CU.
No additional transform core.
  Transform hardware is shared between luma and chroma for 64x64 TU.

## Slide 12: Simulation Results
Test condition on top of VTM6.0:
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.32% | -0.32% | 106% | 99%
Class A2 | -0.01% | -0.20% | -0.19% | 104% | 98%
Class B | 0.00% | -0.19% | -0.27% | 102% | 99%
Class C | 0.01% | -0.07% | 0.00% | 106% | 99%
Class E | -0.05% | -0.29% | -0.75% | 113% | 99%
Overall | -0.01% | -0.20% | -0.29% | 106% | 99%
Class D | 0.01% | 0.03% | 0.04% | 112% | 98%
Class F | -0.03% | -0.25% | -0.30% | 107% | 98%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.47% | -0.59% | 103% | 101%
Class A2 | 0.02% | -0.13% | -0.10% | 104% | 98%
Class B | -0.01% | -0.18% | -0.20% | 101% | 101%
Class C | 0.01% | 0.04% | -0.08% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.17% | -0.22% | 102% | 100%
Class D | -0.01% | -0.02% | -0.18% | 92% | 100%
Class F | -0.02% | -0.41% | 0.08% | 102% | 101%

## Slide 13: Conclusion
The maximum transform unit size of chroma components up to 64x64 is supported by introducing composite VPDU concept.
Gain is obtained in chroma components.
No hardware increase on buffer and transform core.
Suggest to adopt this proposal.
Thank InterDigital for crosschecking.

## Slide 14
Notes: 以上で発表を終わります。
ご清聴ありがとうございました。