## Slide 1: JVET-P0300 – High throughput CABAC mode for VVC
Motivated by two proposals (from the previous JVET meeting):
JVET-O0308: CABAC skip mode
  Write bins into the bit stream without arithmetic coding
JVET-O0554: Generalized bypass (GB) mode
  Coding interval subdivision by bit-shift instead of multiplication
  No context model update
  Applied to selected context models only
Proposed: Use generalized bypass for all regular bins to achieve a high throughput mode

## Slide 2: Proposed method compared to VTM 6.0: Variables per context model
VTM-6.0:
  pStateIdx0: 10 bit, RAM, updated every regular bin pStateIdx1: 14 bit, RAM, updated every regular bin shiftIdx: 4 bit, ROM
  28 bit in total
Proposed high throughput mode:
  valMpsGB: 1 bit, RAM, set once during context initialization pShiftGB: 2 bit, RAM, set once during context initialization
  3 bit in total

## Slide 3: Proposed method compared to VTM 6.0: Coding interval subdivision (done for each regular bin)
VTM-6.0:
qRangeIdx = ivlCurrRange >> 5 pState = pStateIdx1 + 16 * pStateIdx0 valMps = pState >> 14 ivlLpsRange = ( qRangeIdx * ( (valMps ? 32767 − pState : pState )>>9 )>>1 ) + 4
Proposed high throughput mode:
ivlLpsRange = ivlCurrRange >> ( pShiftGB + 1 )

## Slide 4: Proposed method compared to VTM 6.0: Context model update (done for each regular bin)
VTM-6.0:
pStateIdx0 = pStateIdx0  (pStateIdx0 >> shift0) + (1023 * binVal >> shift0) pStateIdx1 = pStateIdx1  (pStateIdx1 >> shift1) + (16383 * binVal >> shift1)
Proposed high throughput mode:
No update.

## Slide 5: Proposed method compared to VTM 6.0: Context initialization
VTM-6.0:
pStateIdx0 = preCtxState << 3 pStateIdx1 = preCtxState << 7
Proposed high throughput mode:
valMpsGB = preCtxState >> 6 pLps = valMpsGB ? 128 - preCtxState : preCtxState logShift = Floor ( Log2( pLps + ( pLps >> 2 ) ) ) pShiftGB = Min( numGB, 6 – logShift )
Parameter numGB controls the maximum allowed shift. Proposed: numGB = 3
The proposed method uses the same set of context init values as VTM-6.0!

## Slide 6: Coding efficiency impact of the maximum shift ‘numGB’ Luma-BD-rate over VTM-6.0, QP2-17 (17 frames):
* Retrained context init values (trained jointly for VTM-6.0 and JVET-P0300)
numGB | LPS probabilities | AI | RA | LB | LP
0 | 1/2 | 18.27% | 23.88% | 23.90% | 23.66%
1 | 1/2, 1/4 | 7.67% | 11.85% | 9.92% | 9.44%
2 | 1/2, 1/4, 1/8 | 6.03% | 8.12% | 7.75% | 7.08%
3 | 1/2, 1/4, 1/8, 1/16 | 5.95% | 7.90% | 7.50% | 6.93%
3* | 1/2, 1/4, 1/8, 1/16 | 3.96% | 4.94% | 4.21% | 4.31%
4 | 1/2, 1/4, 1/8, 1/16, 1/32 | 6.05% | 7.97% | 7.60% | 6.99%

## Slide 7: Joint retraining of context init values
Training method: As specified in CE description JVET-N1021
Bitstreams: VTM-6.0 CTC QPs 22 - 37 and QPs 2 - 17 with 100 frames
Two initialization and entropy coding methods:
  VTM-6.0
  Proposed
Resulting ‘normalized rates d()’ according to JVET-N1021 are weighted before calculating init values:
VTM-6.0: 80 % impact
Proposed: 20 % impact

## Slide 8: Test: VTM-6.0 with jointly trained init values Reference: VTM-6.0
QP 2-17 100 fr. | Y | U | V
AI | -0.01% | -0.05% | -0.03%
RA | -0.02% | -0.08% | -0.08%
LB | -0.03% | -0.17% | -0.13%
LP | -0.02% | -0.15% | -0.14%
QP 22-37 | Y | U | V
AI | 0.05% | 0.04% | -0.06%
RA | 0.00% | 0.52% | 0.25%
LB | -0.03% | 0.28% | 0.58%
LP | -0.01% | 0.38% | 0.97%

## Slide 9: Test: VTM-6.0 with init values retrained on VTM-6.0 Reference: VTM-6.0
QP 2-17 100 fr. | Y | U | V
AI | 0.00% | -0.04% | -0.02%
RA | -0.01% | -0.07% | -0.09%
LB | -0.02% | -0.13% | -0.14%
LP | -0.01% | -0.13% | -0.14%
QP 22-37 | Y | U | V
AI | 0.01% | 0.07% | 0.00%
RA | -0.02% | 0.53% | 0.00%
LB | -0.08% | 0.72% | 0.12%
LP | 0.01% | 0.69% | 0.23%

## Slide 10: Test: Proposed, numGB=3, jointly trained init values Reference: VTM-6.0
QP 2-17 100 fr. | Y | U | V | DecT
AI | 3.89% | 3.78% | 4.05% | 89%
RA |  |  |  | 
LB | 4.09% | 3.54% | 3.77% | 89%
LP | 4.23% | 3.74% | 3.66% | 88%
Decoder runtimes should be accurate (simulated on an isolated computer).

## Slide 11: Test: Proposed, numGB=3, jointly trained init values Reference: VTM-6.0
QP 22-37 | Y | U | V | DecT
AI | 3.68% | 2.84% | 2.86% | 95%
RA | 4.49% | 3.35% | 4.33% | 97%
LB | 3.09% | 0.63% | 0.30% | 97%
LP | 3.15% | 0.50% | 0.20% | 97%
Decoder runtimes should be accurate (simulated on an isolated computer).

## Slide 12: Variant 1: Fixed LPS width coding interval subdivision
ivlCurrRange is initialized with 480 (instead of 510)
Bypass mode is used for pShiftGB = 0
For pShiftGB > 0, coding interval subdivision is changed from
ivlLpsRange = ivlCurrRange >> ( pShiftGB + 1 )
to
ivlLpsRange = 384 >> ( pShiftGB + 1 )
With this setting, ivlLpsRange can be implemented with 6 instead of 9 bit.

## Slide 13: Summary of proposed methods Luma-BD-rate over VTM-6.0, QP2-17
QP | Method | AI | RA | LB | LP
2-17 | P0300 baseline | 3.89% |  | 4.09% | 4.23%
 | P0300 variant 1 | 4.24% |  | 4.55% | 4.70%
22-37 | P0300 baseline | 3.68% | 4.49% | 3.09% | 3.15%
 | P0300 variant 1 | 4.10% | 4.85% |  | 3.72%