## Slide 1
AHG17: External reference picture
JVET-P0326
P. Bordes, D. Doyen, F. Galpin, M. Kerdranvat

## Slide 2: Motivation JVET_P0326
One picture of current layer may be predicted with a reconstructed picture decoded from another layer coded with another standard
  e.g. layer-1 is VVC encoded and layer-0 is HEVC or AVC encoded
  In SHVC, base layer (layer-0) only can be coded with another standard, and the other layers are coded with SHVC
Use of one additional reference picture generated with application-based modules
  e.g. “virtual reference” frame computed with deep-learning based frame rate-up conversion algorithm
Current (RPLS) specification allows duplicating one reference picture with different weighted prediction parameters to manage local illumination compensation or for increasing motion precision
  This principle could be extended with more elaborated illumination change models

## Slide 3: Motivation (cont.) JVET_P0326
(JVET-P0114) external decoding refresh (EDR) pictures
  e.g. stream-switching feature
In multi-view coding, one view can be a good predictor for another one. Several models exist (e.g. depth-based…)
  To predict one view from another one, there is a need to have a way to signal that one view in the DPB has been generated with external means to be used as a predictor

## Slide 4: Proposal-1 “external reference picture” JVET_P0326
sps_enabled_external_ref_pic_flag equal to 0 specifies that no external reference pictures is used for inter prediction of any coded picture in the CVS. sps_enabled_external_ref_pic_flag equal to 1 specifies that external reference pictures may be used for inter prediction of one or more coded pictures in the CVS.
external_ref_pic_flag[ listIdx ][ rplsIdx ][ i ] equal to 1 specifies that the i-th entry in the ref_pic_list_struct( listIdx, rplsIdx ) syntax structure is provided by an external means not specified in this Specification. external_ref_pic_flag[ listIdx ][ rplsIdx ][ i ] equal to 0 specifies that the i-th entry in the ref_pic_list_struct( listIdx, rplsIdx ) syntax structure is a reconstructed picture specified by this Specification.
When external_ref_pic_flag[ listIdx ][ rplsIdx ][ i ] is not present, it is inferred to be equal to 0.

## Slide 5: Proposal-2 “reference with/without motion info” JVET_P0326
Signal that the one reference (can be ILRP) has no motion-info
  To avoid the burden of copying motion vectors, ref-idx, etc… in-between codecs/layers
  Or because the reference is external and motion-info is not available
  Or because using default motion-info values is good enough
zero_mv_ref_flag[ listIdx ][ rplsIdx ][ i ] equal to 1 specifies that the i-th entry in the ref_pic_list_struct( listIdx, rplsIdx ) syntax structure has collocated motion vectors equal to default. zero_mv_ref_flag[ listIdx ][ rplsIdx ][ i ] equal to 0 specifies that the i-th entry in the ref_pic_list_struct( listIdx, rplsIdx ) syntax structure has collocated motion vectors that may be not equal to default.
CONFORMANCE NOTE: it is a requirement that the values of the reconstructed motion vectors are equal to zero when the reference is ILRP and has zero_mv_ref_flag equal to 1.

## Slide 6: Proposal-2 “reference with/without motion info” JVET_P0326
Multi-view example (TMVP)
  Current is view-A
  Another view-B is external reference
  Motion-info contains 2D inter-view disparity DAB
  pocCol = pocRef = pocCur