## Slide 1: AHG 17: On constant slice header parameter set in PPS
Biao Wang, Anand Meher Kotra, Semih Esenlik, Han Gao, Jianle Chen

## Slide 2
A syntax element in Constant slice header Parameter Set in PPS (Left) indicates its corresponding Syntax element (Right) value in slice header is a constant value for all slices referring to this PPS
Advantage: saving bits by avoiding signalling duplicated value in slice header
Applicable scenario: these parameters in slice header are the same for all slices referring to a same PPS
constant slice header parameter set in PPS | Corresponding Syntax Element in Slice header
pps_dep_quant_enabled_idc | dep_quant_enabled_flag
pps_ref_pic_list_sps_idc[ i ] | ref_pic_list_sps_flag[ i ]
pps_temporal_mvp_enabled_idc | slice_temporal_mvp_enabled_flag
pps_mvd_l1_zero_idc | mvd_l1_zero_flag
pps_collocated_from_l0_idc | collocated_from_l0_flag
pps_six_minus_max_num_merge_cand_plus1 | six_minus_max_num_merge_cand
pps_five_minus_max_num_subblock_merge_cand_plus1 | five_minus_max_num_subblock_merge_cand
pps_max_num_merge_cand_minus_max_num_triangle_cand_minus1 | max_num_merge_cand_minus_max_num_triangle_cand
Background

## Slide 3: Modification 1: Extension of constant parameters
It is asserted that for a real-world encoder, the highlighted syntax elements are constant during encoding.
Advantage: saving more bits by avoiding signalling more duplicated value in slice header
constant_slice_header_params_enabled_flag | u(1)
if( constant_slice_header_params_enabled_flag ) { | 
pps_dep_quant_enabled_idc | u(2)
for( i = 0; i < 2; i++ ) | 
pps_ref_pic_list_sps_idc[ i ] | u(2)
pps_temporal_mvp_enabled_idc | u(2)
pps_mvd_l1_zero_idc | u(2)
pps_collocated_from_l0_idc | u(2)
pps_six_minus_max_num_merge_cand_plus1 | ue(v)
pps_five_minus_max_num_subblock_merge_cand_plus1 | ue(v)
pps_max_num_merge_cand_minus_max_num_triangle_cand_minus1 | ue(v)
pps_six_minus_max_num_ibc_merge_cand_plus1 | ue(v)
pps_fpel_mmvd_enabled_idc | u(2)
pps_joint_cbcr_sign_idc | u(2)
pps_sao_luma_idc | u(2)
pps_sao_chroma_idc | u(2)
pps_alf_enabled_idc | u(2)
pps_alf_chroma_idc | u(3)
pps_lmcs_enabled_idc | u(2)
pps_chroma_residual_scale_idc | u(2)
pps_cabac_init_idc | u(2)
pps_sign_data_hiding_enabled_idc | u(2)
pps_disable_bdof_dmvr_idc | u(2)
log2_transform_skip_max_size_minus2 | ue(v)
} | 

## Slide 4
When slices of a same picture have different content, they might require different coding parameters. Proposal allows signalling multiple default coding parameters for different parts (e.g. tiles, sub-pictures) of the picture.
Advantage: bitrate saving for the case of mixed content.
1~7 parameter sets per PPS are allowed
pic_parameter_set_rbsp( ) { | Descriptor
… | 
num_constant_slice_header_params | u(3)
constant_slice_header_params_enabled_flag | 
if( constant_slice_header_params_enabled_flag ) | 
for( k=0;k< num_constant_slice_header_params;k++ ) { | 
pps_sub_pic_id[ k ] | 
log2_transform_skip_max_size_minus2[ k ] | ue(v)
pps_dep_quant_enabled_idc[ k ] | u(2)
for( i = 0; i < 2; i++ ) | 
pps_ref_pic_list_sps_idc[ i ] [ k ] | u(2)
pps_temporal_mvp_enabled_idc[ k ] | u(2)
pps_mvd_l1_zero_idc[ k ] | u(2)
pps_collocated_from_l0_idc[ k ] | u(2)
pps_six_minus_max_num_merge_cand_plus1[ k ] | ue(v)
pps_five_minus_max_num_subblock_merge_cand_plus1[ k ] | ue(v)
pps_max_num_merge_cand_minus_max_num_triangle_cand_minus1[ k ] | ue(v)
} | 
Modification 2: multiple constant parameter sets (I)

## Slide 5
Using the signaled slice_sub_picture_id as the key in slice header to index the parameter set id k
parameter_set_id is a function used to get the parameter set K, pseudo code is follows:
slice_header( ) { | Descriptor
slice_pic_parameter_set_id | ue(v)
if( rect_slice_flag ¦ ¦ NumBricksInPic > 1 ) | 
slice_address | u(v)
if( !rect_slice_flag && !single_brick_per_slice_flag ) | 
num_bricks_in_slice_minus1 | ue(v)
non_reference_picture_flag | u(1)
slice_type | ue(v)
slice_sub_picture_id | 
k = parameter_set_id (slice_sub_picture_id, pps_sub_pic_id) | 
… | 
for( i = 0; i < 2; i++ ) { | 
if( num_ref_pic_lists_in_sps[ i ] > 0 && (!pps_ref_pic_list_sps_idc[ i ][k]) && ( i = = 0 ¦ ¦ ( i = = 1 && rpl1_idx_present_flag ) ) ) | 
ref_pic_list_sps_flag[ i ] | u(1)
… | 
Modification 2: multiple constant parameter sets (II)

## Slide 6
When slice_override_constant_params_flag is equal to 0 (signalled or inferred), the coding parameters are overridden in the slice header.
Benefit: Coding parameters can be changed for a small set of slices while remaining slices use default parameters.
slice_header( ) { | Descriptor
slice_pic_parameter_set_id | ue(v)
if( rect_slice_flag ¦ ¦ NumBricksInPic > 1 ) | 
slice_address | u(v)
if( !rect_slice_flag && !single_brick_per_slice_flag ) | 
num_bricks_in_slice_minus1 | ue(v)
non_reference_picture_flag | u(1)
slice_type | ue(v)
slice_override_constant_params_flag | ue(v)
k = slice_override_constant_params_flag | 
… | 
for( i = 0; i < 2; i++ ) { | 
if( num_ref_pic_lists_in_sps[ i ] > 0 && (k==1 ?1:!pps_ref_pic_list_sps_idc[ i ]) && ( i = = 0 ¦ ¦ ( i = = 1 && rpl1_idx_present_flag ) ) ) | 
ref_pic_list_sps_flag[ i ] | u(1)
… | 
Modification 3: overriding slice header parameters

## Slide 7
The coding parameters corresponding to screen content are expected to be different from natural content, especially tools like DMVR, BDOF, IBC, Transform skip, MMVD, in-loop filtering etc.
Page 7
Sub-picture/tile/slice with screen content
Sub-picture/tile/slice with natural content
Scenario for multi-set of constant parameters (I)

## Slide 8
When merging two (or more) sub-picture bitstreams with different constant parameter sets:
Recomposed picture
PPS 1 with
Constant
parameter
Set 1
PPS 2: with
Constant
parameter
Set 2
sub-picture 1
sub-picture 2
sub-picture 1
sub-picture 2
PPS 3
Constant
parameter
Set 2
Constant
parameter
Set 1
With VVC 6 design: have to rewrite all parameters in all slice headers for recomposed picture, as a single constant parameter set cannot apply for all slices
With proposed: don’t need to touch the slice header. In PPS 3, the mapping between parameter set and subpicture ID could be built.
Scenario for multi-set of constant parameters (II)

## Slide 9
Proposed modifications:
Include more syntax elements in constant parameter set
Multiple sets of constant parameters
Allow overriding constant parameter at slice level.
It is suggested to adopt the proposed modifications to the next version of VVC draft.
Summary && Conclusions