## Slide 1
JVET-P0347: AhG17: Comments on maximum MTT hierarchy depth and MinCbSize
T.Poirier, F. Le Léannec, F. Urban, F. Galpin

## Slide 2: Maximum MTT hierarchy depth (Inter_slice, intra_slice_luma and intra_slice_chroma)
The value of sps_max_mtt_hierarchy_depth shall be in the range of 0 to CtbLog2SizeY − MinCbLog2SizeY, inclusive.
But using only BT splits, 2*(CtbLog2SizeY − MinCbLog2SizeY) splits are required if you want to reach the minimum size
In CTC, CtbSize is equal to 128 and MinCbSizeY is equal to 4, thus max_mtt_hierarchy_depth shall be in the range 0 to 5.

## Slide 3: Maximum MTT hierarchy depth Subhead goes here
In other conditions, where CtbSize is equal to 32, MinCbSizeY is equal to 8, max_mtt_hierarchy_depth shall be in the range 0 to 2.
Example of CTU split in such a case using TT splits

## Slide 4: MinCbSize Problem statement
Maximum value of log2_min_luma_coding_block_size_minus2 is not defined in VVC Draft 6.

## Slide 5: MinCbSize Problem statement
If CtbSize is equal to 32 and MinCbize is equal to 64, The value of sps_max_mtt_hierarchy_depth shall be in the range of 0 to -1, inclusive.
Another issue is CtbSize of 128, MinCbSize of 128 and qtbt_dual_tree_intra_flag is equal to 1, in this case all CB would be implicitly split into 64x64 blocks.

## Slide 6: JVET-P0347 Proposal
sps_max_mtt_hierarchy_depth_inter_slice specifies the default maximum hierarchy depth for coding units resulting from multi-type tree splitting of a quadtree leaf in slices with slice_type equal to 0 (B) or 1 (P) referring to the SPS. When partition_constraints_override_ flag is equal to 1, the default maximum hierarchy depth can be overridden by slice_max_mtt_hierarchy_depth_luma present in the slice header of the slices referring to the SPS. The value of sps_max_mtt_hierarchy_depth_inter_slice shall be in the range of 0 to 2*(CtbLog2SizeY − MinCbLog2SizeY), inclusive.
log2_min_luma_coding_block_size_minus2 plus 2 specifies the minimum luma coding block size. The value of log2_min_luma_coding_block_size_minus2 shall be in the range of 0 to sps_max_luma_transform_size_64_flag ? 4 : 3, inclusive.