## Slide 1
JVET-P0353
CE1-related: Reference picture resampling filters
2019/10/3

## Slide 2
Proposed down-sample filter
is the cut-off frequency, r is the down-sampling ratio
Follow SHM down-sampling filter design: cosine windowed sinc filter

## Slide 3
Proposed down-sample filter
No change to filter length and precision form MCIF in VVC
For MC with reference picture larger than current picture:
Replace 8-tap MCIF with 8-tap SHM filter
Replace 6-tap MCIF with 6-tap SHM filter
Replace 4-tap MCIF with 4-tap SHM filter
Select from 2 sets of filters depending on resampling ratio
if ratio > 1.75
use 2x SHM filter
else if 1.25 < ratio <= 1.75
use 1.5x SHM filters
else
use existing MCIF
The use of hpel-If is not changed

## Slide 4
Proposed down-sample filter frequency response
Frequency response of 2x filter at phase 0

## Slide 5
Proposed down-sample filter
2x | Low delay Main 10 PSNR1 |  |  |  |  | Low delay B Main10 PSNR2 |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
1-1.1 Lanczos2 | -4.45% | -2.70% | -2,47% | 100% | 100% | -2.89% | -1.79% | -1.72% | 100% | 100%
1-3 SHM | -6.47% | -4.55% | -4.62% | 99% | 102% | -3.98% | -2.67% | -3.00% | 99% | 102%
P0353 |  |  |  |  |  |  |  |  |  | 
1.5x | Low delay Main 10 PSNR1 |  |  |  |  | Low delay B Main10 PSNR2 |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
1-1.1 Lanczos2 | -2.23% | -1.23% | -1.06% | 100% | 102% | -1.85% | -1.68% | -1.34% | 100% | 102%
1-3 SHM | -3.13% | -2.50% | -2.28% | 99% | 101% | -2.23% | -2.21% | -1.87% | 99% | 101%
P0353 |  |  |  |  |  |  |  |  |  |