## Slide 1
JVET-P0370
Non-CE7: Signaling of coded_sub_block_flag
2019/10/3

## Slide 2
Problem statement
In VVC 6, coded_sub_block_flag is always context coded
Even after reaching the context coded bins to maximum limit, CABAC module still has to switch between by-pass and context coding
Example: VVC6 residual coding block bit-stream

## Slide 3
Proposed method : Method 1
After reaching the context coded bins to maximum limit, coded_sub_block_flag is by-pass coded.
Count coded_sub_block_flag along with context coded bins count
In regular residual coding,
  if (MaxCcbs >= 4)
    coded_sub_block_flag is context coded
    MaxCcbs--
  Otherwise, coded_sub_block_flag is by-pass coded
In transform-skip residual coding,
  if (MaxCcbs > 0)
    coded_sub_block_flag is context coded
    MaxCcbs--
  Otherwise, coded_sub_block_flag is by-pass coded

## Slide 4
Proposed method : Method 2
Reposition coded_sub_block_flag at the beginning of the transform block ( right after the last position signal in case of regular residual coding).

## Slide 5
Simulation results
Method 1
  Test 1.1 : maximum number of context coded bins (MaxCcbs) are same as VVC 6.
  Test 1.2 : MaxCcbs = (VVC6 max number of bins) + numberOfSubBlock
Method 2
  Test 2: Reposition coded_sub_block_flag at beginning, maximum number of context coded bins (MaxCcbs) are same as VVC 6.

## Slide 6
Simulation results : Test 1.1
CTC QP
Low QP
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.01% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.05% | 99% | 100%
Class B | 0.00% | 0.01% | 0.01% | 100% | 101%
Class C | 0.02% | -0.12% | 0.01% | 99% | 103%
Class E | -0.01% | 0.00% | -0.05% | 100% | 103%
Overall | 0.00% | -0.03% | 0.00% | 99% | 102%
Class D | 0.01% | -0.12% | -0.01% | 98% | 100%
Class F | 0.04% | 0.01% | -0.02% | 101% | 102%
Class SCC | 0.05% | 0.05% | 0.02% | 100% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.04% | 100% | 99%
Class A2 | 0.02% | 0.17% | 0.08% | 100% | 99%
Class B | -0.01% | 0.04% | 0.02% | 100% | 99%
Class C | 0.00% | 0.00% | -0.08% | 100% | 96%
Class E |  |  |  |  | 
Overall | 0.00% | 0.05% | 0.01% | 100% | 99%
Class D | -0.01% | -0.29% | -0.16% | 100% | 93%
Class F | 0.02% | 0.07% | 0.01% | 100% | 103%
Class SCC | 0.04% | 0.01% | 0.04% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.16% | 0.21% | 100% | 100%
Class C | -0.02% | 0.08% | -0.15% | 100% | 101%
Class E | 0.11% | -0.65% | -0.96% | 101% | 101%
Overall | 0.02% | -0.07% | -0.20% | 100% | 101%
Class D | 0.05% | 0.03% | -0.03% | 100% | 106%
Class F | 0.07% | -0.01% | 0.42% | 101% | 101%
Class SCC | -0.03% | -0.03% | -0.04% | 101% | 105%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.05% | 0.13% | 0.15% | 100% | 98%
Class A2 | 0.09% | 0.19% | 0.19% | 100% | 99%
Class B | 0.03% | 0.04% | 0.05% | 100% | 99%
Class C | 0.03% | 0.09% | 0.09% | 98% | 100%
Class E | 0.03% | 0.02% | 0.03% | 100% | 99%
Overall | 0.04% | 0.09% | 0.09% | 99% | 99%
Class D | 0.02% | 0.00% | 0.04% | 100% | 102%
Class F | 0.10% | -0.01% | 0.02% | 101% | 97%
Class SCC | 0.06% | 0.07% | 0.05% | 100% | 97%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05% | 0.09% | 0.10% | 99% | 101%
Class C | 0.06% | 0.13% | 0.15% | 100% | 101%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.05% | 0.17% | 0.08% | 100% | 102%
Class F | 0.13% | -0.13% | -0.20% | 101% | 102%
Class SCC | 0.08% | 0.12% | 0.15% | 102% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05% | 0.11% | 0.11% | 100% | 98%
Class C | 0.06% | 0.19% | 0.20% | 100% | 101%
Class E | 0.05% | 0.01% | 0.07% | 100% | 98%
Overall | 0.05% | 0.11% | 0.13% | 100% | 99%
Class D | 0.05% | 0.11% | 0.11% | 100% | 101%
Class F | 0.04% | 0.10% | 0.16% | 102% | 93%
Class SCC | 0.06% | 0.02% | 0.06% | 102% | 86%
* RA results will be updated

## Slide 7
Simulation results : Test 1.2
CTC QP
Low QP
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | 0.00% | 100% | 108%
Class A2 | 0.00% | 0.01% | 0.02% | 101% | 107%
Class B | 0.00% | 0.01% | 0.02% | 101% | 107%
Class C | 0.02% | -0.16% | 0.02% | 100% | 108%
Class E | 0.00% | 0.01% | -0.06% | 101% | 110%
Overall | 0.00% | -0.03% | 0.00% | 100% | 108%
Class D | -0.01% | -0.06% | 0.00% | 98% | 109%
Class F | -0.01% | 0.02% | -0.01% | 101% | 103%
Class SCC | -0.03% | -0.01% | -0.02% | 101% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.05% | 0.02% | 101% | 112%
Class A2 | 0.04% | -0.03% | 0.00% | 101% | 111%
Class B | -0.04% | 0.02% | -0.04% | 101% | 113%
Class C | -0.01% | 0.02% | -0.07% | 101% | 109%
Class E |  |  |  |  | 
Overall | -0.01% | 0.02% | -0.03% | 101% | 111%
Class D | -0.02% | 0.00% | 0.04% | 101% | 108%
Class F | 0.01% | 0.05% | 0.03% | 101% | 103%
Class SCC | 0.03% | -0.04% | -0.04% | 101% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.06% | -0.18% | 101% | 112%
Class C | 0.00% | -0.37% | -0.41% | 102% | 112%
Class E | -0.07% | 0.21% | 0.23% | 102% | 121%
Overall | -0.02% | -0.10% | -0.15% | 101% | 114%
Class D | 0.04% | -0.21% | 0.01% | 101% | 115%
Class F | -0.05% | -0.02% | 0.00% | 101% | 103%
Class SCC | -0.10% | -0.03% | 0.02% | 103% | 106%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.05% | 0.05% | 100% | 98%
Class A2 | 0.02% | 0.10% | 0.10% | 100% | 99%
Class B | -0.01% | 0.02% | 0.02% | 100% | 99%
Class C | 0.01% | 0.04% | 0.07% | 98% | 100%
Class E | -0.01% | -0.01% | 0.03% | 100% | 99%
Overall | 0.00% | 0.04% | 0.05% | 100% | 99%
Class D | 0.00% | 0.00% | 0.00% | 100% | 103%
Class F | 0.03% | -0.04% | -0.02% | 100% | 100%
Class SCC | -0.04% | -0.03% | -0.04% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.03% | 0.04% | 100% | 101%
Class C | -0.01% | 0.02% | 0.07% | 101% | 102%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.02% | -0.10% | 0.03% | 100% | 101%
Class F | 0.00% | -0.23% | -0.23% | 101% | 101%
Class SCC | 0.04% | -0.06% | -0.06% | 101% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.03% | 0.03% | 101% | 98%
Class C | -0.01% | 0.06% | 0.08% | 101% | 100%
Class E | 0.01% | 0.00% | 0.04% | 101% | 99%
Overall | 0.00% | 0.03% | 0.05% | 101% | 99%
Class D | -0.02% | 0.00% | -0.01% | 101% | 102%
Class F | -0.09% | -0.07% | -0.11% | 101% | 92%
Class SCC | -0.08% | -0.18% | -0.10% | 101% | 87%
RA results will be updated
** run-time is not accurate

## Slide 8
Simulation results : Test 2
CTC QP
Low QP
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 101% | 100%
Class B | 0.00% | 0.00% | 0.00% | 101% | 100%
Class C | 0.00% | 0.00% | 0.00% | 99% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 101% | 99%
Class F | 0.00% | 0.00% | 0.00% | 101% | 97%
Class SCC | 0.00% | 0.00% | 0.00% | 101% | 98%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 101%
Class C | 0.00% | 0.00% | 0.00% | 101% | 102%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.00% | 0.00% | 0.00% | 101% | 103%
Class F |  |  |  |  | 
Class SCC |  |  |  |  | 
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 101% | 100%
Class C | 0.00% | 0.00% | 0.00% | 101% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 101%
Overall | 0.00% | 0.00% | 0.00% | 101% | 100%
Class D | 0.00% | 0.00% | 0.00% | 101% | 100%
Class F | 0.00% | 0.00% | 0.00% | 101% | 97%
Class SCC | 0.00% | 0.00% | 0.00% | 100% | 97%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 108%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 106%
Class B | 0.00% | 0.00% | 0.00% | 101% | 107%
Class C | 0.00% | 0.00% | 0.00% | 100% | 108%
Class E | 0.00% | 0.00% | 0.00% | 101% | 110%
Overall | 0.00% | 0.00% | 0.00% | 100% | 108%
Class D | 0.00% | 0.00% | 0.00% | 99% | 109%
Class F | 0.00% | 0.00% | 0.00% | 102% | 103%
Class SCC | 0.00% | 0.00% | 0.00% | 101% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 111%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 110%
Class B | 0.00% | 0.00% | 0.00% | 101% | 112%
Class C | 0.00% | 0.00% | 0.00% | 101% | 109%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 111%
Class D | 0.00% | 0.00% | 0.00% | 101% | 108%
Class F | 0.00% | 0.00% | 0.00% | 101% | 103%
Class SCC | 0.00% | 0.00% | 0.00% | 101% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 109%
Class C | 0.00% | 0.00% | 0.00% | 101% | 110%
Class E | 0.00% | 0.00% | 0.00% | 101% | 119%
Overall | 0.00% | 0.00% | 0.00% | 101% | 112%
Class D | 0.00% | 0.00% | 0.00% | 101% | 114%
Class F | 0.00% | 0.00% | 0.00% | 101% | 102%
Class SCC | 0.00% | 0.00% | 0.00% | 102% | 104%
** run-time is not accurate
RA results will be updated

## Slide 9
Conclusion
Summary results
  Test 1.1: 0.00% (AI), 0.00% (RA), 0.02% (LB) luma BD-rate
  Test 1.2: 0.00% (AI), -0.01% (RA), -0.02% (LB) luma BD-rate
  Test 2 : 0.00% (AI), 0.00% (RA), 0.00% (LB) luma BD-rate
The proposed method reduces context/bypass switching
Guarantee there is no context coding after reaching to the maximum context coded bins.

## Slide 10
Additional results : Test 1.1
CTC QP
Low QP
** run-time is not accurate
RA results will be updated
Anchor: VTM-6.0 ( Max. num of context coded bins = 2 bins per coefficients)
Test: test 1.1 + Max. num of context coded bins = 1.75 bins per coefficients
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.13% | 0.12% | 0.04% | 101% | 98%
Class SCC | 0.34% | 0.29% | 0.28% | 101% | 97%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.12% | 0.10% | 0.13% | 101% | 90%
Class SCC | 0.23% | 0.18% | 0.16% | 100% | 88%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.44% | 0.19% | 0.21% | 100% | 97%
Class SCC | 0.53% | 0.49% | 0.50% | 100% | 96%