## Slide 1
Non-CE4: Flexible MMVD candidates
JVET-P0384
F. Galpin, F. Le Léannec, A. Robert

## Slide 2: Problem
In VTM-6.0 some heuristics are hard-coded in the syntax:
  E.g.: only the first 2 merge candidates are used for MMVD mode
While it offers a good complexity/gains tradeoff in the VTM, different encoders may want to implement different heuristics:
  Encoders working from pre-computed motion field want flexibility in motion vector candidates choice, as opposed to VTM full RDO.
  High complexity encoders (e.g. streaming application) may have a different complexity/gains tradeoff compared to JVET choices.
Consistency: other merge modes use the whole candidates list derivation

## Slide 3: Proposal
It is proposed use the same merge list as other merge modes.
In order to keep current heuristic and tradeoff in VTM, the hard-coded heuristic is transformed into a soft heuristic (CABAC context on the second merge candidate).

## Slide 4: Results Test 1
No encoder change, VTM-6.0 heuristics (2 candidates)
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.06% | -0.01% | 102% | 105%
Class A2 | 0.02% | 0.10% | 0.04% | 104% | 110%
Class B | 0.00% | 0.10% | 0.02% | 97% | 99%
Class C | -0.01% | 0.01% | -0.04% | 100% | 96%
Class E |  |  |  |  | 
Overall | 0.00% | 0.04% | 0.00% | 100% | 102%
Class D | -0.05% | -0.05% | -0.14% | 100% | 88%
Class F | 0.01% | 0.00% | -0.02% | 101% | 95%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.09% | -0.14% | 102% | 104%
Class C | -0.01% | -0.02% | 0.06% | 104% | 109%
Class E | 0.04% | 0.67% | 0.92% | 97% | 94%
Overall | 0.01% | 0.20% | 0.19% | 102% | 103%
Class D | 0.04% | 0.06% | 0.37% | 100% | 98%
Class F | 0.02% | 0.07% | 0.29% | 103% | 104%

## Slide 5: Results Test 2
Encoder leveraging newly available candidates
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.05% | -0.01% | 109% | 107%
Class A2 | -0.11% | -0.09% | -0.19% | 110% | 109%
Class B | -0.10% | -0.07% | -0.16% | 105% | 99%
Class C | -0.07% | 0.08% | 0.04% | 106% | 94%
Class E |  |  |  |  | 
Overall | -0.08% | -0.03% | -0.08% | 107% | 101%
Class D | -0.14% | -0.15% | -0.19% | 107% | 88%
Class F | -0.04% | -0.11% | -0.08% | 105% | 94%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-6.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.02% | -0.43% | 106% | 104%
Class C | -0.06% | -0.14% | -0.14% | 109% | 109%
Class E | 0.05% | 0.64% | 0.61% | 102% | 94%
Overall | -0.02% | 0.10% | -0.07% | 106% | 103%
Class D | -0.07% | 0.41% | 0.36% | 104% | 98%
Class F | 0.04% | 0.19% | 1.06% | 103% | 105%

## Slide 6: Conclusion
Proposed change allows more gains in all configurations when leveraging new available candidates. Increase the flexibility for choosing a motion vector candidate.
Current VTM-6.0 complexity is unchanged.
Impact on VTM-6.0 is minimal:
  the codec design is unchanged (no new mode is introduced),
  the worst case is unchanged,
  VTM-6.0 current heuristics give similar performance and complexity.
Thanks to Qualcomm for cross-checking