## Slide 1: On BD-rate computation for tools affecting quantization
JVET-P0393
Advanced Technology Team
European Professional Engineering
Sony Europe Ltd.
Steve Keating
Sony Corp.

## Slide 2: Introduction
This is to shine light on BD-rate results where effective quantization is affected
LMCS is used as an example but all tools should be examined

## Slide 3: Example results
Look at the standard BD-rate summary (from AHG13 report):
 | All Intra |  |  |  | 
 | LMCS tool off over VTM6.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 2.08% | 0.35% | 2.70% | 104% | 96%
Class A2 | 3.04% | -0.38% | -0.76% | 103% | 99%
Class B | 0.75% | 0.10% | 0.29% | 98% | 97%
Class C | 0.23% | -2.61% | -2.66% | 95% | 93%
Class E | 0.06% | -3.09% | -2.84% | 94% | 94%
Overall | 1.12% | -1.07% | -0.66% | 98% | 96%
Class D | 0.18% | -2.17% | -2.37% | 97% | 95%
Class F | 0.65% | -1.26% | -1.24% | 98% | 94%
Class TGM | 1.22% | -0.01% | 0.21% | 100% | 97%

## Slide 4: Example results
Now look at the results for each sequence:
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class A1 | Tango2 | 1.48% | 1.26% | 1.71% | 1.29% | 1.56% | 2.09%
 | FoodMarket4 | 2.49% | 4.89% | 5.80% | 2.55% | 4.95% | 5.84%
 | CampfireParty2 | 1.68% | -4.89% | 0.64% | 2.26% | -5.06% | 0.53%
Class A2 | CatRobot1 | 1.05% | 2.01% | 1.45% | 0.80% | 2.20% | 1.68%
 | DaylightRoad2 | 3.16% | 2.40% | 1.91% | 1.87% | 2.78% | 2.47%
 | ParkRunning3 | 4.84% | -5.43% | -5.59% | 4.84% | -5.43% | -5.59%
Class B | MarketPlace | 2.04% | 1.04% | 2.55% | 2.04% | 1.08% | 2.54%
 | RitualDance | 0.22% | -2.60% | -2.68% | 0.22% | -2.59% | -2.68%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.43% | -1.82% | -2.18% | 0.16% | -1.84% | -2.17%
 | BQTerrace | 0.88% | 3.15% | 2.99% | -0.17% | 3.42% | 3.18%

## Slide 5: Example results
Now look at the results for each sequence:
For some sequences there’s a big discrepancy between the two interpolation methods
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class A1 | Tango2 | 1.48% | 1.26% | 1.71% | 1.29% | 1.56% | 2.09%
 | FoodMarket4 | 2.49% | 4.89% | 5.80% | 2.55% | 4.95% | 5.84%
 | CampfireParty2 | 1.68% | -4.89% | 0.64% | 2.26% | -5.06% | 0.53%
Class A2 | CatRobot1 | 1.05% | 2.01% | 1.45% | 0.80% | 2.20% | 1.68%
 | DaylightRoad2 | 3.16% | 2.40% | 1.91% | 1.87% | 2.78% | 2.47%
 | ParkRunning3 | 4.84% | -5.43% | -5.59% | 4.84% | -5.43% | -5.59%
Class B | MarketPlace | 2.04% | 1.04% | 2.55% | 2.04% | 1.08% | 2.54%
 | RitualDance | 0.22% | -2.60% | -2.68% | 0.22% | -2.59% | -2.68%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.43% | -1.82% | -2.18% | 0.16% | -1.84% | -2.17%
 | BQTerrace | 0.88% | 3.15% | 2.99% | -0.17% | 3.42% | 3.18%

## Slide 6: Example results
Now look at the results for each sequence:
For some sequences there’s a big discrepancy between the two interpolation methods
This should be a red flag
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class A1 | Tango2 | 1.48% | 1.26% | 1.71% | 1.29% | 1.56% | 2.09%
 | FoodMarket4 | 2.49% | 4.89% | 5.80% | 2.55% | 4.95% | 5.84%
 | CampfireParty2 | 1.68% | -4.89% | 0.64% | 2.26% | -5.06% | 0.53%
Class A2 | CatRobot1 | 1.05% | 2.01% | 1.45% | 0.80% | 2.20% | 1.68%
 | DaylightRoad2 | 3.16% | 2.40% | 1.91% | 1.87% | 2.78% | 2.47%
 | ParkRunning3 | 4.84% | -5.43% | -5.59% | 4.84% | -5.43% | -5.59%
Class B | MarketPlace | 2.04% | 1.04% | 2.55% | 2.04% | 1.08% | 2.54%
 | RitualDance | 0.22% | -2.60% | -2.68% | 0.22% | -2.59% | -2.68%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.43% | -1.82% | -2.18% | 0.16% | -1.84% | -2.17%
 | BQTerrace | 0.88% | 3.15% | 2.99% | -0.17% | 3.42% | 3.18%

## Slide 7: Why is this happening?
JVET-N0031 already proposed increasing the number of points used in rate-distortion calculations
What happens when you test 16 points?

## Slide 8: Why is this happening?
    4-point results 16-point results
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class A1 | Tango2 | 1.48% | 1.26% | 1.71% | 1.29% | 1.56% | 2.09%
 | FoodMarket4 | 2.49% | 4.89% | 5.80% | 2.55% | 4.95% | 5.84%
 | CampfireParty2 | 1.68% | -4.89% | 0.64% | 2.26% | -5.06% | 0.53%
Class A2 | CatRobot1 | 1.05% | 2.01% | 1.45% | 0.80% | 2.20% | 1.68%
 | DaylightRoad2 | 3.16% | 2.40% | 1.91% | 1.87% | 2.78% | 2.47%
 | ParkRunning3 | 4.84% | -5.43% | -5.59% | 4.84% | -5.43% | -5.59%
Class B | MarketPlace | 2.04% | 1.04% | 2.55% | 2.04% | 1.08% | 2.54%
 | RitualDance | 0.22% | -2.60% | -2.68% | 0.22% | -2.59% | -2.68%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.43% | -1.82% | -2.18% | 0.16% | -1.84% | -2.17%
 | BQTerrace | 0.88% | 3.15% | 2.99% | -0.17% | 3.42% | 3.18%
 |  | BD-rate (piecewise cubic) |  |  | 
 |  | Y | U | V | YUV
Class A1 | Tango2 | -0.51% | 3.77% | 4.05% | 0.02%
 | FoodMarket4 | 2.44% | 4.97% | 5.96% | -0.60%
 | CampfireParty2 | 1.39% | -4.75% | 0.67% | 0.30%
Class A2 | CatRobot1 | -0.75% | 3.99% | 3.40% | 0.10%
 | DaylightRoad2 | -1.30% | 5.78% | 5.30% | -0.58%
 | ParkRunning3 | 4.82% | -5.45% | -5.62% | -1.04%
Class B | MarketPlace | 1.95% | 0.65% | 2.40% | -1.02%
 | RitualDance | 0.20% | -2.58% | -2.67% | -0.21%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.21% | -1.58% | -1.70% | -0.22%
 | BQTerrace | 0.25% | 3.12% | 3.04% | -0.18%

## Slide 9: Why is this happening?
The tool effectively moves the luma QP by ~1

## Slide 10: Why is this happening?

## Slide 11: Why is this happening?
Did we really subsample that curve?

## Slide 12: Why is this happening?
Recommend that if piecewise cubic and cubic results differ by ~10% then test with 16 points (tolerating small BD-rates)
So we don’t need to do this for every tool
We don’t need to do it for every sequence either
Any tool which effectively moves the QP should be closely examined

## Slide 13: Using Combined YUV PSNR
JVET-N0341 proposed also reporting a combined YUV PSNR
This could be very useful for comparing Y-only tools (MIP), C-only tools (CCLM) or where there’s a shift between Y and C (LMCS)
  Separate Y, U and V metrics are still important for subjective understanding
 | LMCS Tool Off over VTM6.1 (16-point) |  |  | 
 | Y | U | V | YUV
Class A1 | 1.11% | 1.33% | 3.56% | -0.09%
Class A2 | 0.92% | 1.44% | 1.03% | -0.51%
Class B | 0.52% | -0.08% | 0.21% | -0.33%
Class C | 0.29% | -2.27% | -2.38% | -0.21%
Class E | 0.06% | -3.14% | -3.01% | -0.35%
Overall | 0.56% | -0.59% | -0.30% | -0.30%
Class D | 0.17% | -2.16% | -2.19% | -0.27%
Class F | 0.39% | -1.23% | -1.22% | 0.04%
Class TGM | 0.67% | 0.10% | 0.28% | 0.50%

## Slide 14: Using Combined YUV PSNR
Sometimes there are conflicting results
 |  | BD-rate (piecewise cubic) |  |  | 
 |  | Y | U | V | YUV
Class A1 | Tango2 | -0.51% | 3.77% | 4.05% | 0.02%
 | FoodMarket4 | 2.44% | 4.97% | 5.96% | -0.60%
 | CampfireParty2 | 1.39% | -4.75% | 0.67% | 0.30%
Class A2 | CatRobot1 | -0.75% | 3.99% | 3.40% | 0.10%
 | DaylightRoad2 | -1.30% | 5.78% | 5.30% | -0.58%
 | ParkRunning3 | 4.82% | -5.45% | -5.62% | -1.04%
Class B | MarketPlace | 1.95% | 0.65% | 2.40% | -1.02%
 | RitualDance | 0.20% | -2.58% | -2.67% | -0.21%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.21% | -1.58% | -1.70% | -0.22%
 | BQTerrace | 0.25% | 3.12% | 3.04% | -0.18%

## Slide 15: Using Combined YUV PSNR
Sometimes there are conflicting results
How can YUV be negative when Y, U and V are all positive?
Let’s look more closely at FoodMarket
  In particular, on a per-POC basis
 |  | BD-rate (piecewise cubic) |  |  | 
 |  | Y | U | V | YUV
Class A1 | Tango2 | -0.51% | 3.77% | 4.05% | 0.02%
 | FoodMarket4 | 2.44% | 4.97% | 5.96% | -0.60%
 | CampfireParty2 | 1.39% | -4.75% | 0.67% | 0.30%
Class A2 | CatRobot1 | -0.75% | 3.99% | 3.40% | 0.10%
 | DaylightRoad2 | -1.30% | 5.78% | 5.30% | -0.58%
 | ParkRunning3 | 4.82% | -5.45% | -5.62% | -1.04%
Class B | MarketPlace | 1.95% | 0.65% | 2.40% | -1.02%
 | RitualDance | 0.20% | -2.58% | -2.67% | -0.21%
 | Cactus | 0.00% | 0.00% | 0.00% | 0.00%
 | BasketballDrive | 0.21% | -1.58% | -1.70% | -0.22%
 | BQTerrace | 0.25% | 3.12% | 3.04% | -0.18%

## Slide 16: Using Combined YUV PSNR
Should we really be just averaging this data?

## Slide 17: Using Combined YUV PSNR
Should we really be just averaging this data?
In this case the only line that it’s safe to average is the purple YUV line.
When there are such radical shifts we shouldn’t be averaging the PSNR for each POC…
We should calculate PSNR on the MSE of the whole data, or split the sequence

## Slide 18: Low QP Tests
Currently these only use the first 100 frames
Is this representative?

## Slide 19: Low QP Tests
Currently these only use the first 100 frames
Is this representative?

## Slide 20: Low QP Tests - recommendations
(Don’t do BD-rate calculations using a mix of low QP and normal QP results under CTC)
Maybe it would be better objectively for: AI to do 1 in 32 frames RA to do 17 frames every 64 across the whole sequence

## Slide 21: Summary 1/2
We hear arguments for tool inclusion with a BD-rate gain of 0.2% - 0.3%
We need to be confident that the figure is meaningful
  In some cases it probably isn’t
We already collate figures for two different interpolation methods
The spreadsheet could be modified to flag up differences of ~10%
  These should then be investigated
  Probably only affects a few tools
    AHG13 could confirm.

## Slide 22: Summary 2/2
We should include YUV BD-rate into the spreadsheet
Where this gives different results they should be justified
  E.g. monochrome testing
  E.g. luma/chroma QP/lambda testing
  E.g. per-POC BD-rates should be examined
We should add YUV PNSR (and hex PSNR) to per-POC line of VTM
The impact of sequences that have a change in PSNR, bit-rate or BD-rate from one end to the other should be studied further.
Consider changing low QP to cover the whole sequence