## Slide 1: Switching between CABAC context coded bins and bypass coded bins
JVET-P0396
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Steve Keating / Karl Sharman
Sony Corp.

## Slide 2: Introduction
JVET-O0519 introduced switching between CABAC and bypass coding
  Avoids padding with CABAC zero words
  Padding implicitly coded into bit stream by using bypass bins instead of CABAC bins followed by CABAC zero words at the end of the slice
    Reduces ratio of CABAC bins to bypass bins, potentially making decoding simpler.
  In addition control of transform block coefficient coded bins was moved to the entropy layer
When presented during the 15th JVET meeting in Gothenburg it was noted:
  The decision path required for switching might increase the length of the critical path for the CABAC engine.
  The proposal allowed switching in too many places.
  (and further work was encouraged.)

## Slide 3: Introduction
This proposal attempts to resolve the issues in the previous proposal
  A limited number of potential switching points has been introduced
    At fixed points in the coding
  Decisions and switching are separated
    To alleviate CABAC engine critical path issues
This proposal maintains the gains, particularly for low QP and screen content, seen for the previous proposal.
In addition, following the adoption of JVET-O0052, the new limits on context coded bins have been removed to allow for bin-to-bit control in the entropy layer.

## Slide 4: Background
JVET-O0519 introduced counters in the entropy level of both the encoder and decoder.
  Counters constrain bin-to-bit ratio
  Counters initialised to a value based on the current CABAC zero word threshold.
  Counters are incremented whenever bits are read/written
  Counters are decremented whenever bins are coded
  Mixed CABAC/bypass coding is used if the counter indicates bins can be coded without exceeding the CABAC zero word threshold
  Otherwise, use pure bypass coding
    CABAC usage effectively rationed to maintain threshold
    No CABAC zero words required
JVET-O0519 replaced counters for bins in TU level coefficient coding

## Slide 5: Changes from JVET-O0519
Switching between mixed and pure bypass coding only occurs at discrete points:
  At the beginning of each CTU
  Immediately after encoding a merge skip CU
  Immediately before encoding a sub-TU residual block
  Immediately before encoding a sub-TU transform skip residual block
  Immediately after encoding a TU if CBF=0
    when no sub-TU residual has been encoded

## Slide 6: Changes from JVET-O0519
Initial counter setting decremented by fixed quantity
  2 * maximum number of bins used between any two switch points
    Value derived empirically as specification still subject to change (+50% margin)
At switch point a decision is made to use mixed or bypass coding
  Based on simple test of counter against zero
Decision is not applied until the next switch point
  Adds pipeline delay of one switch point on each decision
    Removes hardware pipelining issue
Removed bin limits introduced in JVET-O0052

## Slide 7: Implementation - Counter
Assuming CABAC zero word threshold is given as in 7.4.3.11 of specification
Initial value of counter is given as:
availableBinFractionalCount = 3 * ( RawMinCuBits * PicSizeInMinCbsY )  32 – 2 * 256
Increment count by 4 for every bit read
Decrement count by 3 for every bin coded
Increment count by 1 (4 – 3) for every bypass bin coded
Max CABAC bins between switchpoints

## Slide 8: Implementation - Switching
forceBypassFlag and nextForceBypassFlag are initialized to 0.
To remove conditional in VTM’s DecodeBin, forceBypassFlag could be replaced by another construct
e.g. function pointer in C++.
DecodeMixedBin is identical to DecodeBin in existing specification

## Slide 9: Results - CTC
 |  |  | AI |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.02% | -0.01% | 100% | 101%
Class A2 | 0.00% | -0.01% | 0.03% | 100% | 100%
Class B | 0.01% | 0.03% | -0.02% | 100% | 100%
Class C | -0.05% | -0.20% | -0.09% | 100% | 101%
Class E | 0.01% | 0.05% | 0.04% | 100% | 100%
Overall | -0.01% | -0.03% | -0.02% | 100% | 100%
Class D | -0.04% | -0.08% | -0.24% | 100% | 99%
Class F | -0.18% | -0.34% | -0.23% | 100% | 101%
Class TGM | -0.43% | -0.41% | -0.38% | 100% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.06% | 0.07% | 101% | 100%
Class A2 | 0.03% | 0.11% | -0.02% | 100% | 100%
Class B | -0.01% | 0.19% | 0.09% | 100% | 100%
Class C | -0.02% | 0.03% | -0.04% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.10% | 0.03% | 100% | 100%
Class D | -0.05% | -0.41% | -0.14% | 100% | 101%
Class F | -0.21% | -0.35% | -0.14% | 100% | 100%
Class TGM | -0.38% | -0.33% | -0.35% | 101% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.27% | -0.22% | 101% | 99%
Class C | -0.04% | -0.19% | 0.12% | 100% | 100%
Class E | -0.23% | 0.27% | 0.32% | 101% | 101%
Overall | -0.07% | 0.12% | 0.03% | 101% | 100%
Class D | 0.01% | -0.09% | 0.61% | 100% | 99%
Class F | -0.04% | -0.36% | 0.08% | 101% | 101%
Class TGM | -0.38% | -0.27% | -0.23% | 100% | 100%

## Slide 10: Results – low QP
 |  |  | AI |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.40% | -0.47% | -0.49% | 101% | 104%
Class A2 | -0.34% | -0.53% | -0.54% | 102% | 107%
Class B | -0.06% | -0.07% | -0.11% | 103% | 107%
Class C | -0.03% | -0.10% | -0.09% | 104% | 108%
Class E | -0.10% | -0.26% | -0.21% | 100% | 102%
Overall | -0.16% | -0.25% | -0.26% | 102% | 106%
Class D | -0.04% | -0.13% | -0.11% | 102% | 105%
Class F | -1.69% | -0.83% | -0.85% | 100% | 101%
Class TGM | -2.24% | -1.83% | -1.81% | 101% | 101%
 |  |  | RA |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.36% | -0.40% | -0.46% | 100% | 102%
Class A2 | -0.56% | -0.85% | -0.85% | 102% | 104%
Class B | -0.29% | -0.34% | -0.40% | 101% | 103%
Class C | -0.19% | -0.35% | -0.40% | 102% | 104%
Class E |  |  |  |  | 
Overall | -0.33% | -0.46% | -0.50% | 101% | 103%
Class D | -0.23% | -0.42% | -0.39% | 102% | 103%
Class F | -2.46% | -0.86% | -0.74% | 100% | 101%
Class TGM | -2.49% | -1.65% | -1.66% | 103% | 101%
 |  |  | LDB |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.34% | -0.40% | -0.45% | 101% | 103%
Class C | -0.26% | -0.44% | -0.49% | 102% | 105%
Class E | -0.22% | -0.08% | -0.14% | 100% | 101%
Overall | -0.28% | -0.34% | -0.39% | 101% | 103%
Class D | -0.26% | -0.39% | -0.42% | 102% | 105%
Class F | -0.78% | -0.62% | -0.71% | 101% | 101%
Class TGM | -1.55% | -1.28% | -1.28% | 104% | 101%

## Slide 11: Draft text
Included in Word document
Switch points described as “aes()” in the syntax tables
  arithmetic engine switch

## Slide 12: Conclusion 1/2
Presented a modified version of JVET-O519 in response to comments
  Reduced switching
    Only at discrete points
  Simpler decision
    Simple comparison with 0
  Separated switch from decision
    Improved pipelining
    Reduced length of critical path for entropy decoder
  Gains maintained for low QP (-0.33% overall for RA)
  Gains presented for screen content (-2.49% low QP / -0.38% CTC)
  No losses for other content in CTC

## Slide 13: Conclusion 2/2
We have presented a modification that:
  has fewer counters than VTM
  is effective over all bins – not just TU coefficients
  could support sliding scale of bin/bit ratio for future profiles
  eliminates CABAC zero word padding at end of picture
    Simpler splicing of decodable regions
  reduces CABAC/bypass-bin ratio
    Without impact to bin/bit ratio
    Each byte of CABAC zero word padding represents a wasted opportunity
      Could code 8 bypass bins instead