## Slide 1
JVET-P0397
CE7-related: Simplified two-pass transform-skip residual coding
2019/10/3

## Slide 2
Proposed method
The proposed method reduces the number of checks if context coded bins are available or not from 8 per coefficient to 1 per coefficient
Sam as CE7-1.3.b-alt except number of coding passes is 2 whereas number of coding passes in CE7-1.3b-alt is 3

## Slide 3
Proposed method
Pass 1: for(n = 0; n <= numSbCoeff - 1; n++ )
sig_coeff_flag (MaxCcbs > 0 ? Context : Bypass)
coeff_sign_flag (MaxCcbs > 0 ? Context : Bypass)
gt1 (MaxCcbs > 0 ? Context : Bypass)
par_level_flag (MaxCcbs > 0 ? Context : Bypass)
Pass 2: for(n = 0; n <= numSbCoeff - 1 ; n++ )
gt3 (MaxCcbs > 0 ? Context : Bypass)
gt5 (MaxCcbs > 0 ? Context : Bypass)
gt7 (MaxCcbs > 0 ? Context : Bypass)
gt9 (MaxCcbs > 0 ? Context : Bypass)
Pass 3: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
Pass 1: for(n = 0; n <= numSbCoeff - 1 && MaxCcbs >= 8; n++ )
sig_coeff_flag (context)
coeff_sign_flag (context)
gt1(context)
par_level_flag (context)
gt3 (context)
gt5 (context)
gt7 (context)
gt9 (context)
firstScanPos[1] = n
Pass 2: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
VVC6
JVET-P0397

## Slide 4
Pass 1: for(n = 0; n <= numSbCoeff - 1 && MaxCcbs >= 4; n++ )
sig_coeff_flag (context)
coeff_sign_flag (context)
gt1(context)
par_level_flag (context)
firstScanPos[2] = n
Pass 2: for(n = 0; n <= firstScanPos[2] && MaxCcbs >= 4; n++ )
gt3 (context)
gt5 (context)
gt7 (context)
gt9 (context)
firstScanPos[1] = n
Pass 3: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
Pass 1: for(n = 0; n <= numSbCoeff - 1 && MaxCcbs >= 8; n++ )
sig_coeff_flag (context)
coeff_sign_flag (context)
gt1(context)
par_level_flag (context)
gt3 (context)
gt5 (context)
gt7 (context)
gt9 (context)
firstScanPos[1] = n
Pass 2: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
Proposed method
CE7-1.3.b-alternative
JVET-P0397

## Slide 5
Simulation results:
CTC QP
Low QP
* RA results will be updated
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | -0.01% | 100% | 101%
Class A2 | 0.00% | 0.00% | 0.02% | 100% | 101%
Class B | 0.00% | -0.02% | -0.04% | 101% | 102%
Class C | 0.01% | -0.02% | -0.01% | 100% | 104%
Class E | 0.00% | 0.08% | 0.00% | 101% | 104%
Overall | 0.00% | 0.01% | -0.01% | 100% | 102%
Class D | 0.01% | 0.01% | -0.07% | 99% | 106%
Class F | 0.10% | 0.07% | 0.03% | 101% | 99%
Class SCC | 0.25% | 0.30% | 0.29% | 100% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | 0.01% | 100% | 100%
Class A2 | 0.02% | 0.11% | 0.07% | 101% | 100%
Class B | -0.02% | 0.04% | 0.09% | 101% | 102%
Class C | 0.01% | -0.01% | 0.04% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.06% | 101% | 101%
Class D | -0.04% | -0.17% | -0.16% | 100% | 101%
Class F | 0.10% | 0.05% | 0.19% | 100% | 100%
Class SCC | 0.17% | 0.14% | 0.20% | 99% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.04% | 0.11% | -0.32% | 101% | 101%
Class C | 0.01% | -0.01% | -0.03% | 101% | 104%
Class E | -0.13% | 0.07% | -0.14% | 102% | 102%
Overall | -0.05% | 0.06% | -0.17% | 101% | 102%
Class D | -0.04% | 0.10% | -0.18% | 101% | 107%
Class F | 0.16% | 0.11% | 0.54% | 99% | 99%
Class SCC | -0.03% | 0.01% | 0.09% | 100% | 104%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.04% | 100% | 97%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 98%
Class B | -0.01% | 0.00% | 0.01% | 100% | 98%
Class C | -0.04% | -0.03% | -0.02% | 98% | 99%
Class E | -0.06% | -0.04% | -0.05% | 100% | 98%
Overall | -0.02% | -0.01% | -0.01% | 99% | 98%
Class D | -0.04% | -0.04% | -0.03% | 99% | 101%
Class F | -1.00% | -0.28% | -0.28% | 99% | 98%
Class SCC | -0.69% | -0.40% | -0.38% | 98% | 97%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.01% | 100% | 101%
Class C | -0.02% | -0.02% | -0.02% | 100% | 101%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.06% | -0.04% | 0.00% | 99% | 101%
Class F | -1.33% | -0.44% | -0.35% | 100% | 109%
Class SCC | -1.46% | -0.39% | -0.41% | 100% | 113%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.01% | 0.00% | 100% | 98%
Class C | -0.01% | 0.01% | -0.03% | 100% | 100%
Class E | -0.07% | 0.00% | 0.01% | 100% | 99%
Overall | -0.03% | 0.00% | -0.01% | 100% | 99%
Class D | -0.04% | 0.05% | -0.08% | 99% | 100%
Class F | -0.34% | -0.18% | -0.19% | 100% | 100%
Class SCC | -0.46% | -0.19% | -0.13% | 100% | 98%

## Slide 6
Conclusion
The proposed method reduces the worst case number of checking of whether to perform bypass or context coding from 8 per coefficient position to 1 per coefficient position.
Experimental results show that 0.25% (AI), 0.17% (RA), -0.03% (LB) luma BD-rate of SCC sequences under CTC test conditions.
In low QP test settings, the proposed method can achieve -0.69% (AI), -1.46% (RA), -0.46% (LB) luma BD-rate of SCC sequences.

## Slide 7
Additional results:
Anchor: VTM-6.0 ( where maximum context coded bins is 2 per coeff)
Test: Proposed + max Context coded bins 1.75 per coeff
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.25% | 0.16% | 0.23% | 101% | 102%
Class SCC | 0.53% | 0.55% | 0.52% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.21% | 0.38% | 0.30% | 101% | 103%
Class SCC | 0.34% | 0.39% | 0.35% | 101% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.02% | -0.08% | 0.66% | 101% | 103%
Class SCC | 0.11% | 0.25% | 0.23% | 101% | 106%
CTC QP

## Slide 8
Pass 1: for(n = 0; n <= numSbCoeff - 1 && MaxCcbs >= 8; n++ )
sig_coeff_flag (context)
coeff_sign_flag (context)
gt1(context)
par_level_flag (context)
gt3 (context)
gt5 (context)
gt7 (context)
gt9 (context)
firstScanPos[1] = n
Pass 2: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
Proposed method
VVC6 transform residual coding
JVET-P0397
Pass 1: for(n = 0; n <= numSbCoeff - 1 && MaxCcbs >= 8; n++ )
sig_coeff_flag (context)
gt1(context)
par_level_flag (context)
Gt2 (context)
firstScanPos[1] = n
Pass 2: for(n = 0; n <= numSbCoeff - 1; n++ )
Rice-Golomb Coding
Pass 3: for(n = 0; n <= numSbCoeff - 1; n++ )
coeff_sign_flag (By-pass)