## Slide 1
CE7-related: Unification of CCB count method between transform residual and TS residual coding
JVET-P0402
Y. Chen, F. Le Léannec, T. Poirier, K.Naser

## Slide 2: JVET-P0402: Unification of CCB count method between transform and TS residual
VTM-6.0
  Transform residual: 1.75 bin/coefficient
  TS residual: 2 bin/coefficient
  Transform residual: coeff_sign_flag bypass
  TS residual: coeff_sign_flag context-coded, and included into CCB count

## Slide 3: JVET-P0402: Unification of CCB count method between transform and TS residual
Proposed Test1
  TS residual: 1.75 bin/coefficient
  TS residual: exclude coeff_sign_flag from CCB count

## Slide 4: JVET-P0402: Unification of CCB count method between transform and TS residual
Proposed Test2 (based on Test1)
  Assign CCB_SIGN for coeff_sign_flag to control the CABAC throughput of this syntax independently
  CCB_SIGN: 0.5 bin/coefficient at TB level

## Slide 5: JVET-P0402-Test1: CTC results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | 0.00% | 105% | 104%
Class A2 | 0.00% | 0.00% | 0.01% | 104% | 104%
Class B | 0.00% | 0.00% | -0.05% | 104% | 104%
Class C | -0.01% | -0.05% | 0.07% | 106% | 106%
Class E | 0.00% | 0.04% | -0.04% | 107% | 106%
Overall | 0.00% | -0.01% | 0.00% | 105% | 105%
Class D | -0.02% | -0.02% | -0.05% | 104% | 107%
Class F | -0.06% | -0.11% | 0.09% | 106% | 126%
TGM | -0.11% | -0.07% | -0.09% | 104% | 119%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.05% | 104% | 105%
Class A2 | 0.00% | 0.12% | 0.07% | 104% | 106%
Class B | -0.01% | 0.11% | 0.11% | 98% | 97%
Class C | -0.02% | -0.13% | -0.16% | 101% | 94%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.02% | 101% | 100%
Class D | -0.05% | -0.21% | 0.00% | 101% | 90%
Class F | -0.10% | -0.05% | 0.04% | 101% | 102%
TGM | -0.09% | -0.08% | -0.03% | 101% | 106%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.17% | -0.21% | 105% | 104%
Class C | -0.03% | -0.02% | -0.12% | 105% | 108%
Class E | -0.06% | 0.05% | -0.40% | 100% | 94%
Overall | -0.03% | 0.08% | -0.23% | 104% | 103%
Class D | 0.02% | -0.11% | 0.07% | 103% | 101%
Class F | -0.05% | -0.28% | 0.23% | 112% | 138%
TGM | -0.02% | 0.04% | 0.08% | 99% | 96%

## Slide 6: JVET-P0402-Test2: CTC results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | -0.01% | 104% | 103%
Class A2 | 0.00% | 0.00% | 0.00% | 104% | 105%
Class B | 0.00% | 0.01% | -0.03% | 106% | 105%
Class C | 0.01% | -0.06% | -0.02% | 105% | 106%
Class E | 0.00% | 0.04% | -0.03% | 106% | 105%
Overall | 0.00% | -0.01% | -0.02% | 105% | 105%
Class D | -0.01% | -0.02% | 0.05% | 105% | 108%
Class F | -0.05% | -0.06% | 0.04% | 88% | 94%
TGM | -0.09% | -0.06% | -0.06% | 88% | 91%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.01% | 0.03% | 103% | 105%
Class A2 | 0.00% | 0.08% | 0.09% | 103% | 106%
Class B | -0.01% | 0.11% | 0.06% | 98% | 99%
Class C | 0.00% | 0.08% | -0.09% | 101% | 93%
Class E |  |  |  |  | 
Overall | 0.00% | 0.07% | 0.02% | 101% | 100%
Class D | -0.04% | -0.22% | 0.09% | 101% | 86%
Class F | -0.06% | -0.04% | 0.09% | 104% | 96%
TGM | -0.07% | -0.06% | -0.10% | 98% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.10% | 0.12% | 103% | 102%
Class C | -0.05% | 0.02% | -0.15% | 105% | 108%
Class E | -0.07% | -0.28% | -0.28% | 98% | 93%
Overall | -0.03% | -0.02% | -0.07% | 102% | 101%
Class D | 0.01% | -0.17% | 0.45% | 102% | 98%
Class F | 0.05% | 0.03% | 0.60% | 88% | 97%
TGM | -0.09% | -0.07% | 0.00% | 89% | 93%

## Slide 7: JVET-P0402-Test1: LowQP results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.03% | -0.03% | 118% | 93%
Class A2 | 0.00% | 0.00% | 0.01% | 112% | 90%
Class B | -0.01% | -0.01% | 0.03% | 114% | 90%
Class C | 0.00% | 0.00% | 0.00% | 111% | 92%
Class E | -0.04% | -0.05% | -0.05% | 115% | 91%
Overall | -0.01% | -0.02% | -0.01% | 114% | 91%
Class D | -0.01% | -0.03% | 0.03% | 112% | 93%
Class F | -0.33% | -0.13% | -0.15% | 110% | 90%
TGM | -0.18% | -0.12% | -0.13% | 112% | 93%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.02% | 0.03% | 0.00% | 113% | 97%
Class C | 0.00% | 0.00% | -0.02% | 113% | 97%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.01% | -0.01% | 0.01% | 112% | 96%
Class F | -0.58% | -0.21% | -0.09% | 107% | 87%
TGM | -0.17% | -0.15% | -0.15% | 101% | 83%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.02% | -0.01% | 98% | 88%
Class C | 0.00% | 0.01% | 0.01% | 102% | 91%
Class E | -0.01% | -0.01% | 0.00% | 103% | 90%
Overall | 0.00% | 0.01% | 0.00% | 101% | 90%
Class D | 0.00% | 0.00% | 0.00% | 89% | 85%
Class F | -0.21% | -0.22% | -0.28% | 101% | 79%
TGM | -0.15% | -0.23% | -0.18% | 102% | 73%

## Slide 8: JVET-P0402-Test2: LowQP results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.03% | -0.04% | 91% | 84%
Class A2 | -0.01% | 0.00% | 0.01% | 86% | 83%
Class B | -0.01% | -0.01% | 0.02% | 87% | 81%
Class C | 0.00% | 0.00% | 0.01% | 82% | 80%
Class E | -0.03% | -0.03% | -0.03% | 86% | 80%
Overall | -0.01% | -0.01% | 0.00% | 86% | 81%
Class D | 0.00% | -0.02% | -0.02% | 88% | 85%
Class F | -0.18% | -0.12% | -0.13% | 82% | 78%
TGM | -0.11% | -0.09% | -0.08% | 93% | 83%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.02% | 0.03% | 0.00% | 95% | 88%
Class C | 0.01% | 0.02% | 0.00% | 93% | 87%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | -0.07% | 0.04% | 93% | 87%
Class F | -0.35% | -0.15% | -0.10% | 87% | 77%
TGM | -0.14% | -0.12% | -0.10% | 89% | 77%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.00% | -0.02% | 87% | 80%
Class C | -0.01% | -0.01% | 0.02% | 88% | 83%
Class E | -0.02% | 0.00% | 0.03% | 99% | 89%
Overall | -0.01% | 0.00% | 0.00% | 90% | 83%
Class D | 0.01% | 0.01% | 0.00% | 88% | 85%
Class F | -0.17% | -0.25% | -0.19% | 85% | 72%
TGM | -0.11% | -0.19% | -0.16% | 85% | 65%

## Slide 9: JVET-P0402-Test1 CTC bin2bit results

## Slide 10: JVET-P0402-Test1 LowQP bin2bit results

## Slide 11: JVET-P0402-Test2 CTC bin2bit results

## Slide 12: JVET-P0402-Test2 LowQP bin2bit results

## Slide 13: Conclusion
In TS residual coding, it is proposed to
  Assign 1.75 bin/coefficient at TB-level;
  Exclude coeff_sign_flag from CCB count;
  Based on the above proposals, set another CCB_SIGN limit for coeff_sign_flag
Unify the CCB count method between transform residual and TS residual coding
Performance:
  There are some gains in Class F and TGM screen content sequences, especially under Low QP conditions
  No coding losses in all classes by this unification

## Slide 14: Thanks Qualcomm’s cross-checking!