## Slide 1: JVET-P0406: Non-CE3: Generalization of SCIPU for different YUV formats
L. Pham Van, G. Van der Auwera, V. Seregin, H. Huang,
A. K. Ramasubramonian, M. Karczewicz
@qualcomm
10/2019
AV

## Slide 2: Content
SCIPU constraint in VD6 of VVC
Problem
Solution
Experimental results
Conclusion

## Slide 3: SCIPU constraint in VD6 of VVC
area == 64 && split == QT?
area == 64 && split == TT_V || split == TT_H
0
1
area = w * h in luma samples
1
1
area == 32 && split == BT_V || split == BT_H?
1
area == 64 && split == BT_V || split == BT_H
slice == intra?
1
2
area == 128 && split == TT_V || split == TT_H
0
0
1
2
No SCIPU restriction
Inferred intra SCIPU without signaling
Inter or intra SCIPU and 1 flag is signaled
0
0
0
0
0
1
1
1
1
1

## Slide 4: Problem: SCIPU constraint derivation works correctly only YUV 4:2:0
2x2/2x4/4x2 chroma blocks do not exist in YUV 4:0:0 and YUV 4:4:4
 No need SCIPU constraint
Some cases, 2x2/2x4/4x2 occurs in YUV 4:2:0 but not in YUV 4:2:2
No SCIPU restriction in these coding trees for YUV 4:2:2

## Slide 5: Proposed fix
Disable SCIPU constraint in YUV 4:0:0 and YUV 4:4:4
In YUV 4:2:2, remove SCIPU restriction in coding trees where there is no 2x2/2x4/4x2 blocks
  Method 1: Using chroma scaling factors in SCIPU constraint derivation
  Method 2: Use chroma block size in SCIPU constraint derivation

## Slide 6: Proposed method 2: Use chroma size base on luma split
minL = w*h
if split == BT_H or BT_V, minL = minL >>1
Else if split = TT_H or TT_V or QT, minL = minL >>2
sclX, sclY is the chroma scaling factors
minL >> (sclX + sclY) >=16 || 4:4:4 || 4:0:0?
0
1
slice == intra or minL <=16
1
1
2
0
0

## Slide 7: Experimental results
Thank Bytedance for cross-check!
RA CTC condition, QP = {22, 27, 32, 37}
8 YUV 4:2:2 sequences are tested
Sequence | Frame rate | #Frame | Intra period
Traffic | 30 | 150 | 32
Seeking | 50 | 500 | 48
Kimono | 24 | 240 | 32
EBUKidsSoccer | 50 | 500 | 48
EBUHorse | 50 | 500 | 48
EBUGraphics | 50 | 500 | 48
DucksAndLegs | 60 | 600 | 64
CrowdRun | 50 | 500 | 48
Sequence | Random Access Main 10 (Over VTM-6.0) |  |  |  | 
 | Y | U | V | EncT | DecT
Traffic | -0.08% | -0.08% | -0.02% | 99% | 100%
Seeking | -0.12% | -0.99% | -0.49% | 99% | 100%
Kimono | -0.05% | -0.10% | -0.04% | 101% | 101%
EBUKidsSoccer | -0.05% | -0.07% | -0.08% | 99% | 100%
EBUHorse | -0.10% | -0.20% | -0.22% | 100% | 99%
EBUGraphics | -0.81% | -1.05% | -0.98% | 100% | 100%
DucksAndLegs | -0.10% | -0.10% | -0.25% | 99% | 100%
CrowdRun | -0.37% | -1.16% | -1.08% | 98% | 102%
Average | -0.21% | -0.47% | -0.40% | 99% | 100%

## Slide 8: Conclusions
Proposed techniques to fix a bug for local dual tree
It is recommended to adopt the proposed method 2 into the next version of VTM:
  Clean design and clean specification text