## Slide 1: JVET-P0427 AHG17: Bugfixes on constant slice header parameters
​Yao-Jen Chang, Vadim Seregin, Muhammed Coban, Adarsh Ramasubramonian, Marta Karczewicz
​
​Geneva, CH
​Oct. 2019

## Slide 2: Background on constant flag in PPS
constant_slice_header_params_enabled_flag (O0238)
  Syntax element can be either signaled in PPS or slice header
    If pps_six_minus_max_num_merge_cand_plus1 = 0, slice_six_minus_max_num_merge_cand is signaled in slice header
    Otherwise, pps_six_minus_max_num_merge_cand_plus1 > 0, then slice_six_minus_max_num_merge_cand is NOT signaled in slice header

## Slide 3: Issue
Current spec:
  PPS: pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1 shall be in the range of 0 to MaxNumMergeCand – 1, inclusive
  Slice header: slice_max_num_merge_cand_minus_max_num_triangle_cand shall be in the range of 0 to MaxNumMergeCand – 2, inclusive
    MaxNumMergeCand = 6 − six_minus_max_num_merge_cand
    MaxNumTriangleMergeCand = MaxNumMergeCand − slice_max_num_merge_cand_minus_max_num_triangle_cand
MaxNumMergeCand is a variable derived in different slice headers by slice_six_minus_max_num_merge_cand

## Slide 4: Bugfixes
The range of pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1 is changed to “0 to PpsMaxNumMergeCand – 1”
  PpsMaxNumMergeCand = 6 – ( pps_six_minus_max_num_merge_cand_plus1 – 1 )
Derive MaxNumMergeCand and MaxNumTriangleMergeCand together in either PPS or slice header.