## Slide 1: JVET-P0443 non-CE4 On DMVR early termination
G. Li, X. Li, X. Xu, S. Liu
2019/10

## Slide 2: Introduction
Early termination is used for DMVR
SAD of the initial MV pair is first calculated and reduced by 1/4
If reduced SAD of the initial MV pair is smaller than a threshold, early stop is triggered
  SAD < sbWidth * sbHeight

## Slide 3: Proposed Method
In addition to MV(0, 0), utilize left and above neighboring sub-PU’s MV offset for early stop
Early termination condition:
  minSAD * 5 / 8 < sbWidth * sbHeight

## Slide 4: Simulation results
Anchor: VTM-6.0
 |  |  | RA |  |  | 
 |  |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT | DMVR Time
Class A1 | 0.04% | 0.03% | 0.02% | 100% | 99% | 98%
Class A2 | 0.04% | 0.08% | 0.10% | 100% | 100% | 98%
Class B | 0.03% | 0.09% | 0.07% | 100% | 100% | 97%
Class C | 0.02% | 0.06% | 0.00% | 100% | 100% | 93%
Class E |  |  |  |  |  | 
Overall | 0.03% | 0.07% | 0.05% | 100% | 100% | 96%
Class D | 0.06% | 0.06% | 0.01% | 100% | 100% | 98%
Class F | 0.03% | 0.06% | 0.02% | 100% | 100% | 96%

## Slide 5: Conclusion
The proposed method has BD-rate change of 0.03% on RA
DMVR module’s processing time reduced by 4%.
Thanks to Kwai for crosschecking!

## Slide 6
Thank you!