## Slide 1
CE4-related:
Thin Partition Mode
JVET-P0449

## Slide 2: TPM (Triangle Partition Mode)
One of merge modes
  Use neighbors MV, no further refinement
Partition CU into two triangles
  2 options; diagonal split or anti-diagonal split
  Uni-prediction used for each partition
Blending of two triangles around triangle split
  Bi-prediction with MV from both triangles for those pixels
MV storage for future AMVP, TMVP

## Slide 3: Motivation
Blending effect for 4xN TPM 45- and 135- degree splits are similar (same for Nx4 TPM)
  Not efficient use of split direction flag
Blending weight calculation is a complex task due to irregular weight pattern
  SIMD implementation requires weight LUT
LUT to store blending weights for 4xN and Nx4 TPM
  4*(8+16+32+64+128)*2*4 = 3968 bits for luma
  2*(4+8+16+32+64)*2*4 = 1984 bits for chroma

## Slide 4: Thin Partition Mode
Similar to TPM
Partition CU into two rectangles
  One way to split CU; either Horizontal or vertical split, depending on CU dimension
  Uni-prediction used for each partition
Blending of two rectangles around partition split
  Bi-prediction with MV from both rectangles for those pixels
MV storage for future AMVP, TMVP

## Slide 5: Proposed Changes
Replace TPM partitions with Thin partitions for 4xN and Nx4 size CU
  Keep TPM partitions for other CU sizes unchanged
Use current TPM syntax
  Not signal split direction for 4xN and Nx4 CU
  Split 4xN CU into two 2xN thin partitions
  Split Nx4 CU into two Nx2 thin partitions
New Blending weights
  [7/8 5/8 3/8 1/8] for luma and [5/8 3/8] for chroma
Use MV of the second partition of a CU for MV context storage

## Slide 6: Proposed Adaptive TPM/Thin for Different CU Sizes
Width/ Height | 4 | 8 | 16 | 32 | 64 | 128
4 | N/A | N/A | Thin | Thin | Thin | Thin
8 | N/A | TPM | TPM | TPM | TPM | TPM
16 | Thin | TPM | TPM | TPM | TPM | TPM
32 | Thin | TPM | TPM | TPM | TPM | TPM
64 | Thin | TPM | TPM | TPM | TPM | TPM
128 | Thin | TPM | TPM | TPM | TPM | TPM

## Slide 7: Simulation Results
With SIMD implementation (O0280)
Thanks to Broadcom for crosschecking (P0779)

## Slide 8: Simulation Results
With SIMD implementation (O0280)
Thanks to Broadcom for crosschecking (P0779)

## Slide 9: Conclusions
Simplify TPM for 4xN and Nx4 CU by allowing one split direction
Simplify blending operation with regular weights
Simplify MV context storage by only storing MV of second partition
Simplify mode decision since only one split direction is tested
No coding performance impact
No conflict with GEO since GEO is not used for 4xN and Nx4 CU

## Slide 11: Simulation Results
With CE4_1_2_REDUCED_TO_64 enabled