## Slide 1: JVET-P0504 CE5-related: Harmonization of Hadamard filter, SAO and ALF
V. Stepin, S. Ikonin, A. Karabutov, S. Nikolaeva

## Slide 2
From CE5 result it can be concluded that coding gain of SAO and ALF is significantly overlapped.
At the same time, for low complexity configuration when ALF is off SAO provides significant gain
It is proposed:
Use Hadamard filter when ALF is enabled instead of SAO since it provides additional coding gain
Use combination of SAO and Hadamard filter when ALF is disabled since this combination provides substantial coding gain
Introduction

## Slide 3
Proposed loop filters configuration when ALF is ON
HTDF
DBF
ALF

## Slide 4
Proposed loop filters configuration when ALF is ON
Anchor: VTM6.0
 | All Intra |  |  |  |  | Random Access |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO tool-off (CE5-3.3.2) | 0.01% | 0.14% | 0.17% | 100%* | 99%* | 0.08% | 0.28% | 0.35% | 100%* | 98%*
HTDF (CE5-3.2.2, no SAO) | -0.42% | 0.53% | 0.53% | 107% | 103% | -0.38% | 0.39% | 0.51% | 104% | 100%
 | Low Delay B |  |  |  |  | Low Delay P |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO tool-off (CE5-3.3.2) | 0.07% | 0.58% | 1.24% | 101%* | 101%* | 0.14% | 0.41% | 1.14% | 100%* | 100%
HTDF (CE5-3.2.2, no SAO) | -0.17% | 1.05% | 1.54% | 102% | 99% | -0.19% | 1.00% | 1.77% | 104% | 99%

## Slide 5
Proposed loop filters configuration when ALF is OFF
Option 1
Option 2

## Slide 6
Proposed loop filters configuration when ALF is OFF
Anchor: VTM6.0.noSAO.noALF
 | All Intra |  |  |  |  | Random Access |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO (CE5-3.3.2) | -0.32% | -0.37% | -0.70% | 100% | 104% | -0.79% | -0.80% | -0.72% | 100% | 102%
HTDF (CE5-3.2.2) | -0.93% | 0.43% | 0.41% | 108% | 107% | -1.35% | 0.10% | 0.13% | 104% | 103%
SAO + HTDF parallel | -0.99% | 0.23% | 0.08% | 109% | 111% | -1.50% | -0.22% | -0.23% | 104% | 107%
SAO + HTDF sequential | -1.02% | -0.02% | -0.37% | 108% | 109% | -1.64% | -0.72% | -0.64% | 103% | 104%
 | Low Delay B |  |  |  |  | Low Delay P |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO (CE5-3.3.2) | -0.95% | -1.71% | -2.82% | 100% | 102% | -2.59% | -3.06% | -3.65% | 100% | 102%
HTDF (CE5-3.2.2) | -1.34% | 1.00% | 0.83% | 102% | 102% | -2.65% | 0.71% | 1.10% | 104% | 103%
SAO + HTDF parallel | -1.49% | -0.11% | -1.01% | 102% | 106% | -3.27% | -1.08% | -1.59% | 104% | 107%
SAO + HTDF sequential | -1.59% | -1.04% | -2.25% | 102% | 104% | -3.48% | -2.22% | -2.88% | 104% | 104%

## Slide 7
Acknowledgment
Thanks Ericsson for cross-checking!
(JVET-P1011)