## Slide 1
JVET-P0516
Non-CE8: On palette mode signaling binarization
Yi-Wen Chen

## Slide 2: Introduction
The PLT mode flag is signaled when the pred_mode_flag is signaled as 1 which implies the current CU is intra mode alike
One exception breaks the physical meaning of pred_mode_flag and complicates the signaling conditions of PLT mode flag:
Pred_Modes | pred_mode_flag | pred_mode_ibc_flag | pred_mode_plt_flag
INTER | 0 | - | 0
PLT | 0 | - | 1
INTRA | 1 | - | -

## Slide 3: Proposed Fix
Proposed to signal pred_mode_plt_flag when pred_mode_flag is signaled as 1 under all conditions
The re-designed codeword (when IBC is not allowed):
Signaling conditions of PLT mode flag is simplified:
Pred_Modes | pred_mode_flag | pred_mode_ibc_flag | pred_mode_plt_flag
INTER | 0 | - | -
PLT | 1 | - | 1
INTRA | 1 | - | 0
if( ( ( ( slice_type = = I ¦ ¦ ( cbWidth = = 4 && cbHeight = = 4 ) ¦ ¦ sps_ibc_enabled_flag ) && CuPredMode[ x0 ][ y0 ] = = MODE_INTRA ) ¦ ¦ ( slice_type != I && !( cbWidth = = 4 && cbHeight = = 4 ) && !sps_ibc_enabled_flag && CuPredMode[ x0 ][ y0 ] != MODE_INTRA ) ) && sps_palette_enabled_flag && cbWidth <= 64 && cbHeight <= 64 && cu_skip_flag[ x0 ][ y0 ] = = 0 && modeType != MODE_INTER ) | 
pred_mode_plt_flag | ae(v)

## Slide 4: Simulation Results
Anchor :VTM-6.0 (IBC=0)
Test: Anchor + proposed fix
(DualITree = 0)
(DualITree = 1)

## Slide 5: Summary
Propose to fix the un-aligned codewords design of PLT mode
  Fix the physical meaning of prediction mode flag (e.g. 0inter, 1intra)
  Simplify the signaling condition of PLT flag
  Negligible coding performance (minor coding gain)
Thanks for Qualcomm being our cross-checker

## Slide 6: Thank you