## Slide 1
JVET-P0562
Non-CE8: Transform skip residual coding simplification
Yi-Wen Chen, Xiaoyu Xiu, Xianglin Wang and et al.

## Slide 2: Introduction
In TS residual coding, per-sample adaptive codewords (Golomb Rice) is used for the coding of the level remainder
  The rice parameter is derived from the neighbouring levels (locSumAbs)
Proposed methods to replace per-sample adaptive codewords
  Fixed codeword (rice parameter is fixed as K)
  CU-level adaptive codeword (rice parameter is determined by the CU QP)

## Slide 3
Anchor :VTM-6.0
 |  | Standard QPs (22, 27, 32, 37) |  |  | Low QPs (2, 7, 12, 17) |  | 
 |  | AI | RA | LDB | AI | RA | LDB
Fix Rice Parameter (K=1) | F | 0.00% | -0.07% | 0.09% | 0.02% | 0.01% | 0.04%
 | TGM | 0.02% | -0.02% | -0.06% | -0.37% | 0.08% | -0.19%
Fix Rice Parameter (K=2) | F | 0.09% | 0.07% | 0.13% | -0.65% | -0.64% | -0.47%
 | TGM | 0.25% | 0.11% | 0.03% | -2.15% | -1.81% | -1.35%
 |  | Standard QPs (22, 27, 32, 37) |  |  | Low QPs (2, 7, 12, 17) |  | 
 |  | AI | RA | LDB | AI | RA | LDB
Fix Rice Parameter (K=1) + CE7-1.3b* | F | 0.32% | 0.23% | - | -0.21% | -0.02% | -0.16%
 | TGM | 0.68% | 0.38% | - | -0.68% | -0.31% | -0.04%
Fix Rice Parameter (K=2) + CE7-1.3b* | F | 0.61% | 0.50% | - | -0.29% | -0.11% | -0.14%
 | TGM | 1.41% | 0.76% | - | -2.36% | -1.91% | -0.96%
 |  | Standard QPs (22, 27, 32, 37) |  |  | Low QPs (2, 7, 12, 17) |  | 
 |  | AI | RA | LDB | AI | RA | LDB
CE7-1.3b* | F | 0.12% | 0.11% | 0.14% | -1.08% | -1.23% | -0.44%
 | TGM | 0.33% | 0.18% | -0.02% | -1.16% | -1.67% | -0.74%

## Slide 4: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=1)
(Standard QPs)
(Low QPs)

## Slide 5: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=2)
(Standard QPs)
(Low QPs)

## Slide 6: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=1) + CE7-1.3b*
(Standard QPs)
(Low QPs)

## Slide 7: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=2) + CE7-1.3b*
(Standard QPs)
(Low QPs)

## Slide 8: Summary
Proposed methods to replace per-sample adaptive codewords for the coding of level remainder in TS residual coding
  Fixed codeword (rice parameter is fixed as K)
  CU-level adaptive codeword (rice parameter is determined by the CU QP)
Recommend to adopt the proposed fixed codeword into VVC
Thanks for Tencent (P0642) and Alibaba (P1003) being our cross-checker

## Slide 9: Thank you
Standard QPs (22, 27, 32, 37)

## Slide 10
Rice Parameter deriviation in VTM6.0