## Slide 1: JVET-P0566 CE6-related: On LFNST Support Patterns
Hilmi E. Egilmez, Amir Said, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
CE6-2.3a (JVET-P0065) replacing the L-shaped pattern for 8x8 LFNSTs
CE test: Two separate patterns with 36 samples are used.
This contribution: proposes two alternatives using a single pattern.
lfnst_idx =1
lfnst_idx =2
VTM-6.0: 8x8 LFNST

## Slide 3: Proposed Method 1
6x6 square pattern 36 samples (as in CE6-2.3a)
  Reduces the number of multiplications
  Reduces memory requirements 8KB  6.7KB
6x6 square pattern
Replace L-shaped design with 6x6 square pattern for 8x8 LFNST
VTM-6.0: 8x8 LFNST

## Slide 4: Proposed Method 2
Circular pattern has 48 samples (as in VTM-6.0)
  Same number of multiplications and memory requirements
  Provides support for mid-range coefficients
Replace L-shaped design with a circular pattern for 8x8 LFNST
VTM-6.0: 8x8 LFNST
Circular pattern with 48 samples

## Slide 5: Results
Both 4x4 and 8x8 matrices are optimized
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.09% | 0.22% | 0.37% | 100% | 100%
Class A2 | 0.00% | 0.14% | 0.08% | 101% | 101%
Class B | -0.01% | 0.12% | 0.11% | 100% | 100%
Class C | -0.07% | -0.11% | 0.01% | 101% | 102%
Class E | -0.05% | 0.10% | 0.08% | 101% | 101%
Overall | -0.01% | 0.09% | 0.12% | 101% | 101%
Class D | -0.04% | 0.10% | 0.03% | 100% | 100%
Class F | -0.09% | 0.04% | 0.02% | 100% | 99%
 | Random Access |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.08% | 0.11% | 0.18% | 100% | 100%
0.04% | 0.13% | 0.03% | 101% | 102%
-0.02% | 0.07% | -0.02% | 100% | 100%
-0.04% | -0.01% | 0.13% | 101% | 102%
0.00% | 0.07% | 0.07% | 101% | 101%
-0.07% | -0.22% | -0.05% | 100% | 100%
0.01% | 0.00% | -0.02% | 100% | 100%
6x6 square pattern
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | 0.13% | 0.18% | 100% | 100%
Class A2 | -0.06% | 0.10% | 0.00% | 101% | 101%
Class B | -0.07% | 0.12% | 0.10% | 100% | 99%
Class C | -0.12% | -0.09% | 0.04% | 101% | 105%
Class E | -0.12% | 0.02% | 0.01% | 101% | 101%
Overall | -0.09% | 0.06% | 0.07% | 101% | 101%
Class D | -0.09% | -0.01% | -0.08% | 101% | 100%
Class F | -0.09% | -0.06% | -0.14% | 100% | 100%
 | Random Access |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.04% | 0.08% | 0.13% | 100% | 100%
0.00% | 0.09% | 0.06% | 101% | 102%
-0.05% | 0.06% | 0.12% | 100% | 101%
-0.06% | 0.02% | 0.12% | 102% | 103%
-0.04% | 0.06% | 0.11% | 101% | 101%
-0.06% | 0.00% | -0.14% | 101% | 101%
-0.09% | -0.16% | 0.04% | 100% | 100%
Circular pattern with 48 samples

## Slide 6: Results
Only 8x8 matrices are optimized
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.09% | 0.28% | 0.31% | 100% | 103%
Class A2 | 0.02% | 0.02% | 0.02% | 101% | 100%
Class B | 0.02% | 0.13% | 0.12% | 100% | 99%
Class C | 0.01% | -0.04% | 0.10% | 100% | 101%
Class E | 0.02% | 0.15% | 0.08% | 101% | 100%
Overall | 0.03% | 0.10% | 0.12% | 100% | 100%
Class D | 0.00% | 0.10% | -0.02% | 100% | 99%
Class F | 0.01% | -0.04% | -0.10% | 100% | 101%
 | Random Access |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.06% | 0.22% | 0.27% | 101% | 100%
0.03% | 0.17% | 0.17% | 101% | 101%
-0.01% | 0.15% | -0.02% | 100% | 100%
0.02% | 0.06% | -0.05% | 101% | 102%
0.02% | 0.14% | 0.07% | 101% | 101%
-0.03% | -0.23% | 0.09% | 100% | 99%
0.00% | -0.08% | 0.07% | 100% | 100%
6x6 square pattern
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | 0.05% | 0.21% | 100% | 100%
Class A2 | -0.03% | 0.07% | -0.05% | 100% | 100%
Class B | -0.05% | 0.08% | 0.07% | 100% | 100%
Class C | -0.03% | -0.09% | 0.01% | 101% | 103%
Class E | -0.05% | 0.10% | 0.09% | 101% | 98%
Overall | -0.05% | 0.04% | 0.06% | 100% | 100%
Class D | -0.02% | 0.09% | -0.10% | 100% | 100%
Class F | -0.04% | -0.10% | -0.11% | 100% | 98%
 | Random Access |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.04% | 0.07% | 0.12% | 100% | 100%
0.02% | 0.07% | -0.01% | 100% | 100%
-0.03% | 0.12% | 0.05% | 100% | 101%
-0.01% | 0.08% | 0.09% | 100% | 101%
-0.02% | 0.09% | 0.06% | 100% | 100%
-0.04% | -0.27% | 0.03% | 100% | 100%
-0.01% | -0.06% | 0.06% | 100% | 100%
Circular pattern with 48 samples

## Slide 7: Conclusions
Proposed two alternatives for LFNST support pattern shape
Method 1:
Method 2:
Recommendation: to adopt one of the proposed methods or further study in a CE.
Cross-checker: Jonathan Gan (Canon)
6x6 square pattern
VTM-6.0: 8x8 LFNST
VTM-6.0: 8x8 LFNST
Circular pattern with 48 samples