## Slide 1: JVET-P0599 Non-CE3: Cleanup of interpolation filtering for intra prediction
Alexey Filippov
Vasily Rufitskiy

## Slide 2: Motivation
This contribution is an update of JVET-M0158 “Non-CE3: LUT-free interpolation filters for intra prediction”
No difference in coding efficiency was shown. This could be kept in mind in further work, but there didn’t seem to be a need to consider this change at this stage. It was remarked that these proposals may be logical, but we don’t need to consider such a small change before the design is more mature.
Jan 2019, JVET-M_Notes_dH

## Slide 3: Frequency responses of smoothing interpolation filters
Current “Gaussian” filters in VTM 6.0
Proposed filters
Fractional sample position p | fG interpolation filter coefficients |  |  | 
 | fG0 | fG1 | fG2 | fG3
0 | 16 | 32 | 16 | 0
1 | 15 | 29 | 17 | 3
2 | 15 | 29 | 17 | 3
3 | 14 | 29 | 18 | 3
4 | 13 | 29 | 18 | 4
5 | 13 | 28 | 19 | 4
6 | 13 | 28 | 19 | 4
7 | 12 | 28 | 20 | 4
Fractional sample position p | fG interpolation filter coefficients |  |  | 
 | fG0 | fG1 | fG2 | fG3
8 | 11 | 28 | 20 | 5
9 | 11 | 27 | 21 | 5
10 | 10 | 27 | 22 | 5
11 | 9 | 27 | 22 | 6
12 | 9 | 26 | 23 | 6
13 | 9 | 26 | 23 | 6
14 | 8 | 25 | 24 | 7
15 | 8 | 25 | 24 | 7
16 | 8 | 24 | 24 | 8
Fractional sample position p | fG interpolation filter coefficients |  |  | 
 | fG0 | fG1 | fG2 | fG3
0 | 16 | 32 | 16 | 0
1 | 16 | 32 | 16 | 0
2 | 15 | 31 | 17 | 1
3 | 15 | 31 | 17 | 1
4 | 14 | 30 | 18 | 2
5 | 14 | 30 | 18 | 2
6 | 13 | 29 | 19 | 3
7 | 13 | 29 | 19 | 3
Fractional sample position p | fG interpolation filter coefficients |  |  | 
 | fG0 | fG1 | fG2 | fG3
8 | 12 | 28 | 20 | 4
9 | 12 | 28 | 20 | 4
10 | 11 | 27 | 21 | 5
11 | 11 | 27 | 21 | 5
12 | 10 | 26 | 22 | 6
13 | 10 | 26 | 22 | 6
14 | 9 | 25 | 23 | 7
15 | 9 | 25 | 23 | 7
16 | 8 | 24 | 24 | 8

## Slide 4: Frequency responses of
[1,2,1] filter in VTM 6.0
Current “Gaussian” filters in VTM-6.0
Proposed filter

## Slide 5: Magnitude and phase responses
VTM-6.0 “Gaussian”filter
the proposed filter
Fractional sample positions p:
4, 8, and 11
Fractional sample position p | Gaussian filter |  |  |  | Smoothing filter |  |  | 
 | fG[p][0] | fG[p][1] | fG[p][2] | fG[p][3] | fG[p][0] | fG[p][1] | fG[p][2] | fG[p][3]
4 | 13 | 29 | 18 | 4 | 14 | 30 | 18 | 2
8 | 11 | 28 | 20 | 5 | 12 | 28 | 20 | 4
11 | 9 | 27 | 22 | 6 | 11 | 27 | 21 | 5

## Slide 6: Comparison of predicted blocks
mode 14 (HOR_IDX-4)
intraPredAng=4
Current “Gaussian” filters in VTM-6.0
Proposed filter

## Slide 7: Mode=15
Current “Gaussian” filters in VTM-6.0
Proposed filter

## Slide 8: Mode=14
Current “Gaussian” filters in VTM-6.0
Proposed filter

## Slide 9: Mode=13
Current “Gaussian” filters in VTM-6.0
Proposed filter

## Slide 10: CTC results
 | All Intra |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.02% | -0.01% | 100% | 100%
Class A2 | 0.00% | 0.01% | -0.04% | 100% | 100%
Class B | 0.00% | 0.00% | -0.03% | 100% | 100%
Class C | 0.01% | -0.07% | 0.06% | 100% | 100%
Class E | -0.01% | -0.02% | -0.05% | 100% | 100%
Overall | 0.00% | -0.02% | -0.01% | 100% | 100%
Class D | 0.00% | 0.01% | -0.10% | 100% | 100%
Class F | -0.02% | 0.00% | -0.08% | 100% | 100%
 | Random Access |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.07% | -0.04% | 100% | 100%
Class A2 | 0.02% | 0.02% | -0.05% | 100% | 100%
Class B | -0.04% | 0.06% | 0.03% | 100% | 100%
Class C | -0.04% | 0.13% | -0.02% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.07% | -0.01% | 100% | 100%
Class D | -0.01% | -0.29% | -0.02% | 100% | 100%
Class F | 0.00% | -0.17% | 0.02% | 100% | 100%

## Slide 11: DCT-IF filter disabled
Anchor: Gaussian interpolation filter
Test: Smoothing interpolation filter
 | All Intra |  |  |  | 
 | Over VTM6.0 without DCTIF intra interpolation |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.10% | -0.06% | 100% | 100%
Class A2 | -0.06% | 0.01% | -0.05% | 100% | 100%
Class B | -0.07% | -0.12% | -0.05% | 100% | 100%
Class C | -0.05% | 0.01% | 0.06% | 100% | 100%
Class E | -0.09% | -0.10% | -0.05% | 100% | 100%
Overall | -0.06% | -0.06% | -0.03% | 100% | 100%
Class D | -0.04% | -0.01% | -0.07% | 100% | 100%
Class F | -0.02% | 0.02% | 0.09% | 100% | 101%
 | Random Access |  |  |  | 
 | Over VTM6.0 without DCTIF intra interpolation |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | 0.06% | 0.02% | 100% | 100%
Class A2 | -0.06% | -0.20% | -0.07% | 100% | 100%
Class B | -0.04% | 0.05% | -0.13% | 100% | 100%
Class C | -0.01% | -0.08% | -0.06% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.03% | -0.03% | -0.07% | 100% | 100%
Class D | -0.02% | 0.20% | 0.20% | 100% | 100%
Class F | -0.03% | 0.10% | -0.07% | 100% | 100%

## Slide 12: Examples

## Slide 13: Example 1
Scenario: FourPeople @ qp37, POC=8 (CTC coded POC=1 for AI)
FourPeople original

## Slide 14
Original Picture

## Slide 15
VTM6.0 stream
VTM6.0 decoder

## Slide 16
VTM6.0 stream
VTM6.0 decoder (no markup)

## Slide 17
Synthetic test
Synthetic test
Decoded picture

## Slide 20: Example 2
FourPeople @ qp27, POC=24 (CTC coded POC=3 for AI)
FourPeople original

## Slide 21
Original Picture

## Slide 22
Stream with Gauss filter forced
decoder with Gauss filter forced

## Slide 23
Stream with Gauss filter forced
decoder with Smoothing filter forced

## Slide 26: Example 3
Catrobot @ qp42, POC=96 (CTC coded POC=12 for AI)

## Slide 27
VTM6.0 stream
VTM6.0 decoder

## Slide 28
Mode 15
Synthetic test
Synthetic test
Decoded picture

## Slide 30: Example 4
RitualDance@qp37, POC=192 (CTC coded POC=24 for AI)

## Slide 31
VTM6.0 stream
VTM6.0 decoder

## Slide 32
Mode 21
Synthetic test
Decoded picture