## Slide 1: JVET-P0604 Non-CE4: Motion field storage optimization for the line buffer
Timofey Solovyev
Sergey Ikonin
Alexander Karabutov
Chernyak Roman

## Slide 2: Motion information storage in line buffer
miK
mi3
mi2
mi1
4
CTU00
CTU01
CTU10
CTU11
CTU boundary
Picture width
…
CTU0N
CTU1N
…

## Slide 3: Motion information stored for each 4 pixels in a line
Element | Number of bits
MV0 | 2*18 = 36
MV1 | 2*18 = 36
refIdx0 | 4
refIdx1 | 4
Total | 80
Resolution | Line memory usage
HD | 4800 bytes
4K | 10 Kbytes
8K | 20 Kbytes
The total line memory consumption is (pic_width / 4) * 10 bytes
Motion information storage in line buffer

## Slide 4
4
8
Motion field
Motion field stored in line buffer
Skipped motion information units
Motion information units stored in line buffer
8 pixel grid usage for motion information storage

## Slide 5
Total line memory saving is (pic_width / 8) * 10 bytes
Line memory saving
Resolution | Line memory usage VTM 6.0 | Line memory usage with P0604 | Line memory saving
HD | 4800 bytes | 2400 bytes | 2400 bytes
4K | 10 Kbytes | 5 Kbytes | 5 Kbytes
8K | 20 Kbytes | 10 Kbytes | 10 Kbytes

## Slide 6: Simulation results

## Slide 7: Conclusion
Motion info storage optimization is proposed
5 Kbytes saved for 4K, 10Kbytes for 8K
Performance changes: 0.01% for RA

## Slide 8: Thanks HHI for crosschecking!

## Slide 10: Per sequence results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Tango2 | -0.01% | 0.27% | 0.13% | 102% | 102%
FoodMarket4 | -0.03% | 0.19% | -0.14% | 102% | 102%
CampfireParty2 | 0.02% | -0.04% | 0.01% | 102% | 102%
CatRobot1 | 0.06% | 0.15% | -0.05% | 102% | 102%
DaylightRoad2 | 0.07% | 0.09% | 0.16% | 102% | 101%
ParkRunning3 | 0.04% | 0.03% | 0.04% | 102% | 102%
MarketPlace | 0.01% | 0.09% | 0.05% | 102% | 102%
RitualDance | 0.03% | -0.02% | -0.20% | 102% | 102%
Cactus | -0.04% | 0.11% | -0.16% | 102% | 102%
BasketballDrive | 0.02% | 0.12% | 0.29% | 102% | 102%
BQTerrace | 0.00% | 0.02% | -0.07% | 102% | 102%
BasketballDrill | 0.04% | 0.02% | 0.08% | 103% | 104%
BQMall | 0.00% | 0.15% | -0.10% | 102% | 104%
PartyScene | -0.03% | -0.14% | -0.08% | 103% | 104%
RaceHorses | 0.02% | 0.13% | -0.03% | 103% | 105%
BasketballPass | 0.01% | 0.08% | -0.01% | 103% | 105%
BQSquare | -0.05% | 0.13% | 0.08% | 103% | 105%
BlowingBubbles | -0.06% | -0.40% | -0.03% | 102% | 106%
RaceHorses | -0.01% | -0.11% | 0.16% | 103% | 107%
FourPeople |  |  |  |  | 
Johnny |  |  |  |  | 
KristenAndSara |  |  |  |  | 
Class A1 | -0.01% | 0.14% | 0.00% | 102% | 102%
Class A2 | 0.05% | 0.09% | 0.05% | 102% | 102%
Class B | 0.00% | 0.06% | -0.02% | 102% | 102%
Class C | 0.01% | 0.04% | -0.03% | 103% | 104%
Class E |  |  |  |  | 
Overall | 0.01% | 0.08% | 0.00% | 102% | 103%
Class D | -0.03% | -0.08% | 0.05% | 102% | 106%
Class F (optional) | 0.01% | 0.06% | -0.01% | 103% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Tango2 |  |  |  |  | 
FoodMarket4 |  |  |  |  | 
CampfireParty2 |  |  |  |  | 
CatRobot1 |  |  |  |  | 
DaylightRoad2 |  |  |  |  | 
ParkRunning3 |  |  |  |  | 
MarketPlace | -0.05% | -0.14% | -0.24% | 102% | 103%
RitualDance | 0.02% | -0.05% | 0.09% | 102% | 102%
Cactus | -0.06% | 0.26% | 0.18% | 101% | 102%
BasketballDrive | #VALUE! | #VALUE! | #VALUE! | ####### | #######
BQTerrace | 0.01% | 0.24% | -0.68% | 102% | 104%
BasketballDrill | -0.11% | 0.05% | -0.02% | 102% | 102%
BQMall | -0.05% | 0.13% | 0.23% | 102% | 103%
PartyScene | -0.05% | 0.27% | -0.05% | 101% | 102%
RaceHorses | 0.07% | 0.02% | 0.01% | 101% | 103%
BasketballPass | -0.08% | -0.11% | 0.17% | 102% | 100%
BQSquare | 0.16% | 1.39% | 1.23% | 101% | 102%
BlowingBubbles | -0.04% | -0.32% | 0.22% | 102% | 103%
RaceHorses | 0.05% | -0.27% | 0.25% | 102% | 100%
FourPeople | -0.01% | -0.27% | -0.05% | 101% | 103%
Johnny | -0.15% | 1.10% | 2.11% | 101% | 101%
KristenAndSara | 0.26% | -0.32% | -0.16% | 101% | 100%
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | ####### | #######
Class C | -0.04% | 0.12% | 0.04% | 102% | 102%
Class E | 0.03% | 0.17% | 0.63% | 101% | 102%
Overall | #VALUE! | #VALUE! | #VALUE! | ####### | #######
Class D | 0.02% | 0.17% | 0.46% | 102% | 101%
Class F (optional) | 0.01% | -0.41% | 0.65% | 102% | 102%

## Slide 11: Affine model derivation for inherited candidates
w - 8
w
w / 2
4

## Slide 12: Simulation results 1 point (LDB BasketballDrive qp 22) was taken from the anchor
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.14% | 0.00% | 102% | 102%
Class A2 | 0.05% | 0.09% | 0.05% | 102% | 102%
Class B | 0.00% | 0.06% | -0.02% | 102% | 102%
Class C | 0.01% | 0.04% | -0.03% | 103% | 104%
Class E |  |  |  |  | 
Overall | 0.01% | 0.08% | 0.00% | 102% | 103%
Class D | -0.03% | -0.08% | 0.05% | 102% | 106%
Class F (optional) | 0.01% | 0.06% | -0.01% | 103% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.09% | -0.13% | 102% | 103%
Class C | -0.04% | 0.12% | 0.04% | 102% | 102%
Class E | 0.03% | 0.17% | 0.63% | 101% | 102%
Overall | -0.01% | 0.12% | 0.12% | 101% | 102%
Class D | 0.02% | 0.17% | 0.46% | 102% | 101%
Class F (optional) | 0.01% | -0.41% | 0.65% | 102% | 102%