## Slide 1: [JVET-P0669] AHG6: Wrap-around motion vector prediction at the picture boundary
ETRI (Electronics and Telecommunications Research Institute)
KWU (Kwangwoon University)
Notes: This presentation show the contribution of JVET-P0669,
AHG6: Wrap-around motion vector prediction at the picture boundary
From Kwangwoon university and ETRI

## Slide 2: Introduction
Int the current draft spec., if the spatial and temporal candidates out of the picture boundary, such as B2, B0, A1, A0 and C0 in Fig 1, are excluded from the motion vector predictor candidate list
In SbTMVP mode, if the position pointed to by the motion vector of left neighbor block in collocated picture is out of left or right boundary, then the corresponding position for each sub block is clipped inside the picture
Figure 1. Example of unavailable candidates
CU
Picture boundary
CU
B0
C0
B2
A1
A0
Collocated picture
Picture boundary
Figure 2. Example of unavailable candidates
Co-located
CU
Co-located
CU
Notes: In VVC, Wrap-around motion compensation is already adopted.
And In VVC, the spatial and temporal can~
And in this contribution propose wrap-around motion vector prediction, the concept of proposed methods are same as wrap-around MC

## Slide 3: Proposed Method
If the spatial and temporal candidates are out of the picture boundary, then adding or subtracting wrap-around-offset from the position of the out-of-boundary candidate in the horizontal direction as:
  wrap-around-offset = (sps_ref_wraparound_offset_minus1 + 1) * MinCbSizeY
In the figure below, A0 and A1 are not used for the proposed method because motion vectors, ‘wrap-arounded A0’ and ‘wrap-arounded A1’, are unavailable
CU
A0
A1
B0
CU
B2
C0
B0
C0
B2
A0
A1
Picture boundary
wrap-around-offset
wrap-around-offset
wrap-around-offset
wrap-around-offset
wrap-around-offset
Notes: In the proposed method, in merge and AMVP modes, ‘Wrap-around B0’, ‘Wrap-around B2’ and ‘Wrap-around C0’ are only additionally exploited.
Because the left and right picture boundary of ERP or PERP format has connected each other.

## Slide 4: Proposed Method
If the position pointed to by the motion vector of left neighbor block in collocated picture is out of boundary, then adding or subtracting wrap-around-offset from the out-of-boundary position in the horizontal direction
The proposed methods are simply applicable, same as ‘Wrap-around MC’
  just adding or subtracting offset is only needed
Collocated picture
Picture boundary
Co-located
CU
Co-located
CU
wrap-around-offset
wrap-around-offset

## Slide 5: Simulation Results
RD performance of VTM6.0 with 360Lib-9.1 in RA configuration
  Simulation results show that the proposed methods yields -0.02%, -0.04% and -0.12% BD-rate gain in end-to-end WS-PSNR with no additional complexity
 |  | Random Access |  |  |  | 
Reference: VTM-6.0 |  | Over VTM-6.0 |  |  |  | 
Tested: Proposed |  | Y | U | V | EncT | DecT
S1 | SkateboardInLot | -0.06% | -0.20% | -0.41% | 100% | 100%
 | ChairliftRide | 0.00% | 0.04% | 0.03% | 100% | 99%
 | KiteFlite | -0.02% | 0.00% | 0.07% | 100% | 100%
 | Harbor | -0.01% | -0.05% | -0.13% | 100% | 100%
 | Trolley | -0.03% | 0.00% | -0.02% | 100% | 100%
 | GasLamp | -0.01% | -0.01% | 0.00% | 101% | 99%
S2 | Balboa | 0.00% | -0.02% | -0.41% | 100% | 100%
 | Broadway | -0.01% | -0.04% | -0.01% | 101% | 100%
 | Landing2 | 0.00% | -0.03% | -0.15% | 100% | 100%
 | BranCastle2 | -0.02% | -0.09% | -0.12% | 100% | 100%
Overall |  | -0.02% | -0.04% | -0.12% | 100% | 100%
Notes: Simulation results show that the wrap-around motion vector prediction at the picture boundary yields -0.02%, -0.04% and -0.12% BD-rate gain in end-to-end WS-PSNR with no complexity burden for PERP with horizontal geometry padding of reference pictures.
A little gain with no complexity

## Slide 6: Conclusion
This contribution proposes a wrap-around motion vector prediction at the picture boundary to improve the coding efficiency of 360 video
  Using only adding/subtracting offset
In VVC, Wrap-around MC is already adopted, the proposed methods in this contribution are very simply applicable, same as Wrap-around MC and there is no additional syntax signalling and no additional complexity
Due to the characteristics of 360 video, affine mode is selected highly around the picture boundary, so these proposed methods are expected that it will perform better if it is applied to the affine mode
Thanks to Samsung for crosschecking (JVET-P1016)