## Slide 1: JVET-P0884: Simplified GEO without multiplication and minimum blending mask storage
Han Gao, Semih Esenlik, Elena Alshina, Anand Meher Kotra, Biao Wang (Huawei)
Max Bläser, Johannes Sauer (RWTH Aachen)
Contribution identical to JVET-P0885

## Slide 2
Summary
CE4-1.14 test is used as base code.
Additionally 2 modifications are included
  Modification 1: Quantize GEO angles to replace per-sample multiplications with shift (JVET-P0107, JVET-P0264).
  Benefit: No multiplications (for on-the-fly calculation implementation)
  Modification 2: Crop the mask to reduce the memory storage of weight mask (JVET-P0304).
  Benefit: Reduce storage memory from ~3.4MBytes to 204Bytes (for off-line calculation implementation)

## Slide 3
Modification 1: Quantization of GEO angles
Equation to calculate sample distance to line:
Benefits:
  All mults. replaced by shifts (on-the-fly calculation implementation)
  Possibly reusing weights row by row (column by column)
idx | 0 | 1 | 2 | 4 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 15
Dis[idx] | 8 | 8 | 8 | 8 | 4 | 2 | 0 | -2 | -4 | -8 | -8 | -8
idx | 16 | 17 | 18 | 20 | 22 | 23 | 24 | 25 | 26 | 28 | 30 | 31
Dis[idx] | -8 | -8 | -8 | -8 | -4 | -2 | 0 | 2 | 4 | 8 | 8 | 8
dependent on block size

## Slide 4
Modification 2: Cropping weight mask
Equation to calculate sample distance to line:
(W, H)
Benefits:
  Reducing Storage from ~3.4 MBytes to 204 Bytes (off-line calculation implementation)
  2. Possibly reusing masks for all block sizes
Derived based angle and block size
 | CE4-1.14 | P0884
Blending Mask | 3,301,760 bytes | 168 bytes
Motion storage Mask | 103,180 bytes | 36 bytes
Total | 3,404,940 bytes (3.4 Mbytes) | 204 bytes
independent on block size

## Slide 5
Simulation results

## Slide 6
Conclusion
Based on CE4-1.14 with independent motion storage.
Most 2 simplifications are selected from contributions: JVET-P0107, JVET-P0264, JVET-P0304.
  All multiplications can be implemented with shift operation
  Makes storage size of precalculated weights feasible 204 bytes (vs 3.4Mbytes in CE solution).
0.32% BD-rate reduction with 2% encoding time increasing
Suggested to adopt this version in the next version of VVC.
Thanks Mediatek for crosschecking.

## Slide 8
Comparison with GEO contribution in last meeting
  Number of modes reduced from 140 to 80
  Motion storage logic got simplified: Distance of one sample of 4x4 motion unit is calculated using same distance equation
  All multiplications can be implemented with shift operation
  Makes storage size of off-line calculated weights feasible: 204 bytes

## Slide 9
Details of Quantization of GEO angles (P0107, P0264)
Due to the quantization of the GEO angles, angle that are above are possible.
The angles are aligned with what TPM has.

## Slide 10
Details of pre-calculated weight (P0304)
Given a block W × H with angle φ and distance index ρ
W × H weights are cropped from pre-calculated weight mask with top-left position (offsetX, offsetY)
.
pre-calculated weight
weight for the block

## Slide 11
Combined with two modifications
blendWeight[angle][14] = {
{ 8, 8, 8, 7, 5, 3, 1, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 1, 1, 2, 3, 3, 4, 4, 5, 5, 6, 7, 7, 8 },
{ 0, 0, 0, 1, 2, 3, 5, 6, 7, 8, 8, 8, 8, 8 },
{ 8, 8, 8, 8, 6, 4, 2, 0, 0, 0, 0, 0, 0, 0 },
…

## Slide 12
GEO+Overlay
LDB, 37, F23

## Slide 13
VTM-6.0
LDB, 37, F23

## Slide 14
GEO
LDB, 37, F23

## Slide 15
GEO+Overlay
LDB, 37, F81

## Slide 16
VTM-6.0
LDB, 37, F81

## Slide 17
GEO
LDB, 37, F81

## Slide 18
GEO+Overlay
RA, 37, F30

## Slide 19
VTM-6.0
RA, 37, F30

## Slide 20
GEO
RA, 37, F30

## Slide 21
GEO+Overlay
RA, 37, F106

## Slide 22
VTM-6.0
RA, 37, F106

## Slide 23
GEO
RA, 37, F106

## Slide 24
GEO+Overlay
LDB, 37, F209

## Slide 25
VTM-6.0
LDB, 37, F209

## Slide 26
GEO
LDB, 37, F209

## Slide 27
GEO+Overlay
LDB, 37, F8

## Slide 28
VTM-6.0
LDB, 37, F8

## Slide 29
GEO
LDB, 37, F8

## Slide 30
GEO+Overlay
LDB, 37, F3

## Slide 31
VTM-6.0
LDB, 37, F3

## Slide 32
GEO
LDB, 37, F3