## Slide 1: CE5-related: On the design of CC-ALF (JVET-P1008)
K. Misra, F. Bossen, A. Segall (Sharp Labs of America),
N. Hu, J. Dong, V. Seregin, M. Karczewicz (Qualcomm),
P. Onno, C. Gisquet, G. Laroche (Canon),
J. Li, C.S. Lim, C.-W. Kuo (Panasonic),
J. Nam, J. Choi, J. Lim, S. Kim (LGE)
O. Chubach, C.-Y. Lai, C.-Y. Chen, T.-D. Chuang,
Y.-W. Huang, and S.-M. Lei (MediaTek)

## Slide 2: Introduction
CC-ALF was proposed at the last meeting and studied in CE5
  CC-ALF is a loop-filter that generates a correction for the chroma samples by filtering luma samples
The purpose of this proposal is to recommend a design for the CC-ALF tool that is
  Simplified compared to the CE5 configuration
  Better harmonized with the ALF design

## Slide 3: Overview
Proposed simplifications:
Complexity reduction
  Reduce the number of multiplies in the filter operation
  Limit dynamic range of coefficient to 6-bits
  Allow for sharing of multipliers with chroma ALF
Alignment with ALF
  Limit filter selection to signaling at a CTU level
  Removal of the temporal layer coefficient buffers
  Use of symmetric line selection at virtual boundary
Additionally, as the simplifications reduce coding efficiency, we also propose to use up to 4 filter per chroma component

## Slide 4: Reduce filter shape
Complexity Reduction
  Change filter shape to 3x4 diamond shape
  Goal is to reduce the number of multiplications
  Benefit is a 43% decrease
CE5-2
Proposed
 | CE5-2 | Proposed | Change
Number of taps | 18 | 8 | -56%
Unique coefficient count | 14 | 8 | -43%

## Slide 5: Align with ALF
Alignment with ALF
  Limit filter selection to signaling at a CTU level
  Removal of the temporal layer coefficient buffers
  Use of symmetric line selection at virtual boundary
slice_header( ) { | Descriptor
… | 
if( ChromaArrayType != 0 ) | 
slice_cross_component_alf_cb_enabled_flag | u(1)
if( slice_cross_component_alf_cb_enabled_flag ) | 
slice_cross_component_alf_cb_aps_id | u(3)
if( ChromaArrayType != 0 ) | 
slice_cross_component_alf_cr_enabled_flag | u(1)
if( slice_cross_component_alf_cr_enabled_flag ) | 
slice_cross_component_alf_cr_aps_id | u(3)
… | 
} | 
coding_tree_unit( ) { | Descriptor
… | 
if ( slice_cross_component_alf_cb_enabled_flag ) | 
alf_ctb_cross_component_cb_idc[ xCtb >> CtbLog2SizeY ][ yCtb >> CtbLog2SizeY ] | ae(v)
if ( slice_cross_component_alf_cr_enabled_flag ) | 
alf_ctb_cross_component_cr_idc[ xCtb >> CtbLog2SizeY ][ yCtb >> CtbLog2SizeY ] | ae(v)
… | 
} | 

## Slide 6: Exclusive Application of CC-ALF and Chroma ALF
Disallow the use of both CC-ALF and chroma ALF in a CTB
For each chroma CTB
  Signal CC-ALF on/off flag
  If CC-ALF enabled, chroma ALF is disabled
  Otherwise, signal chroma ALF on/off flag
Benefit: Number of multiplications per pixel are reduced from 19 to 16. (15 in current ALF)

## Slide 7: Coding Efficiency Improvement
Coding efficiency
  Use up to four filter per chroma component
  Selected at CTU level
alf_cross_component_cb_filters_signalled_minus1 plus 1 specifies the number of cross component Cb filters signalled in the current ALF APS.
alf_cross_component_cr_filters_signalled_minus1 plus 1 specifies the number of cross component Cr filters signalled in the current ALF APS.
alf_data( ) { | Descriptor
… | 
if ( alf_cross_component_cb_filter_signal_flag ) { | 
alf_cross_component_cb_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cb_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 8; j++ ) | 
alf_cross_component_cb_coeff_plus32[ k ][ j ] | u(6)
} | 
} | 
if ( alf_cross_component_cr_ filter_signal_flag ) { | 
alf_cross_component_cr_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cr_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 8; j++ ) | 
alf_cross_component_cr_coeff_plus32[ k ][ j ] | u(6)
} | 
} | 
} | 

## Slide 8: Limit dynamic range of coefficient to 6-bits
alf_data( ) { | Descriptor
… | 
if ( alf_cross_component_cb_filter_signal_flag ) { | 
alf_cross_component_cb_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cb_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 8; j++ ) | 
alf_cross_component_cb_coeff_plus32[ k ][ j ] | u(6)
} | 
} | 
if ( alf_cross_component_cr_ filter_signal_flag ) { | 
alf_cross_component_cr_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cr_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 8; j++ ) | 
alf_cross_component_cr_coeff_plus32[ k ][ j ] | u(6)
} | 
} | 
} | 
alf_cross_component_cr_coeff_plus32[ k ][ j ] minus 32 specifies the value of the j-th coefficient of the signalled k-th cross-component Cr filter set. When alf_cross_component_cr_coeff_abs[ k ][ j ] is not present, it is inferred to be equal to 32.
…
It is a requirement of bitstream conformance that the values of CcAlfApsCoeffCr[ adaptation_parameter_set_id ][ k ][ j ] with j = 0..7 shall be in the range of −25 to 25 − 1, inclusive.
Semantic for Cb parallels the one above
Dynamic range of coefficients is limited to 6-bits:
  Reduces complexity of multiply
  Smaller memory requirement

## Slide 9
Results

## Slide 10: Results
We provide results for two configurations
  Allow for the use of Chroma ALF and CC-ALF in the same CTB
  Do not allow for the use of Chroma ALF and CC-ALF in the same CTB

## Slide 11: Comparison versus CE5-2.1
Anchor: CE5-2.1
Compared to CE5-2.1
  AI: -0.39%
  RA: -0.23%
  LDB: 0.21%
Observations
  Improvement for higher resolution
 | All Intra Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.10% | -1.98% | -1.44% | -0.26% | 98% | 97%
Class A2 | 0.04% | -0.70% | -6.72% | -0.71% | 99% | 96%
Class B | 0.11% | -6.18% | -4.04% | -0.94% | 99% | 97%
Class C | 0.09% | -0.04% | 0.08% | 0.08% | 99% | 96%
Class E | 0.13% | -1.69% | 1.52% | 0.09% | 99% | 93%
Overall | 0.10% | -2.45% | -2.21% | -0.39% | 99% | 96%
Class D | -0.02% | -0.79% | 1.51% | 0.06% | 100% | 91%
Class F | 0.03% | 0.79% | 0.07% | 0.11% | 99% | 94%
 | Random access Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.01% | -0.23% | -1.05% | -0.12% | 99% | 98%
Class A2 | 0.03% | -0.42% | -3.59% | -0.38% | 98% | 98%
Class B | -0.02% | -3.45% | -1.68% | -0.53% | 98% | 98%
Class C | 0.04% | 0.64% | 0.81% | 0.18% | 98% | 98%
Overall | 0.01% | -1.11% | -1.27% | -0.23% | 98% | 98%
Class D | -0.03% | 0.29% | 1.58% | 0.17% | 100% | 98%
Class F | 0.02% | 0.51% | 0.10% | 0.08% | 101% | 100%
 | Low delay B Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class B | 0.07% | -0.64% | -0.21% | -0.03% | 98% | 99%
Class C | 0.02% | 3.08% | 2.52% | 0.58% | 98% | 96%
Class E | -0.28% | 0.35% | 3.30% | 0.14% | 98% | 97%
Overall | -0.03% | 0.85% | 1.58% | 0.21% | 98% | 98%
Class D | -0.13% | 4.59% | 3.51% | 0.71% | 96% | 97%
Class F | 0.08% | 2.45% | 1.47% | 0.45% | 97% | 98%
Configuration #1: Chroma ALF and CC-ALF can be enabled in each CTB in these results

## Slide 12: Experimental Results
CTC Results
  Overall BD Rate (using 8:1:1 metric from AhG13) :
    AI: -1.58%
    RA: -2.11%
    LDB: -2.38%
    LDP: -2.33%
 | All Intra Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.23% | -5.30% | -5.56% | -0.90% | 103% | 100%
Class A2 | 0.18% | -9.41% | -14.64% | -2.26% | 102% | 100%
Class B | 0.21% | -15.85% | -12.00% | -2.62% | 101% | 99%
Class C | 0.22% | -4.17% | -3.79% | -0.62% | 101% | 97%
Class E | 0.32% | -11.64% | -1.88% | -1.10% | 102% | 96%
Overall | 0.23% | -9.72% | -7.86% | -1.58% | 102% | 98%
Class D | 0.10% | -3.34% | -1.74% | -0.43% | 101% | 94%
Class F | 0.21% | -6.26% | -6.63% | -1.12% | 101% | 96%
 | Random access Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.14% | -5.79% | -6.33% | -1.10% | 99% | 97%
Class A2 | 0.24% | -12.10% | -18.54% | -2.87% | 98% | 99%
Class B | 0.19% | -20.32% | -15.20% | -3.40% | 100% | 98%
Class C | 0.12% | -4.41% | -3.55% | -0.70% | 101% | 98%
Overall | 0.17% | -11.53% | -10.99% | -2.11% | 100% | 98%
Class D | 0.08% | -4.05% | -2.90% | -0.63% | 99% | 98%
Class F | 0.21% | -4.62% | -4.62% | -0.76% | 104% | 99%
 | Low delay B Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class B | 0.25% | -21.96% | -19.09% | -3.91% | 100% | 99%
Class C | 0.14% | -5.44% | -4.11% | -0.84% | 99% | 96%
Class E | -0.05% | -15.42% | -3.22% | -1.90% | 98% | 94%
Overall | 0.14% | -14.82% | -10.13% | -2.38% | 99% | 97%
Class D | 0.05% | -3.74% | -2.82% | -0.62% | 99% | 99%
Class F | 0.21% | -8.56% | -6.24% | -1.31% | 101% | 99%
Configuration #1: Chroma ALF and CC-ALF can be enabled in each CTB in these results (Total 19 multiplications per pixel; 15 in current ALF)

## Slide 13: Experimental Results
CTC Results
  Overall BD Rate (using 8:1:1 metric from AhG13) :
    AI: -1.30%
 | All Intra Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -3.64% | -3.36% | -0.61% | 103% | 97%
Class A2 | 0.11% | -7.91% | -13.61% | -2.06% | 104% | 100%
Class B | 0.16% | -14.35% | -10.30% | -2.34% | 102% | 98%
Class C | 0.13% | -2.77% | -1.67% | -0.34% | 101% | 97%
Class E | 0.25% | -9.28% | -0.42% | -0.77% | 102% | 97%
Overall | 0.15% | -8.07% | -6.13% | -1.30% | 102% | 98%
Class D | 0.08% | -3.00% | -1.53% | -0.39% | 103% | 98%
Class F | 0.14% | -5.07% | -5.22% | -0.92% | 102% | 96%
 | Random access Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.17% | -19.03% | -14.06% | -3.17% | 98% | 97%
Class C | 0.09% | -3.53% | -2.15% | -0.49% | 100% | 97%
Overall |  |  |  |  |  | 
Class D | 0.07% | -3.89% | -2.52% | -0.59% | 98% | 97%
Class F | 0.16% | -3.87% | -3.60% | -0.62% | 101% | 97%
 | Low delay B Main10 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class E | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.10% | -4.01% | -2.75% | -0.60% | 101% | 99%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Configuration #2: Chroma ALF and CC-ALF can be enabled in each CTB in these results (Total 16 multiplications per pixel; 15 in current ALF)

## Slide 14: Recommendations
Summary
  Multi-company proposal for the design of the Cross Component Adaptative Loop Filter
    Simplified relative to what was studied in CE5
    Aligned with ALF
  Operates in parallel to luma ALF
  Predicts correction for chroma channel from filtered luma samples
  Average YUV gains of 1.58%, 2.11%, 2.38%, 2.33% (for AI, RA, LDB, LDP)
  Average YUV gains of 1.30% (for AI ) when CC-ALF and Chroma ALF are mutually exclusive
  Thanks to:
    Interdigital for cross-checking JVET-P1008 (JVET-P1010)
    HHI for cross-check JVET-P1009 of JVET-P0468
Recommend adopting CC-ALF into VVC Draft