## Slide 1: An alternative IBC virtual buffer setting to avoid REFERENCE wrapping around
Jizheng Xu, Li Zhang, Weijia Zhu, Kai Zhang, Hongbin Liu (Bytedance)
Xiaozhong Xu, Xiang Li, Shan Liu (Tencent)

## Slide 2: Proposed change
Enlarge the IBC virtual buffer by 2x to place “fire break”
  Disable discontinuous reference

## Slide 3: CTU64
Any reference block to the right of the current VPDU is determined as invalid.

## Slide 4: CTU128
Virtual buffer view
Picture view
Virtual buffer view
Picture view

## Slide 5: Performance
No BD-rate change since the current encoder does not search reference block that needs wrapping around
Software patch is attached.
Thanks Panasonic for crosschecking!
 | All Intra |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 100% | 96%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 100% | 100%
 | Random Access |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 99% | 100%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 100% | 98%

## Slide 6: Performance – cont.
CTU64
CTU32
 | All Intra |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 101% | 99%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 101% | 100%
 | Random Access |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 101% | 100%
 | All Intra |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 100% | 101%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 100% | 99%
 | Random Access |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.00% | 0.00% | 0.00% | 100% | 101%
4:2:0 TGM | 0.00% | 0.00% | 0.00% | 100% | 100%

## Slide 7: Text changes

## Slide 8: Conclusions
A simple IBC virtual buffer setting change
  Avoid discontinuous reference block
  Does not enforce decoders to implement the storage following the VPDU concept
  Decoder can be implemented as in VTM-5.0/VTM-4.0
Cost for decoders that want to implement BV checking
  Current setting: 128x128/4/4 bits = 128 Bytes
  Proposed setting: 256x128/4/4 bits = 256 Bytes