## Slide 1: JVET-P1026
Fraunhofer HHI, LGE and Nokia

## Slide 2: Introduction
Combination of JVET-P0196 and JVET-P0392:
  1) MTS signalling is moved after LFNST signalling
  2) The restriction that disallows the usage of LFNST if the CU is using ISP is removed

## Slide 3: MTS signalling
MTS signalling is moved after LFNST signalling
Therefore, both LFNST and MTS are signalled
  in the same place (at the end of the CU) and
  conditionally to the last significant position syntax element

## Slide 4
MTS Idx Coding
LFNST Idx Coding
Residual Coding
MTS Idx Coding
LFNST Idx Coding
Residual Coding
VTM6:
Proposed:

## Slide 5: ISP + LFNST
In VTM-6.0, the LFSNT and ISP are mutually exclusive.
In this proposal, the LFNST may be applied to ISP CUs if the TU size is at least .
The same LFNST is applied to all TUs in the same way as in VTM-6.0.
No new kernels are added.
The existing kernels are not retrained.

## Slide 6: Results
 | All Intra Main10 |  |  |  | 
 | Over anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.52% | -0.40% | 103% | 100%
Class A2 | -0.10% | -0.33% | -0.34% | 102% | 101%
Class B | -0.16% | -0.51% | -0.62% | 101% | 99%
Class C | -0.30% | -0.40% | -0.33% | 99% | 101%
Class E | -0.23% | -0.57% | -0.60% | 101% | 100%
Overall | -0.19% | -0.47% | -0.47% | 101% | 100%
Class D | -0.21% | -0.30% | -0.27% | 101% | 104%
Class F | -0.21% | -0.29% | -0.30% | 101% | 101%
 | Random Access Main10 |  |  |  | 
 | Over anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | -0.34% | -0.14% | 102% | 99%
Class A2 | -0.09% | -0.19% | -0.25% | 101% | 99%
Class B | -0.18% | -0.12% | -0.09% | 101% | 101%
Class C | -0.25% | -0.12% | -0.31% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.18% | -0.18% | -0.19% | 101% | 100%
Class D | -0.20% | -0.46% | -0.20% | 100% | 98%
Class F | -0.17% | -0.21% | 0.10% | 100% | 97%

## Slide 7: Conclusion
The residual coding process does not depend on the MTS index anymore.
The LFNST is now applied to all intra-predicted blocks with the appropriate size.
The gain of the combination is almost the same as the sum of the individual gains (0.19% for AI and 0.18% for RA).