## Slide 1: JVET-Q0104 On worst-case complexity of LFNST
Hilmi E. Egilmez, Alican Nalci, Muhammed Çoban, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
LFNST supports two dimensions
  4x4 LFNST: 4x4 square, and 4xN/Nx4 for N>8 rectangular TUs
    16x16 LFNST matrices, square support
  8x8 LNFST: 8x8 square, and 4xN/Nx4 for N>16 rectangular TUs
    16x48 LFNST matrices, L-shaped support
Inverse LFNST
Inverse DCT-2
Decoded coefficients
8x8 LFNST(L-shape, 48 sample)
Reconstructed TU

## Slide 3: Complexity
Worst-case handling: coefficients are normatively zeroed-out
  For 4x4 and 8x8 TUs
    max. 8 coefficients are allowed
  Other TU sizes
    max. 16 coefficients are allowed
Worst-case complexity
  8 multiplications per coefficient
Memory: 8KB
  4x4 LFNST: 2KB, 8x8 LFNST: 6KB
This contribution: Two simple methods
  some coding benefit
  without changing the worst-case complexity

## Slide 4: Proposal
Method 1: Changes 8x8 LFNST only
  Instead of 16x48 matrices with L-shaped support:
  Propose 16x64 matrices with square support
  Only disadvantage: Increases LFNST memory from 8KB to 10KB
  Benefits: Regular memory handling + coding gains
Inverse 8x8 LFNST
8x8 LFNST with L-shape, 48 samples
Inverse 8x8 LFNST
8x8 LFNST with square-shape, 64 samples
…
nLfnstOutSize = ( nTbW >= 8 && nTbH >= 8 ) ? 48 64 : 16 (1150)
…
The array d[ x ][ y ] with x = 0..nLfnstSize − 1, y = 0..nLfnstSize − 1 is derived as follows:
If predModeIntra is less than or equal to 34, the following applies:
d[ x ][ y ] = v[ x + ( y << log2LfnstSize ) ] (1157)
d[ x ][ y ] = ( y < 4 ) ? v[ x + ( y << log2LfnstSize ) ] : (1157) ( ( x < 4 ) ? v[ 32 + x + ( ( y − 4 ) << 2 ) ] : d[ x ][ y ] )
Otherwise, the following applies:
d[ x ][ y ] = v[ y + ( x << log2LfnstSize ) ] (1158)
d[ x ][ y ] = ( x < 4 ) ? v[ y + ( x << log2LfnstSize ) ] : (1158) ( ( y < 4 ) ? v[ 32 + y + ( ( x − 4 ) << 2 ) ] : d[ x ][ y ] )
Also, 16x64 matrices are included in the array lowFreqTransMatrix[ m ][ n ].
size
Regular memory handling
transform table

## Slide 5: Results of Method 1
Anchor: VTM-7.0
Keeps the worst-case complexity at 8 mult/coeff:
  8x8 LFNST for 8x8 TU: 8 = 8x64/64
Trained on sequences listed on the reflector by LGE.

## Slide 6: Proposal
Method 2: Addresses the following issue
  Removes the unnecessary case of zeroing-out for 8x8 LFNST:
    The worst-case of 8 mult/coeff. is maintained by allowing 10 coefficients:
       7.5 multiplications per coefficient (=10x48/64)
    Same number of checks
In the 14th JVET meeting, based on the discussions, it was concluded that zeroing-out process is undesirable unless it is urgently necessary.
“JVET-N0364: From implementation perspective, there is no problem that this further zeroing-out is necessary. More cases of zeroing are undesirable if not urgently necessary. Furthermore, it is mentioned that 16x16 DST-VII would be an equivalent worst case not resolved here.”
nonZeroSize = ( ( nTbW = = 4 && nTbH = = 4 ) | | ( nTbW = = 8 && nTbH = = 8 ) ) ? 8 : 16 (1153)
  If ( nTbW = = 4 && nTbH = = 4 ) is true, the following applies:
nonZeroSize = 8
  Otherwise, if ( nTbW = = 8 && nTbH = = 8 ) is true, the following applies:
nonZeroSize = 10
  Otherwise, the following applies:
nonZeroSize = 16
…

## Slide 7: Conclusions
Proposed two alternatives LFNST design w/o changing the worst-case comp.
Method 1: Regular memory handling with 0.1% AI and 0.06% RA gains
Method 2: Clean-up – removing unnecessary zero-out
Recommendation: to adopt one of the proposed methods.
Cross-checkers: T. Zhou and T. Ikai (Sharp)
Inverse 8x8 LFNST
nonZeroSize = ( ( nTbW = = 4 && nTbH = = 4 ) | | ( nTbW = = 8 && nTbH = = 8 ) ) ? 8 : 16 (1153)
  If ( nTbW = = 4 && nTbH = = 4 ) is true, the following applies:
nonZeroSize = 8
  Otherwise, if ( nTbW = = 8 && nTbH = = 8 ) is true, the following applies:
nonZeroSize = 10
  Otherwise, the following applies:
nonZeroSize = 16
…