## Slide 1: JVET-Q0150 Fix for ALF virtual boundary processing K. Andersson, J. Ström, Z.. Zhang, J. Enhorn (Ericsson)
Kenneth Andersson
Ericsson
2020-01-10

## Slide 2: Problem statement
ALF virtual boundary processing avoids increasing the size of line buffers for ALF
Visual artifacts observed for row above and below virtual horizontal CTU boundary:
  Caused by extreme padding when filtering row above and below the virtual horizontal CTU boundary which reduces ALF to horizontal filtering with amplification of neighboring samples of current row

## Slide 3: Proposed solution 1 (preferred)
Move ALF virtual boundary one row upwards for both luma and chroma
Allow for usage of row below ALF virtual boundary when filtering above the ALF virtual boundary.
Allow for usage of row above ALF virtual boundary when filtering below the ALF virtual boundary.

## Slide 4: Text proposed solution 1
8.8.5.3 Derivation process for ALF transpose and filter index for luma samples
..
The variables applyAlfLineBufBoundary, minY, maxY, and ac[ x ][ y ] are derived as follows:
If y4 is equal to ( CtbSizeY − 8 ) and one of the following condition is true, minY is set equal to −2, maxY is set equal to 3, applyAlfLineBufBoundary is set equal to 1, and ac[ x ][ y ] is set equal to 96.
  The bottom boundary of the current coding tree block is the bottom boundary of the picture and pic_height_in_luma_samples − yCtb > CtbSizeY − 4.
  The bottom boundary of the current coding tree block is not the bottom boudary of the picture.
Otherwise, if y4 is equal to ( CtbSizeY − 4 ) and one of the following condition is true, minY is set equal to 0, maxY is set equal to 5, applyAlfLineBufBoundary is set equal to 1, and ac[ x ][ y ] is set equal to 96.
  The bottom boundary of the current coding tree block is the bottom boundary of the picture and pic_height_in_luma_samples − yCtb > CtbSizeY − 4.
  The bottom boundary of the current coding tree block is not the bottom boudary of the picture
Otherwise, minY is set equal to −2 and maxY is set equal to 5, applyAlfLineBufBoundary is set equal to 0 and ac[ x ][ y ] is set equal to 64.
Table 43 – Specification of y1, y2 and y3 according
to the vertical luma sample position y and
applyAlfLineBufBoundary
Condition | y1 | y2 | y3
( y = = CtbSizeY − 5 ¦ ¦ y = = CtbSizeY − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 0 | 0 | 0
( y = = CtbSizeY − 6 ¦ ¦ y = = CtbSizeY − 5 ) && ( applyAlfLineBufBoundary = = 1 ) | 1 | 1 | 1
( y = = CtbSizeY − 7 ¦ ¦ y = = CtbSizeY − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 1 | 2 | 2
Otherwise | 1 | 2 | 3
Condition | y1 | y2
( y = = ctbHeightC − 2 ¦ ¦ y = = ctbHeightC − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 0 | 0
( y = = ctbHeightC − 3 ¦ ¦ y = = ctbHeightC − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 1 | 1
Otherwise | 1 | 2
Table 44 – Specification of y1 and y2 according to the vertical
chroma sample position y and applyAlfLineBufBoundary

## Slide 5: Subjective example solution 1
BasketballDrill, LDB QP 37. Left: VTM-7.0, Right: Proposed method 1

## Slide 6: Subjective example solution 1
BasketballDrill, LDB QP 37. Left: VTM-7.0, Right: Proposed method 1

## Slide 7: Proposed solution 2
Reduce filter strength for both luma and chroma when filtering rows adjacent to ALF virtual horizontal CTU boundary to compensate for amplification from neighboring samples of current row

## Slide 8: Text proposed solution 2
sum = curr + ( ( sum + 64 ) >> alfShiftY ) (1425)
sum = curr + ( ( sum + 64 ) >> alfShiftC ) (1466)
Table 43 – Specification of y1, y2, y3 and alfShiftY
according to the vertical luma sample position y and
applyAlfLineBufBoundary
Condition | alfShiftY | y1 | y2 | y3
( y = = CtbSizeY − 5 ¦ ¦ y = = CtbSizeY − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 0 | 0 | 0
( y = = CtbSizeY − 6 ¦ ¦ y = = CtbSizeY − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 1 | 1
( y = = CtbSizeY − 7 ¦ ¦ y = = CtbSizeY − 2 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 2 | 2
Otherwise | 7 | 1 | 2 | 3
Condition | alfShiftC | y1 | y2
( y = = ctbHeightC − 2 ¦ ¦ y = = ctbHeightC − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 0 | 0
( y = = ctbHeightC − 1 ¦ ¦ y = = ctbHeightC − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 1
Otherwise | 7 | 1 | 2
Table 44 – Specification of y1, y2 and alfShiftC according to
the vertical chroma sample position y and
applyAlfLineBufBoundary

## Slide 9: Subjective example solution 2
BasketballDrill, LDB QP 37. Left: VTM-7.0, Right: Proposed method 2

## Slide 10: Subjective example solution 2
BasketballDrill, LDB QP 37. Left: VTM-7.0, Right: Proposed method 2

## Slide 11: Objective results solution 1
 | Random access Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,01% | -0,07% | -0,06% | 98% | 99%
Class A2 | 0,06% | 0,10% | 0,00% | 99% | 100%
Class B | 0,01% | 0,00% | 0,07% | 98% | 101%
Class C | -0,02% | -0,07% | -0,07% | 98% | 100%
Class E |  |  |  |  | 
Overall | 0,01% | -0,02% | -0,01% | 98% | 100%
Class D | -0,07% | 0,14% | -0,20% | 98% | 101%
Class F | -0,07% | -0,01% | -0,09% | 98% | 99%
 | Low delay Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,02% | -0,09% | 0,13% | 96% | 101%
Class C | -0,07% | -0,32% | -0,12% | 98% | 99%
Class E | 0,00% | 0,41% | 0,13% | 100% | 101%
Overall | -0,02% | -0,04% | 0,04% | 98% | 100%
Class D | -0,08% | 0,24% | 0,36% | 100% | 100%
Class F | -0,08% | 0,03% | 0,45% | 98% | 99%
 | Intra Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,01% | -0,14% | -0,14% | 97% | 100%
Class A2 | 0,04% | -0,04% | -0,05% | 96% | 99%
Class B | 0,00% | -0,06% | -0,05% | 97% | 99%
Class C | -0,03% | -0,04% | -0,06% | 100% | 100%
Class E | -0,03% | 0,00% | -0,05% | 97% | 98%
Overall | -0,01% | -0,06% | -0,07% | 98% | 99%
Class D | -0,01% | -0,01% | -0,03% | 97% | 100%
Class F | -0,03% | -0,06% | -0,06% | 97% | 100%
Note: Encoding time inaccurate.

## Slide 12: Objective results solution 2
 | Random access Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,02% | -0,01% | 0,03% | 95% | 101%
Class A2 | 0,00% | 0,10% | 0,09% | 97% | 99%
Class B | 0,01% | 0,13% | 0,11% | 98% | 100%
Class C | -0,01% | -0,03% | -0,06% | 96% | 101%
Class E |  |  |  |  | 
Overall | 0,00% | 0,05% | 0,04% | 97% | 100%
Class D | 0,00% | 0,07% | 0,06% | 97% | 101%
Class F | -0,04% | -0,01% | -0,01% | 98% | 99%
 | Low delay Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,01% | -0,24% | 0,32% | 95% | 99%
Class C | 0,04% | -0,15% | 0,02% | 95% | 100%
Class E | 0,01% | 0,72% | -0,03% | 73% | 99%
Overall | 0,02% | 0,03% | 0,13% | 89% | 99%
Class D | 0,00% | -0,18% | -0,15% | 99% | 100%
Class F | 0,05% | 0,07% | 0,24% | 95% | 99%
 | Intra Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,01% | 0,04% | 0,07% | 96% | 97%
Class A2 | 0,01% | 0,02% | 0,03% | 96% | 100%
Class B | 0,01% | 0,02% | 0,03% | 98% | 101%
Class C | -0,01% | 0,03% | 0,02% | 99% | 100%
Class E | 0,01% | 0,05% | 0,06% | 95% | 100%
Overall | 0,00% | 0,03% | 0,04% | 97% | 100%
Class D | 0,00% | 0,01% | 0,02% | 95% | 100%
Class F | -0,01% | 0,03% | 0,02% | 98% | 100%
Note: Encoding time inaccurate.

## Slide 13: Conclusion
Proposes methods to solve issue for row above and below ALF virtual horizontal CTU boundary:
  Method 1:
    Move ALF virtual horizontal CTU boundary one row upwards and allowing to use one row on the other side of the virtual boundary in addition to the center row thus having one row above and one row below the center row when filtering a row adjacent to the virtual boundary.
  Method 2:
    Reduce filter strength for both luma and chroma when filtering rows adjacent to ALF virtual horizontal CTU boundary
The fixes improves visual quality on some specific content where method 1 is considered to perform best since it keeps the main characteristics of the filter.
It is proposed to include one of the methods for next version of VVC where method 1 is preferred allthough it causes an increase of line buffers by 2 for luma and for chroma.
If time allows an informal viewing could be arranged.
Thanks to Qualcomm for cross-check in JVET-Q0606