## Slide 1: JVET-Q0368: On context model for mvp_flag and ref_idx
Huanbang Chen, Haitao Yang
JVET-Q0368

## Slide 2
Problem Statements
Mismatch between SPEC and SW in the coding of mvp_l0_flag and mvp_l1_flag. Same issue was detected for ref_idx_l0 and ref_idx_l1 and was reported in ticket #749 (https://jvet.hhi.fraunhofer.de/trac/vvc/ticket/749).
      SPEC: Separate contexts
      SW: Shared contexts
Table 48 – Association of ctxIdx and syntax elements for each initializationType in the initialization process |  |  |  |  |  | 
Syntax structure | Syntax element | ctxTable | initType |  |  | 
 |  |  | 0 | 1 | 2 | 
coding_unit( ) | ref_idx_l0[ ][ ] | Table 81 |  | 0..1 | 2..3 | 
 | mvp_l0_flag[ ][ ] | Table 82 | 0..1 | 2..3 | 4..5 | 
 | ref_idx_l1[ ][ ] | Table 83 |  | 0..1 | 2..3 | 
 | mvp_l1_flag[ ][ ] | Table 84 |  | 0..1 | 2..3 | 
JVET-Q0368

## Slide 3
Method 1: Align SW to SPEC
 | Random Access |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.09% | -0.02% | 99% | 99%
Class A2 | -0.03% | -0.04% | 0.00% | 99% | 98%
Class B | 0.00% | 0.07% | -0.03% | 100% | 99%
Class C | 0.01% | -0.06% | 0.01% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.02% | -0.01% | 100% | 99%
Class D | 0.00% | 0.02% | -0.10% | 100% | 100%
Class F | -0.02% | -0.03% | -0.04% | 100% | 99%
 | Low delay B |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.35% | -0.40% | 99% | 98%
Class C | -0.02% | -0.38% | -0.14% | 100% | 99%
Class E | -0.11% | 0.02% | -0.70% | 100% | 100%
Overall | -0.07% | -0.27% | -0.39% | 100% | 99%
Class D | -0.15% | -0.06% | 0.06% | 100% | 100%
Class F | -0.02% | -0.48% | 0.17% | 100% | 99%
JVET-Q0368
Add 1 context for mvp_l1_flag and 2 contexts for ref_idx_l1 to SW
      Simulation results:

## Slide 4
Method 2: Align SPEC to SW
JVET-Q0368
Table 48 – Association of ctxIdx and syntax elements for each initializationType in the initialization process |  |  |  |  |  | 
Syntax structure | Syntax element | ctxTable | initType |  |  | 
 |  |  | 0 | 1 | 2 | 
coding_unit( ) | ref_idx_l0[ ][ ] , ref_idx_l1[ ][ ] | Table 81 |  | 0..1 | 2..3 | 
 | mvp_l0_flag[ ][ ] , mvp_l1_flag[ ][ ] | Table 82 | 0..1 | 2..3 | 4..5 | 
 | ref_idx_l1[ ][ ] | Table 83 |  | 0..1 | 2..3 | 
 | mvp_l1_flag[ ][ ] | Table 84 |  | 0..1 | 2..3 | 
Proposed specification:

## Slide 5
Conclusion
Recommend to adopt one of the methods
Thanks to Xidian University and NPU for cross-checking (JVET-Q0633).
JVET-Q0368