## Slide 1: On context model for merge indices
Huanbang Chen, Haitao Yang
JVET-Q0370

## Slide 2
Problem Statements
Mismatch between SPEC and SW in the coding of merge indices for regular merge mode (merge_idx) and triangle merge mode (merge_triangle_idx0 and merge_triangle_idx1)
      SPEC: Separate contexts
      SW: Shared contexts
JVET-Q0370
Table 48 – Association of ctxIdx and syntax elements for each initialization Type in the initialization process |  |  |  |  |  | 
Syntax structure | Syntax element | ctxTable | initType |  |  | 
 |  |  | 0 | 1 | 2 | 
merge_data( ) | mmvd_cand_flag[ ][ ] | Table 100 |  | 0 | 1 | 
 | merge_triangle_idx0[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_triangle_idx1[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_idx[ ][ ] | Table 105 | 0 | 1 | 2 | 

## Slide 3
Proposed methods
JVET-Q0370
# | Shared contexts | Separate contexts
Method 1 (SW) | merge_idx merge_triangle_idx0 merge_triangle_idx1 | mmvd_cand_flag
Method 2 | merge_idx merge_triangle_idx0 merge_triangle_idx1 mmvd_cand_flag | 
Method 3 (SPEC) |  | merge_idx merge_triangle_idx0 merge_triangle_idx1 mmvd_cand_flag

## Slide 4
Method 1: Align SPEC to SW
JVET-Q0370
Proposed specification:
Table 48 – Association of ctxIdx and syntax elements for each initialization Type in the initialization process |  |  |  |  |  | 
Syntax structure | Syntax element | ctxTable | initType |  |  | 
 |  |  | 0 | 1 | 2 | 
merge_data( ) | mmvd_cand_flag[ ][ ] | Table 100 |  | 0 | 1 | 
 | merge_triangle_idx0[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_triangle_idx1[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_idx[ ][ ] merge_triangle_idx0[ ][ ] merge_triangle_idx1[ ][ ] | Table 105 | 0 | 1 | 2 | 

## Slide 5
Method 2: Share context for all merge indices
JVET-Q0370
Proposed specification:
Table 48 – Association of ctxIdx and syntax elements for each initialization Type in the initialization process |  |  |  |  |  | 
Syntax structure | Syntax element | ctxTable | initType |  |  | 
 |  |  | 0 | 1 | 2 | 
merge_data( ) | mmvd_cand_flag[ ][ ] | Table 100 |  | 0 | 1 | 
 | merge_triangle_idx0[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_triangle_idx1[ ][ ] | Table 105 |  | 1 | 2 | 
 | merge_idx[ ][ ] merge_triangle_idx0[ ][ ] merge_triangle_idx1[ ][ ] mmvd_cand_flag[ ][ ] | Table 105 | 0 | 1 | 2 | 

## Slide 6
Method 2: Share context for all merge indices
JVET-Q0370
Simulation results:
 | Random Access |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.02% | 98% | 98%
Class A2 | -0.01% | 0.01% | 0.02% | 98% | 99%
Class B | 0.00% | 0.05% | 0.13% | 98% | 95%
Class C | 0.00% | 0.00% | -0.04% | 100% | 98%
Class E |  |  |  |  | 
Overall | 0.00% | 0.02% | 0.03% | 99% | 97%
Class D | -0.03% | -0.11% | -0.15% | 100% | 99%
Class F | -0.02% | 0.00% | 0.03% | 99% | 98%
 | Low delay B |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.20% | -0.08% | 99% | 99%
Class C | 0.02% | -0.20% | -0.21% | 99% | 95%
Class E | -0.03% | 0.12% | -0.31% | 99% | 97%
Overall | -0.01% | -0.12% | -0.18% | 99% | 97%
Class D | -0.05% | 0.33% | -0.01% | 100% | 100%
Class F | -0.02% | -0.38% | 0.11% | 99% | 98%

## Slide 7
Method 3: Align SW to SPEC
JVET-Q0370
Simulation results:
 | Random Access |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.04% | -0.02% | 98% | 98%
Class A2 | -0.02% | 0.04% | 0.02% | 98% | 98%
Class B | 0.02% | 0.08% | 0.08% | 99% | 96%
Class C | -0.02% | 0.02% | -0.04% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.02% | 99% | 97%
Class D | 0.01% | -0.04% | -0.07% | 100% | 100%
Class F | -0.01% | 0.00% | -0.01% | 100% | 99%
 | Low delay B |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.26% | -0.12% | 98% | 97%
Class C | 0.00% | -0.27% | 0.10% | 99% | 95%
Class E | 0.04% | 0.07% | -0.33% | 99% | 97%
Overall | 0.01% | -0.18% | -0.10% | 99% | 96%
Class D | -0.01% | -0.03% | -0.33% | 100% | 99%
Class F | -0.02% | -0.04% | -0.07% | 99% | 97%

## Slide 8
Conclusion
Recommend to adopt one of the methods
Thanks to Hikvision for cross-checking (JVET-Q0534).
JVET-Q0370