## Slide 1
Interaction between Affine and SBT
JVET-P0431
F. Le Léannec, K. Naser, T. Poirier, P. Bordes

## Slide 2: Motivation
Observation: sub-block transform (SBT) partitioning of a CU is rarely used for Affine Cus
Significant amount of encoder RD checks related to the usage of SBT in combination with affine mode, with a very low usage rate.

## Slide 3: Proposed Method 1
Deactivate SBT for CU in sub block merge mode, and an affine merge candidate is used (as opposed to SbTMVP)
if( cu_cbf ) { | 
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTER && sps_sbt_enabled_flag && !ciip_flag[ x0 ][ y0 ] && !MergeTriangleFlag[ x0 ][ y0 ] && ( merge_subblock_flag[ x0 ][ y0 ] = =0 ¦¦ ( enabledSbTMVP && merge_subblock_idx[ x0 ][ y0 ] = = 0 ) ) && inter_affine_flag[ x0 ][ y0 ]==0 && cbWidth <= MaxTbSizeY && cbHeight <= MaxTbSizeY ) { | 
allowSbtVerH = cbWidth >= 8 | 
allowSbtVerQ = cbWidth >= 16 | 
allowSbtHorH = cbHeight >= 8 | 
allowSbtHorQ = cbHeight >= 16 | 
if( allowSbtVerH ¦ ¦ allowSbtHorH ) | 
cu_sbt_flag | ae(v)
…… | 

## Slide 4: Results of Method 1
Deactivate SBT for CU in sub block merge mode, and an affine merge candidate is used (as opposed to SbTMVP)
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.00% | 100% | 102%
Class A2 | 0.00% | -0.01% | 0.00% | 99% | 102%
Class B | 0.01% | 0.02% | 0.07% | 99% | 100%
Class C | 0.02% | 0.00% | 0.03% | 96% | 94%
Class E |  |  |  |  | 
Overall | 0.01% | 0.01% | 0.03% | 98% | 99%
Class D | -0.01% | -0.09% | -0.11% | 95% | 91%
Class F | -0.02% | 0.00% | -0.05% | 103% | 103%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.29% | -0.40% | 100% | 101%
Class C | 0.00% | -0.30% | 0.03% | 101% | 100%
Class E | -0.06% | 0.22% | -0.32% | 99% | 100%
Overall | 0.00% | -0.17% | -0.24% | 100% | 100%
Class D | -0.03% | 0.37% | 0.15% | 100% | 100%
Class F | -0.05% | -0.11% | -0.07% | 100% | 92%

## Slide 5: Proposed Method 2
Deactivate SBT for CU for all affine CUs, i.e.
  In sub block merge mode, and an affine merge candidate is used
  In affine AMVP mode
if( cu_cbf ) { | 
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTER && sps_sbt_enabled_flag && !ciip_flag[ x0 ][ y0 ] && !MergeTriangleFlag[ x0 ][ y0 ] && ( merge_subblock_flag[ x0 ][ y0 ] = =0 ¦¦ ( enabledSbTMVP && merge_subblock_idx[ x0 ][ y0 ] = = 0 ) ) && inter_affine_flag[ x0 ][ y0 ]==0 && cbWidth <= MaxTbSizeY && cbHeight <= MaxTbSizeY ) { | 
allowSbtVerH = cbWidth >= 8 | 
allowSbtVerQ = cbWidth >= 16 | 
allowSbtHorH = cbHeight >= 8 | 
allowSbtHorQ = cbHeight >= 16 | 
if( allowSbtVerH ¦ ¦ allowSbtHorH ) | 
cu_sbt_flag | ae(v)
…… | 

## Slide 6: Results of Method 2
Deactivate SBT for CU for all affine CUs, i.e.
  In sub block merge mode, and an affine merge candidate is used
  In affine AMVP mode
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.01% | -0.01% | 98% | 101%
Class A2 | 0.05% | 0.05% | 0.06% | 97% | 102%
Class B | 0.05% | 0.00% | 0.11% | 98% | 103%
Class C | 0.05% | -0.03% | -0.03% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.04% | 0.00% | 0.04% | 98% | 101%
Class D | 0.04% | -0.07% | 0.10% | 98% | 104%
Class F | 0.02% | -0.01% | -0.03% | 97% | 107%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.07% | -0.27% | 0.12% | 99% | 99%
Class C | 0.07% | -0.06% | 0.01% | 98% | 99%
Class E | -0.03% | 0.22% | -0.62% | 98% | 100%
Overall | 0.04% | -0.08% | -0.10% | 99% | 100%
Class D | 0.04% | 0.10% | -0.04% | 99% | 100%
Class F | 0.00% | -0.09% | 0.59% | 99% | 101%

## Slide 7: Conclusion
Proposed to normatively SBT in combination with Affine
  For affine merge mode only (Method 1)
    0.01% / 0.0% BD rate change in RA/LDB
    Encoder time 98% in RA
  Reduces the number of RD checks related to SBT on the encoder side
  Negligible impact on VVC coding efficiency
Thanks to Qualcomm for cross-checking