## Slide 1: CABAC zero word threshold
JVET-Q0436
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Karl Sharman / Steve Keating
Sony Corp.

## Slide 2: Introduction
CABAC zero words limit the bit / bin ratio by adding padding bits
  Effectively defines the bin/second rate
  Limit is important aspect in hardware design
From the specification, the formula for the number of bins is given as:
n = ( 32 ÷ 3 ) * NumBytesInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY )  32
For this presentation we are rewriting this as:
n = β * b + c ÷ α
    n is the number of bins allowed in the stream
    b is the number of bits in the stream
    c is the number of bits in the image or image region
    α and β are two constants with default values of 32 and 4 ÷ 3 respectively
dynamic
component
static
component

## Slide 3: Analysis
HD and 4K pictures from CTC split into tiles of 10, 60, and 120 complete (128x128) CTU
First analysis showed that class TGM had no tiles which exceeded cabac_zero_word threshold
  Excluded from further analysis
Number of complete CTUs in tile | HD format | 4K format
10 | 3 tile columns, 4 tile rows; each tile is 5x2 CTUs | 6 tile columns, 8 tile rows; each tile is 5x2 CTUs
60 | 1 tile column, 2 tile rows; each tile is 15x4 CTUs | 2 tile columns, 4 tile rows; each tile is 15x4 CTUs
120 | Single tile of 15x8 CTUs; | 2 tile columns, 2 tile rows; each tile is 15x8 CTUs

## Slide 4: Analysis
Level | Max luma sample rate MaxLumaSr (samples/sec) | Max bit rate MaxBR (BrVclFactor or BrNalFactor bits/s) |  | Min compression ratio MinCrBase | 
 |  | Main tier | High tier | Main tier | High tier
.. | .. | .. | .. | .. | ..
4.1 | 133 693 440 | 20 000 | 50 000 | 4 | 4
5 | 267 386 880 | 25 000 | 100 000 | 6 | 4
5.1 | 534 773 760 | 40 000 | 160 000 | 8 | 4
.. | .. | .. | .. | .. | ..
Tier and level limits for the video profiles
(Extract from Table A.2 of VVC specification)
HD (class B) sequences level 4.1
4K (class A) sequences levels 5 / 5.1
Previous study (JVET-P0395) indicated high tier most likely to exceed cabac_zero_word threshold

## Slide 5: Analysis – High Tier – 10 CTU Tiles
Points above red line indicate tiles exceeding existing cabac_zero_word threshold
Colour of point indicates QP – most points above red line have QP 18-22
Results for RA and AI – mix of I and B frames

## Slide 6: Analysis
Some sequences (for example DaylightRoad2) exceed cabac_zero_word threshold more commonly than others
  Previous study identified this might be caused by quantization of noise
  Occurs at sequence specific QP ranges
  No evidence of significant “averaging out” as tile size increases
  Percentage tiles are over cabac_zero_word threshold represents cost to coding efficiency of adding cabac_zero_word
 |  | I / B Slice QP |  |  |  | 
 |  | 18 | 19 | 20 | 21 | 22
Tile size in CTU | 10 | 22.9% | 50.0% | 62.5% | 75.0% | 43.75%
 | 60 | 25.0% | 25.0% | 50.0% | 75.0% | 43.75%
 | 120 | 0.0% | 50.0% | 50.0% | 62.5% | 50.00%
 |  | I / B Slice QP |  |  |  | 
 |  | 18 | 19 | 20 | 21 | 22
Tile size in CTU | 10 | 0.93% | 1.70% | 3.14% | 3.81% | 1.85%
 | 60 | 1.74% | 3.61% | 3.52% | 3.73% | 2.23%
 | 120 | 0.00% | 1.38% | 3.26% | 4.30% | 1.53%
Percentage of tiles over cabac_zero_world threshold in “High” tier for DaylightRoad2
Average percent tiles are over cabac_zero_word threshold in “High” tier for DaylightRoad2

## Slide 7: Observation
Addition of cabac_zero_word effectively introduces a loss to coding efficiency
  Can either accept this, or,
  Update formula for cabac_zero_word threshold (unchanged since AVC)
    Increase dynamic component (increase β)
    Increase static component (reduce α)
    Increase both

## Slide 8: Observation – Candidate 1
Increase β to 3 ÷ 2
All tiles below new threshold

## Slide 9: Observation – Candidate 2
Reduce α to 24
All tiles below new threshold

## Slide 10: Comparison of Approaches
Candidate 1 imposes much lower increase on maximum bin rate, hence is selected.
Level | Max bitrate | Max bin rate |  |  |  | 
 |  | Existing α = 32 β = 4 ÷ 3 | Candidate 1 α = 32 β = 3 ÷ 2 |  | Candidate 2 α = 24 β = 4 ÷ 3 | 
 | Kbit/s | Kbin/s | Kbin/s | % increase | Kbin/s | % increase
4 | 12000 | 47334 | 49334 | 4.23 | 57779 | 22.07
4.1 | 20000 | 89335 | 92669 | 3.73 | 110225 | 23.38
5 | 25000 | 158671 | 162838 | 2.63 | 200450 | 26.33
5.1 | 40000 | 304009 | 310675 | 2.19 | 387567 | 27.49
5.2 | 60000 | 581350 | 591350 | 1.72 | 748467 | 28.75
6 | 60000 | 581350 | 591350 | 1.72 | 748467 | 28.75
6.1 | 120000 | 1162701 | 1182701 | 1.72 | 1496934 | 28.75
6.2 | 240000 | 2325402 | 2365402 | 1.72 | 2993869 | 28.75

## Slide 11: Comparison of Approaches
Level | Max bitrate | Max bin rate |  |  |  | 
 |  | Existing α = 32 β = 4 ÷ 3 | Candidate 1 α = 32 β = 3 ÷ 2 |  | Candidate 2 α = 24 β = 4 ÷ 3 | 
 | Kbit/s | Kbin/s | Kbin/s | % increase | Kbin/s | % increase
4 | 30000 | 71334 | 76334 | 7.01 | 81779 | 14.64
4.1 | 50000 | 129335 | 137669 | 6.44 | 150225 | 16.15
5 | 100000 | 258671 | 275338 | 6.44 | 300450 | 16.15
5.1 | 160000 | 464009 | 490675 | 5.75 | 547567 | 18.01
5.2 | 240000 | 821350 | 861350 | 4.87 | 988467 | 20.35
6 | 240000 | 821350 | 861350 | 4.87 | 988467 | 20.35
6.1 | 480000 | 1642701 | 1722701 | 4.87 | 1976934 | 20.35
6.2 | 800000 | 3072068 | 3205402 | 4.34 | 3740535 | 21.76
Candidate 1 imposes much lower increase on maximum bin rate, hence is selected.

## Slide 12: Conclusion
Propose changing the bit length multiplier, β, to in the CABAC zero word threshold to 3 ÷ 2 for (at least) high tier.
  Prevents currently imposed bit rate losses due to addition of cabac_zero_word
    4.3% for slices with QP21 (DaylightRoad2)
Draft text included in submission

## Slide 13: Additional analysis (1)
An analysis of the effect of the proposal on full pictures rather than 10, 20 or 60 CTU tiles has been done.
The sequence DaylightRoad2 was simulated using for RA at all QP between 10 and 30.
Other than the non-standard sequence QP, CTC was used.
The results are given on the next slide and show (for DaylightRoad2):
  no cabac_zero_word are added for main tier using the current threshold
  up to 1.24% of the sequence length is added in cabac_zero_word for high tier.
  Also note that above high tier up to 83.5% of the frames in the sequence require the addition of cabac_zero_word using the current threshold.
  However, with the proposed cabac_zero_word formula, none of the frames exceed the threshold.

## Slide 14: Additional analysis (2)
Sequence QP | Number of frames analysed | Bitrate Kbit/s | Tier rating | Number of frames over current threshold | Percentage of frames over current threshold | Number of frames over proposed threshold | Average % bit cost increase for all slices due to CZW | Average % bit cost increase for slices that have CZW | Maximum % bit cost increase for any slice due to CZW | Percentage of bits added to sequence due to CZW
10 | 212 | 1159036 | > High | 0 | 0 | 0 | 0 | 0 | 0 | 0
11 | 213 | 1039312 | > High | 0 | 0 | 0 | 0 | 0 | 0 | 0
12 | 218 | 923611 | > High | 1 | 0.5 | 0 | 0 | 0.08 | 0.08 | 0
13 | 225 | 814402 | > High | 107 | 47.6 | 0 | 0.77 | 1.61 | 2.73 | 0.62
14 | 228 | 714236 | > High | 163 | 71.5 | 0 | 2.45 | 3.42 | 6.20 | 2.02
15 | 237 | 614525 | > High | 198 | 83.5 | 0 | 3.88 | 4.64 | 7.61 | 3.22
16 | 241 | 522365 | > High | 174 | 72.2 | 0 | 2.17 | 3.01 | 6.85 | 2.03
17 | 250 | 417856 | > High | 60 | 24.0 | 0 | 0.71 | 2.97 | 5.79 | 0.81
18 | 297 | 289197 | > High | 21 | 7.1 | 0 | 0.06 | 0.82 | 1.55 | 0.09
19 | 300 | 186439 | > High | 33 | 11.0 | 0 | 0.21 | 1.88 | 3.70 | 0.68
20 | 300 | 115526 | High | 33 | 11.0 | 0 | 0.27 | 2.50 | 4.66 | 1.24
21 | 300 | 81262 | High | 3 | 1.0 | 0 | 0 | 0.30 | 0.45 | 0.02
22 | 300 | 59095 | High | 0 | 0 | 0 | 0 | 0 | 0 | 0
23 | 300 | 41901 | High | 2 | 0.7 | 0 | 0 | 0.45 | 0.82 | 0.05
24 | 300 | 26796 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
25 | 300 | 19351 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
26 | 300 | 14242 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
27 | 300 | 10333 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
28 | 300 | 7861 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
29 | 300 | 6635 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0
30 | 300 | 5582 | Main | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 15: Additional analysis (3)
Further analysis has identified the slice type and slice QP which cause the cabac_zero_word threshold to be exceeded.
The results are shown in the following table.
  No slice with QP below 17 or above 23 were found to exceed the threshold for DaylightRoad2 and have therefore been excluded.
  The slices that exceed cabac_zero_word are mostly B frames within a small QP range.
  For certain QP, 100% of B frames exceed the cabac_zero_word threshold.
  The exact implications of this on individual sequences depends on the chosen GOP structure.
    For high tier operation, some GOP structures may be able to exacerbate the problem by bringing problematic QPs into the GOP structure.

## Slide 16: Additional analysis (4)
Slice Type | Slice QP | Number of frames analysed | Number of frames over current threshold | Percentage of frames over current threshold | Number of frames over proposed threshold | Average % bit cost increase for all slices due to CZW | Average % bit cost increase for slices that have CZW | Maximum % bit cost increase for any slice due to CZW
B | 17 | 213 | 0 | 0 | 0 | 0 | 0 | 0
B | 18 | 220 | 1 | 0.45 | 0 | 0 | 0.08 | 0.08
B | 19 | 225 | 193 | 85.78 | 0 | 1.1 | 1.28 | 2.73
B | 20 | 229 | 229 | 100 | 0 | 3.87 | 3.87 | 6.2
B | 21 | 238 | 238 | 100 | 0 | 4.96 | 4.96 | 7.61
B | 22 | 247 | 130 | 52.63 | 0 | 0.8 | 1.52 | 3.42
B | 23 | 262 | 0 | 0 | 0 | 0 | 0 | 0
I | 17 | 5 | 0 | 0 | 0 | 0 | 0 | 0
I | 18 | 5 | 0 | 0 | 0 | 0 | 0 | 0
I | 19 | 5 | 0 | 0 | 0 | 0 | 0 | 0
I | 20 | 5 | 2 | 40 | 0 | 0.18 | 0.45 | 0.82
I | 21 | 5 | 0 | 0 | 0 | 0 | 0 | 0
I | 22 | 5 | 0 | 0 | 0 | 0 | 0 | 0
I | 23 | 5 | 0 | 0 | 0 | 0 | 0 | 0