## Slide 1
JVET-Q0507
CE4-related: Quality scalable GEO
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
This contribution proposes a quality scalable GEO design, in which the actual number of used GEO mode is signalled into the bitstream. Purpose of this proposal is to address a concern raised by the AHG16 on the JVET email reflector, which claimed that the proposed GEO design under consideration is not quality scalable on the encoder side, a less capable encoder supporting a subset of GEO modes may incur loss instead of gain.

## Slide 3
Proposal
Scalable geo by signaling number of valid modes in SPS
Encoder is allowed to choose either 16 valid geo modes or 64 valid geo modes.
A flag is signaled in SPS level to switch between 16 and 64 modes.
If 16 mode is selected, only the first 16 modes of GEO mode table are valid.
If 64 mode is selected, all 64 modes of GEO mode table are valid.
(This affects coding of merge_geo_parititon_idx with cmax set to 16 and 64 respectively)
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
GEO (JVET-Q0059, CE4-1) | 1,216 | 64 | 19
Proposal (64 mode) | Same as above | Same as above | Same as above
Proposal (16 mode) | 304 | 16 | 19

## Slide 4
Simulation results
Anchor: VTM7.0
Test: Left - scalable coding with 16 valid modes; Right – scalable coding with 64 valid modes. (implemented over CE4-1, GEO mode table is reordered according to statistics)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.09% | 0.00% | 102% | 101%
Class A2 | -0.06% | 0.04% | 0.05% | 101% | 100%
Class B | -0.06% | 0.03% | -0.04% | 101% | 101%
Class C | -0.21% | -0.34% | -0.28% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.09% | -0.09% | -0.08% | 101% | 100%
Class D | -0.16% | -0.32% | -0.25% | 101% | 100%
Class F | -0.22% | -0.21% | -0.19% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.16% | -0.28% | -0.17% | 101% | 100%
Class C | -0.25% | -0.42% | -0.09% | 101% | 99%
Class E | -0.52% | 0.22% | -0.38% | 99% | 99%
Overall | -0.28% | -0.20% | -0.20% | 100% | 99%
Class D | -0.33% | 0.12% | -0.53% | 100% | 100%
Class F | -0.34% | -0.49% | 0.01% | 100% | 100%
Random Access Main 10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.13% | -0.20% | -0.18% | 103% | 101%
-0.19% | -0.14% | -0.02% | 103% | 100%
-0.14% | -0.11% | -0.09% | 102% | 100%
-0.61% | -0.97% | -0.86% | 102% | 100%
-0.28% | -0.36% | -0.30% | 102% | 100%
-0.41% | -0.64% | -0.52% | 102% | 100%
-0.33% | -0.34% | -0.35% | 101% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.32% | -0.44% | -0.26% | 103% | 100%
-0.81% | -1.15% | -0.96% | 103% | 99%
-1.18% | -0.21% | -0.77% | 101% | 99%
-0.70% | -0.62% | -0.62% | 102% | 99%
-0.68% | -0.56% | -0.76% | 102% | 99%
-0.53% | -0.75% | 0.05% | 102% | 99%

## Slide 5
Simulation results (additional information)
8 valid modes 32 valid modes 48 valid modes
 | Random Access Main 10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 | 0.09% | 0.18% | 0.21%
Class A2 | 0.03% | 0.17% | 0.23%
Class B | 0.06% | 0.21% | 0.13%
Class C | 0.06% | 0.15% | 0.13%
Class E |  |  | 
Overall | 0.06% | 0.18% | 0.16%
Class D | -0.03% | -0.01% | 0.00%
Class F | -0.11% | -0.03% | -0.08%
 | Low delay B Main10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | 0.09% | -0.09% | 0.26%
Class C | 0.18% | 0.09% | 0.40%
Class E | -0.14% | 0.57% | 0.08%
Overall | 0.06% | 0.14% | 0.26%
Class D | 0.00% | 0.32% | 0.48%
Class F | -0.03% | -0.47% | 0.43%
Random Access Main 10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.10% | -0.19% | -0.07%
-0.13% | -0.12% | 0.02%
-0.12% | -0.08% | -0.11%
-0.41% | -0.60% | -0.53%
-0.19% | -0.25% | -0.19%
-0.31% | -0.46% | -0.52%
-0.29% | -0.32% | -0.27%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.29% | -0.34% | -0.17%
-0.59% | -0.80% | -0.48%
-0.84% | -0.24% | -0.49%
-0.53% | -0.47% | -0.35%
-0.54% | -0.46% | -0.64%
-0.41% | -1.17% | -0.22%
Random Access Main 10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.11% | -0.15% | -0.18%
-0.17% | -0.07% | 0.02%
-0.15% | -0.11% | -0.10%
-0.55% | -0.79% | -0.74%
-0.25% | -0.29% | -0.27%
-0.41% | -0.53% | -0.60%
-0.33% | -0.36% | -0.29%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.37% | -0.54% | -0.43%
-0.76% | -1.14% | -0.81%
-0.93% | -0.30% | -1.11%
-0.64% | -0.68% | -0.73%
-0.64% | -0.42% | -0.44%
-0.51% | -1.04% | -0.09%

## Slide 6
Summary
When compared test 6) with test 7), the proposed signaling provides an average gain of roughly -0.15% in RA and -0.37% in LDB when the first 16 modes are enabled.
When compared test 1) with test 6), the re-ordered GEO table provides an average gain of roughly -0.13% in RA and -0.35% in LDB when the first 16 modes are enabled.
When compared test 1) and test 7), the re-ordered GEO table and the proposed signalling together provides an average gain of roughly -0.28% in RA and -0.72% in LDB when the first 16 modes are enabled.
Test # | Setting | RA (Y, U, V) | LDB (Y, U, V)
Test 1) | scalable number of modes (16 modes) | -0.09%, -0.09%, -0.08% | -0.28%, -0.20%, -0.20%
Test 2) | scalable number of modes (64 modes) | -0.28%, -0.36%, -0.30% | -0.70%, -0.62%, -0.62%
Test 3) | scalable number of modes (8 modes) | 0.06%, 0.18%, 0.16% | 0.06%, 0.14%, 0.26%
Test 4) | scalable number of modes (32 modes) | -0.19%, -0.25%, -0.19% | -0.53%, -0.47%, -0.35%
Test 5) | scalable number of modes (48 modes) | -0.25%, -0.29%, -0.27% | -0.64%, -0.68%, -0.73%
Test 6) | scalable number of modes (16 modes, but GEO mode table not re-ordered) | 0.04%, 0.06%, 0.14% | 0.07%, 0.31% ,0.47%
Test 7) | non-scalable number of modes (16 modes, GEO mode table not re-ordered) | 0.19% ,0.30%, 0.30% | 0.44%, 0.62% , 0.69%

## Slide 7
7
Conclusion
This contribution proposes scalable number of modes of GEO to address the concern of quality scalability of GEO. A SPS switch is used to switch between 16 and 64 modes.
16 modes (anchor VTM7.0): -0.09% (RA) and -0.28% (LDB)
  64 modes (anchor VTM7.0): -0.28% (RA) and -0.70% (LDB)

## Slide 8
8
Thank Bytedance for cross-check